## Slide 1: Chapter 1
Computer Abstractions
and Technology
只需要掌握8个伟大思想和CPU评价那些

## Slide 2
Design for Moore’s Law （设计紧跟摩尔定律）
Use Abstraction to Simplify Design (采用抽象分层简化设计)
Make the Common Case Fast (加速大概率事件) 优先优化常用功能
Performance via Parallelism (通过并行提高性能:多个流水线并行，行波加法器)
Performance via Pipelining (通过流水线提高性能)
Performance via Prediction (通过预测提高性能)
Hierarchy of Memories (存储器层次结构)
Dependability via Redundancy (通过冗余提高可靠性)
Express elevators in buildings
Library reserve desk
Increasing the gate area on a CMOS tran，sistor to decrease its switching time
类似福特的工业流水线

## Slide 3: Idea3: Make the Common Case Fast
Amdahl's Law

## Slide 4: Defining Performance
Response (Execution) time 执行时间
  user perception
  system performance
  the only unimpeachable measure of performance 唯一无懈可击的业绩衡量标准
  Mobile devices
CPU time
  designer perception
  CPU performance
Throughput
  administrator perception
  server
改进性能的方法 | Response time | Throughput
Replacing a faster processor | ↑ | ↑
Adding additional processors for a system use MP for independent task | - | ↑

## Slide 5
Response (Execution) time
  计算机完成一项任务所需的总时间，包括磁盘访问、内存访问、I/O活动、操作系统开销、CPU执行时间
CPU time
  CPU用于特定任务的实际计算时间
Throughput(Bandwidth带宽)
  在给定时间内所做的总功
  单位时间内完成的任务数
CPU time is further divided into:
  User time - time spent in user mode
  System time - time spent in OS

## Slide 6: Relative Performance
“Performance of P1 is better than P2 ” is, for a given work load L, P1 takes less time to execute L than P2 does
performance(P1) > Performance(P2)
 Execution Time(P1, L) < Execution Time(P2, L)
“Processor X is n times fast than Y” is

## Slide 7: CPU Clocking
时钟周期 Clock Circle Time
主频的倒数
主频（时钟频率）Clock Rate
  主频越高完成一个指令所需要的时间越短
  CPI cycle per instruction
  执行一条指令所需的时钟周期数（时钟频率不影响CPI）
  CPU执行时间
Instructions指令条数

## Slide 8: CPI是执行所有指令的平均时间周期数

## Slide 9: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 10: Example：Which is fast and by how much ?
 | clock period | CPI | CPU clock cycles | CPU time
A | 250 ps | 2.0 | I 2.0 | 500 I ps
B | 500 ps | 1.2 | I 1.2 | 600 I ps
 | clock period | CPI | CPU clock cycles | CPU time
A | 250 ps | 2.0 |  | 
B | 500 ps | 1.2 |  | 
Answer: CPU PerformanceA Execution TimeB 600 * I ps
--------------------------- = -------------------------- = ------------------- = 1.2
CPU PerformanceB Execution TimeA 500 * I ps