## Slide 1: Ch5-2 Cache coherence
Snooping protocol
Directory protocol

## Slide 2: Centralized Shared-Memory Architecture
Characteristics of SMP
  Limited processors nodes----small scale, share single physical memory connected by a shared bus.
  Large cache ----provide a sufficient amount of memory bandwidth.
    Increase bandwidth versus bus/memory
    Reduce latency of access
    Valuable for both private data and shared data
  UMA----uniform memory access time.

## Slide 3: Major issues for Shared Memory
Cache coherence ( Value, same location)
  “Common Sense”
    P1 Read[X] => P1 Write[X] => P1 Read[X] will return X
    P2 Read[X] => P1 Write[X] => will return value written by P1
    P1 Write[X] => P2 Write[X] => Serialized (all processor see the writes in the same order)
Synchronization
  Atomic read/write operations
Memory consistency Model ( order, different locations)
  In what order must a processor observe the data writes of another processor ?
  What properties must be enforced among reads and writes to different locations by different processors?
These are not issues for message passing systems
  Why?

## Slide 4: What is Multiprocessor Cache Coherence?

## Slide 5: Cache coherence in uniprocessor

## Slide 6: Cache Coherence in Multiprocessor

## Slide 7: Cache incoherence due to write

## Slide 8: Cache incoherence due to write

## Slide 9: What Does Coherency Mean?
Informally:
  “Any read must return the most recent write”
  Too strict and too difficult to implement
Better:
  “Any write must eventually be seen by a read”
  All writes are seen in proper order (“serialization”)
Two rules to ensure this:
  “If P writes x and P1 reads it, P’s write will be seen by P1 if the read and write are sufficiently far apart”
  Writes to a single location are serialized: seen in one order
    Latest write will be seen
    Otherewise could see writes in illogical order (could see older value after a newer value)

## Slide 10: Definition of Cache coherence
Cache coherence
  P1 Read[X] => P1 Write[X] => P1 Read[X] will return X
  P2 Read[X] => P1 Write[X] => will return value written by P1
  P1 Write[X] => P2 Write[X] => Serialized (all processor see the writes in the same order)

## Slide 11: HW Coherence Protocols
Snooping Solution (Snoopy Bus):
  Send all requests for data to all processors
  Processors snoop to see if they have a copy and respond accordingly
  Requires broadcast, since caching information is at processors
  Works well with bus (natural broadcast medium)
  Dominates for small scale machines (most of the market)
Directory-Based Schemes (discuss later)
  Keep track of what is being shared in 1 centralized place (logically)
  Distributed memory => distributed directory for scalability (avoids bottlenecks)
  Send point-to-point requests to processors via network
  Scales better than Snooping
  Actually existed BEFORE Snooping-based schemes

## Slide 12: Snooping solution
Every cache that has a copy of the data from a block of physical memory also has a copy of the sharing status of the block, but no centralized state is kept.

## Slide 13: Basic Snoopy Protocols
Write Invalidate Protocol:
  Multiple readers, single writer
  Write to shared data: an invalidate is sent to all caches which snoop and invalidate any copies
  Read Miss:
    Write-through: memory is always up-to-date
    Write-back: snoop in caches to find most recent copy
Write Broadcast Protocol (typically write through):
  Write to shared data: broadcast on bus, processors snoop, and update any copies
  Read miss: memory is always up-to-date
Write serialization: bus serializes requests!
  Bus is single point of arbitration

## Slide 14: EX: write back Cache, write invalidate
Mechanics
  Broadcast address of cache line to invalidate
  All processor snoop, then invalidate if in local cache
  policy can be used to service cache misses in write-back caches

## Slide 15: Ex: Write back Cache, update(Broadcast)

## Slide 16: Bus-based protocols (Snooping)
Snooping
  All caches see and react to all bus events
  Protocol relies on global visibility of events (ordered broadcast)
  The serialization of access by the bus forces serialization of writes.
Events:
  Processor (events from own processor)
    Read (R), Write (W), Writeback (WB)
  Bus Events (events from other processors)
    Bus Read (BR), Bus Write (BW)

## Slide 17: Implementation of snooping protocols

## Slide 18: 5 snooping protocols

## Slide 19: Simple write-invalidate protocol
Three states
  Invalid, Shared, exclusive
Events
  CPU-R, CPU-W
  BUS-R, BUS-W

## Slide 20: Snoopy Coherence Protocols

## Slide 21: Snoopy-Cache State Machine-I
State machine for CPU requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place read miss
on bus
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Cache Block
State
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 22: Snoopy-Cache State Machine-II
State machine for bus requests for each cache block
Invalid
Shared
(read/only)
Exclusive
(read/write)
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write miss for this block
Write Back
Block; (abort
memory access)

## Slide 23: Snoopy-Cache State Machine-III
State machine for CPU requests for each cache block and for bus requests for each cache block
Cache Block
State
Place read miss
on bus
Invalid
Shared
(read/only)
Exclusive
(read/write)
CPU Read
CPU Write
CPU Read hit
Place Write Miss on bus
CPU read miss
Write back block,
Place read miss
on bus
CPU Write
Place Write Miss on Bus
CPU Read miss
Place read miss
on bus
CPU Write Miss
Write back cache block
Place write miss on bus
CPU read hit
CPU write hit
Write miss for this block
Write Back
Block; (abort
memory access)
Write miss for this block
Read miss for this block
Write Back
Block; (abort
memory access)
Notes: Invalid:
read => shared
write => dirty
shared looks the same

## Slide 24: Example
Assumes A1 and A2 map to same cache block,
initial cache state is invalid

## Slide 25: Example: step 1
Remote
Write
Write Back
Remote Write
Invalid
Shared
Exclusive
CPU Read hit
Read miss on bus
Write miss on bus
CPU Write
Place Write Miss on Bus
CPU read hit
CPU write hit
Remote Read Write Back
Assumes initial cache state
is invalid and A1 and A2 map to same cache block,
but A1 != A2.
Notes: Assumes initial cache state
is invalid and A1 and A2 map to same cache block,
but A1 != A2.

## Slide 26: Example: step 2
Remote
Write
Write Back
Remote Write
Invalid
Shared
Exclusive
CPU Read hit
Read miss on bus
Write miss on bus
CPU Write
Place Write Miss on Bus
CPU read hit
CPU write hit
Remote Read Write Back
CPU Write Miss
Write Back

## Slide 27: Example:step 3
Remote
Write
Write Back
Remote Write
Invalid
Shared
Exclusive
CPU Read hit
Read miss on bus
Write miss on bus
CPU Write
Place Write Miss on Bus
CPU read hit
CPU write hit
Remote Read Write Back
CPU Write Miss
Write Back

## Slide 28: Example: step4
Remote
Write
Write Back
Remote Write
Invalid
Shared
Exclusive
CPU Read hit
Read miss on bus
Write miss on bus
CPU Write
Place Write Miss on Bus
CPU read hit
CPU write hit
Remote Read Write Back

## Slide 29: Example:step 5
Remote
Write
Write Back
Remote Write
Invalid
Shared
Exclusive
CPU Read hit
Read miss on bus
Write miss on bus
CPU Write
Place Write Miss on Bus
CPU read hit
CPU write hit
Remote Read Write Back
CPU Write Miss
Write Back
Notes: Why write miss first?
Because in general, only write a piece of block, may need to read it first so that can have a full vblock; therefore, need to get
Write back is low priority event.

## Slide 30
x 所在的block (w x y z)
i 所在的block ( h i j k )
写x, miss
取入整个 w x y* z

## Slide 31: Snooping Cache Variations
Berkeley Protocol
Owned Exclusive
Owned Shared
Shared
Invalid
Basic Protocol
Exclusive
Shared
Invalid
Illinois Protocol
Private Dirty
Private Clean
Shared
Invalid
Owner can update via bus invalidate operation
Owner must write back when replaced in cache
If read sourced from memory, then Private Clean
if read sourced from other cache, then Shared
Can write in cache if held private clean or dirty
MESI Protocol
Modfied (private,!=Memory)
eXclusive (private,=Memory)
Shared (shared,=Memory)
Invalid

## Slide 32: MESI (Illinois protocol) (write back cache)
CPU Read hit / CPU read miss
place read miss
on bus
Shared
(read/only)
CPU Write
No need to Place Write Miss on Bus
Remote Read
Place Data on Bus
Remote Write
Write back block
Remote Write
Invalid
Modified
(read/write)
CPU Read
Place read miss on Bus
CPU read hit
CPU write hit
Exclusive (read/only)
CPU Read hit
Remote Read
Write back
block
Read-for-ownership
Place read miss on bus
Read-for-ownership
Place read miss on bus
CPU read miss
Write back block
Place read miss on bus
CPU Write miss
Write back Place Write Miss on Bus

## Slide 33: Snoopy Coherence Protocols
Complications for the basic MSI protocol:
  Operations are not atomic
    E.g. detect miss, acquire bus, receive a response
    Creates possibility of deadlock and races
    One solution: processor that sends invalidate can hold bus until other processors receive the invalidate
Extensions:
  Add exclusive state to indicate clean block in only one cache (MESI protocol)
    Prevents needing to write invalidate on a write
  Owned state

## Slide 34: Coherence Protocols: Extensions
Shared memory bus and snooping bandwidth is bottleneck for scaling symmetric multiprocessors
  Duplicating tags
  Place directory in outermost cache
  Use crossbars or point-to-point networks with banked memory

## Slide 35: Coherence Protocols
Every multicore with >8 processors uses an interconnect other than bus
  Makes it difficult to serialize events
  Write and upgrade misses are not atomic
  How can the processor know when all invalidates are complete?
  How can we resolve races when two processors write at the same time?
  Solution: associate each block with a single bus

## Slide 36: Performance
Coherence influences cache miss rate
  Coherence misses
    True sharing misses
      Write to shared block (transmission of invalidation)
      Read an invalidated block
    False sharing misses
      Read an unmodified word in an invalidated block

## Slide 37: Performance Study: Commercial Workload

## Slide 38: Performance Study: Commercial Workload

## Slide 39: Performance Study: Commercial Workload

## Slide 40: Performance Study: Commercial Workload

## Slide 41: Directory-based Cache coherence

## Slide 42: Distributed Shared Memory
Nov. 12 2008
Each node has a local memory and cache
Local or remote memory access via memory controller

## Slide 43: Directory protocol
Directory: track state of every block in memory, and change the state of block in cache according to directory.
Information in directory
  Status of Every block: shared/uncached/exclusive
  Which processors have copies of the block: bit vector
  Whether the block is dirty or clean
Directory protocol can be implemented with a distributed memory
Directory protocol can be applied to a centralized memory organized into banks

## Slide 44: Distributed Directory MPs
Nov. 12 2008
Notes: 44

## Slide 45: Directory protocol implementation
Nov. 12 2008
Block status
  Shared: ≥ 1 processors have data, memory up-to-date
  Uncached (no processor hasit; not valid in any cache)
  Exclusive: 1 processor (owner) has data; memory out-of-date
Directory size = f (entry number * entry size)
  Each memory block has an entry in directory / only keep the entries for cached blocks
  Every processor has one bit / Limited processor bits in bit vector
Directory can be distributed along with the memory to avoid becoming the bottleneck
Assumptions to Keep it simple:
  Writes to non-exclusive data => write miss
  Processor blocks until access completes
  Assume messages received and acted upon in order as sent

## Slide 46: Directory Protocol
Nov. 12 2008
No bus and don’t want to broadcast:
  Interconnect means no longer single arbitration point
  all messages have explicit responses
Terms: typically 3 processors involved
  Local node where a request originates
  Home node where the memory location of an address resides
  Remote node has a copy of a cache block, whether exclusive or shared
Example messages on next slide: P = processor number, A = address
Notes: 46

## Slide 47
Message type Source Destination Msg Content
Read miss Local cache Home directory P, A
  Processor P reads data at address A; make P a read sharer and arrange to send data back
Write miss Local cache Home directory P, A
  Processor P has a write miss at address A; make P the exclusive owner and arrange to send data back
Invalidate Local cache Home directory A
  Request to send invalidates to all remote caches that are caching the block at address A
Invalidate Home directory Remote caches A
  Invalidate a shared copy at address A.
Fetch Home directory Remote cache A
  Fetch the block at address A and send it to its home directory
Fetch/Invalidate Home directory Remote cache A
  Fetch the block at address A and send it to its home directory; invalidate the block in the cache
Data value reply Home directory Local cache Data
  Return a data value from the home memory (read miss response)
Data write-back Remote cache Home directory A, Data
  Write-back a data value for address A (invalidate response)
Notes: 47

## Slide 48: State Transition Diagram for an Individual Cache Block in a Directory Based System
States identical to snoopy case; transactions very similar.
Transitions caused by read misses, write misses, invalidates, data fetch requests
Generates read miss & write miss msg to home directory.
Write misses that were broadcast on the bus for snooping => explicit invalidate & data fetch requests.
Note: on a write, a cache block is bigger, so need to read the full cache block
Notes: 48

## Slide 49: CPU -Cache State Machine
State machine for CPU requests for each memory block
Invalid state if in memory
Invalid
Shared
(read/only)
Exclusive
(read/writ)
CPU Read
Send Read Miss
CPU Write: Send Write Miss
to h.d.
Directory:
Uncached: Send Rp; S shared;
share = {p}
Shared: Send Rp;
share + = {p}
Exclusive: Send Fetch to R.N.
get reply back from R.N.
Send RP;
 Shared
share + = {p}
Directory:
Uncached: Send Rp; S Exclusive
share = {p}
Shared: Send invalidate;
Send Rp;
S Exclusive
share = {p}
Exclusive: Send Fetch/invalidate to R.N.
get reply back from R.N.
Send RP to P; SExclusive
share = {p}
Notes: 49
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 50: CPU -Cache State Machine
State machine for CPU requests for each memory block
Invalid state if in memory
Invalidate
Invalid
Shared
(read/only)
Exclusive
(read/writ)
CPU Read
Send Read Miss
CPU Write: Send Write Miss
to h.d.
CPU Read hit
CPU Write hit:Send invalidate to home directory
CPU read miss:
Send Read Miss
CPU Write miss:Send Write Miss to home directory
Notes: 50
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 51: CPU -Cache State Machine
Nov. 12 2008
State machine for CPU requests for each memory block
Invalid state if in memory
Invalidate
Invalid
Shared
(read/only)
Exclusive
(read/writ)
CPU Read
CPU Read hit
Send Read Miss
CPU Write: Send Write Miss
to h.d.
CPU Write hit:Send invalidate to home directory
CPU read hit
CPU write hit
Fetch/Invalidate
Data Write Back
Fetch: Data Write Back to home directory
CPU read miss:
Send Read Miss
CPU write miss:
Data Write Back
and send Write Miss to home
directory
CPU read miss:
Data Write Back and
Send read miss to home directory
CPU Write miss:Send Write Miss to home directory
Notes: 51
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 52: CPU -Cache State Machine
Nov. 12 2008
State machine for CPU requests for each memory block
Invalid state if in memory
Fetch/Invalidate
Data Write Back
Invalidate
Invalid
Shared
(read/only)
Exclusive
(read/writ)
CPU Read
CPU Read hit
Send Read Miss
CPU Write: Send Write Miss
to h.d.
CPU Write hit:Send invalidate to home directory
CPU read hit
CPU write hit
Fetch: Data Write Back to home directory
CPU read miss:
Send Read Miss
CPU write miss:
Data Write Back
and send Write Miss to home
directory
CPU read miss:
Data Write Back and
Send read miss to home directory
CPU Write miss:Send Write Miss to home directory
Are these write back
the same ?
Notes: 52
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 53: State Transition Diagram for the Directory
Same states & structure as the transition diagram for an individual cache
2 actions: update of directory state & send msgs to statisfy requests
Tracks all copies of memory block.
Also indicates an action that updates the sharing set, Sharers, as well as sending a message.
Notes: 53

## Slide 54: Directory State Machine
State machine for Directory requests for each memory block
Uncached state if in memory
Uncached
Shared
(read only)
Exclusive
(read/writ)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss:
Data Value Reply
Sharers = {P};
Notes: 54
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 55: Directory State Machine
State machine for Directory requests for each memory block
Uncached state if in memory
Uncached
Shared
(read only)
Exclusive
(read/writ)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss:
Data Value Reply
Sharers = {P};
Write Miss/ Invalidate:
Send Invalidate to R.N;
Sharers = {P};
(Data Value Reply)
Read miss:
Data Value Reply
Sharers += {P};
Notes: 55
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 56: Directory State Machine
Nov. 12 2008
State machine for Directory requests for each memory block
Uncached state if in memory
Uncached
Shared
(read only)
Exclusive
(read/writ)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss/Invalid:
Invalidate ;
Sharers = {P};
Data Value Reply
Write Miss:
Data Value Reply
Sharers = {P};
Data Write Back:
Sharers = {}
Read miss:
Send Fetch to R.N.;
Get Data from R. N.
Reply Back to local processor
Sharers += {P};
Read miss:
Data Value Reply
Sharers += {P};
Write Miss:
Fetch/Invalidate;
Receive Date from R.N
Data Value Reply
to local Node
Sharers = {P};
Notes: 56
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 57: Directory State Machine
Nov. 12 2008
State machine for Directory requests for each memory block
Uncached state if in memory
Data Write Back:
Sharers = {}
Uncached
Shared
(read only)
Exclusive
(read/writ)
Read miss:
Sharers = {P}
send Data Value
Reply
Write Miss:
Invalidate ;
Sharers = {P};
Data Value Reply
Write Miss:
Data Value Reply
Sharers = {P};
Read miss:
Fetch;
Data Value Reply
msg to remote cache
Sharers += {P};
Read miss:
Data Value Reply
Sharers += {P};
Write Miss:
Fetch/Invalidate;
Data Value Reply
msg to remote cache
Sharers = {P};
Notes: 57
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 58: Example Directory Protocol
Message sent to directory causes two actions:
  Update the directory
  More messages to satisfy request
Block is in Uncached state: the copy in memory is the current value; only possible requests for that block are:
  Read miss: requesting processor sent data from memory &requestor made only sharing node; state of block made Shared.
  Write miss: requesting processor is sent the value & becomes the Sharing node. The block is made Exclusive to indicate that the only valid copy is cached. Sharers indicates the identity of the owner.
Block is Shared => the memory value is up-to-date:
  Read miss: requesting processor is sent back the data from memory & requesting processor is added to the sharing set.
  Write miss: requesting processor is sent the value. All processors in the set Sharers are sent invalidate messages, & Sharers is set to identity of requesting processor. The state of the block is made Exclusive.
Notes: 58

## Slide 59: Example Directory Protocol
Block is Exclusive: current value of the block is held in the cache of the processor identified by the set Sharers (the owner) => three possible directory requests:
  Read miss: owner processor sent data fetch message, causing state of block in owner’s cache to transition to Shared and causes owner to send data to directory, where it is written to memory & sent back to requesting processor. Identity of requesting processor is added to set Sharers, which still contains the identity of the processor that was the owner (since it still has a readable copy). State is shared.
  Data write-back: owner processor is replacing the block and hence must write it back, making memory copy up-to-date (the home directory essentially becomes the owner), the block is now Uncached, and the Sharer set is empty.
  Write miss: block has a new owner. A message is sent to old owner causing the cache to send the value of the block to the directory from which it is sent to the requesting processor, which becomes the new owner. Sharers is set to identity of new owner, and state of block is made Exclusive.
Notes: 59

## Slide 60: Case Study: p1 write 888 to x
P1(local) P5(home) P2(remote) P3(remote)
P1
P2
X=111
P3
X=111
P4
P5
X’HOME
111
P6
Direct: X: S, {P2,P3}
Cache:X: S
Cache: X: S
Cache X: I
WriteMiss X
Invalidate X
Invalidate X
Ack
Cache:X: I
Cache:X: I
Ack
Direct: X: E, {P1}
Reply X=111
Cache X: E, 888

## Slide 61: P2 write 999 to X
P1(remote) P5(home) P2(local) P3(remote)
P1
X=888
P2
P3
P4
P5
X’HOME
111
P6
X: S, {P2,P3}
X: S
X: S
X: I
X: I
X: I
X: E, {P1}
X: E, 888

## Slide 62: Answer for P2 write 999 to X
P1(remote) P5(home) P2(local) P3(remote)
P1
X=888
P2
P3
P4
P5
X’HOME
111
P6
X: S, {P2,P3}
X: S
X: S
X: I
X: I
X: I
X: E, {P1}
X: E, 888
WriteMiss
Fetch/Invalidate
X: I
Write back X 888
888
X: E,｛P2}
Data reply X 888
X: E, 999
How about P2 read x？

## Slide 63: More Cases for Cache Coherence of Directory Protocol

## Slide 64
Could you feel the blanks to complete the directories ?

## Slide 65
I
P0 read 300

## Slide 66
What operations will do when P0 read 300 ?
I
DataReply 300(0300)
S 300 0300
P0 read 300
ReadMiss 300
{P0} S 300 0300

## Slide 67
P0(local node) P2(home node)
ReadMiss for Tag=300
DataReply 0300
M2, 300, {}, U  {P0}, S
Cach0,
B0: I, 100, 0100
S, 300, 0300
P0 read 300

## Slide 68
What operations will do when P2 read 218 ?
I
ReadMiss(218)
Fetch(218)
S
Writeback 218(1218)
{P0,P2} S 218 1218
Modify Directory
P0 read 300
DataReply 218(1218)
S 218 1218

## Slide 69
P2(local node) P1(home node) P0(remote node)
ReadMiss for Tag=218
DataReply 218(1218)
M1,
218, {P0}, E, 0218
{P1,P0}, S, 1218
Cach2,
B3: I, 118, 0318
S, 218, 1218
Fetch Tag=218
Cach0,
B3: E, 218, 1218
S, 218, 1218
WriteBack218(1218)
P2 read 218

## Slide 70
What operations will do when P1 write 0888 into 310 ?
I
WriteMiss(310)
ACK
{P1} E
P0 read 300
invalidate 310
I
I
invalidate 310
ACK
DataReply 310(0310)
E 310 0310
E 310 0888

## Slide 71
P1(local node ) P2(home node) P0. P2 (remote node)
WriteMiss for Tag=310
DataReply 0310
M2,
310,{P0,P2},S,0310
{P1}, E, 0310
Invalidate Tag=310
Cach0, Cache2
B2: S, 310, 0310
I, 310, 0310
Ack
P1 write 0888 into 310
Cache1,
B2:S, 110, 0110
E, 310, 0888
Anything UNcomfortable ?

## Slide 72
What operations will do when P1 write 0888 into 310 ?
I
WriteMiss(310)
P0 read 300
{ } U
The directory is outdated
with wrong info.
How to solve it?

## Slide 73
P1(local node ) P2(home node) P0(remote node)
WriteMiss for Tag=310
DataReply 0310
M2,
310,{P0,P2},S,0310
{P1}, E, 0310
Invalidate Tag=310
Cach0, {Cache2}
B2: S, 310, 0310
I, 310, 0310
Ack
P1 write 0888 into 310
Cache1,
B2:S, 110, 0110
E, 310, 0888
Kickout 110
M0,
110,{P1},S,0110
{ }, U, 0110

## Slide 74: Example 1: initial
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
Notes: 74

## Slide 75: Example: P1 write 10 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
Notes: 75

## Slide 76: Example: P1 read A1, P2 read A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
Notes: 76

## Slide 77: Example: P2 write 20 to A1
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
Notes: 77

## Slide 78: Example: P2 write 40 to A2
A1 and A2 map to the same cache block
Processor 1
Processor 2
Interconnect
Memory
Directory
A1
Notes: 78

## Slide 79
Implementation of Directory-base Coherence

## Slide 80: Implementation issues
Nonatomic operations
Write serialization
Without Broadcast

## Slide 81: Assumptions for implementation simplicity
Network provides point-to-point in-order delivery of message
Network has unlimited buffering
Network delivers all messages within a finite time.
Coherence controller is duplicated for each cache block.
A transition only completes when a message has been transmitted and a data value reply received.
  Omit the pending status
Outgoing message can be transmitted before the next incoming message is accepted.

## Slide 82: Deadlock example
Assume P1 and P2 each have exclusive copies of cache blocks X1 and X2 that have different home directories.
Resolve: duplicate coherence controller for each block

## Slide 83: CPU -Cache State Machine
State machine for CPU requests for each memory block
Invalid state if in memory
Nov. 12 2008
Fetch/Invalidate
Data Write Back
Invalidate
Invalid
Shared
(read/only)
Exclusive
(read/writ)
CPU Read
CPU Read hit
Send Read Miss
CPU Write: Send Write Miss
to h.d.
CPU Write hit:Send invalidate to home directory
CPU read hit
CPU write hit
Fetch: Data Write Back to home directory
CPU read miss:
Send Read Miss
CPU write miss:
Data Write Back
and send Write Miss to home
directory
CPU read miss:
Data Write Back and
Send read miss to home directory
CPU Write miss:Send Write Miss to home directory
Notes: 83
Invalid:
read => shared
write => dirty
shared looks the same

## Slide 84: How to assure write serialization ?
Serialization exclusive access by Home directory
  Buffer all the request (write miss/ invalidate );
  Process the request in order;
  Only start to process the new request until complete the previous one.

## Slide 85: How to solve the “race” ?
How does the processor know who is the winner?
  Get acknowledgement message from home directory
    Date Reply (For write miss)
    Explicit ACK (For invalidate)
  About the loser:
    Simplest: home directory send a NAK to loser.
How to know the invalidations are completed?
  1. Directory collect and count ACK messages from remote nodes, and then send confirmation to requester.
  2. Home node collect and count ACK messages from remote nodes directly.

## Slide 86: Buffer requirement
Large amount of buffers required
A write miss may produce a large amount invalidate message
Prefetch scheme might be used
Multiple outstanding misses
Limited buffer in practice

## Slide 87: Avoid deadlock with limited buffering
Deadlock arises from three properties
  More than one resource is needed to complete a transaction
  Buffers for request, reply, and accept message
Resources are held until a nonatomic transaction completes
There is no global partial order on the acquisition of resource

## Slide 88: Resolution
Strategy: Try to ensure that the resources will always be available.
  Separate network is used for request and replies.
  Every request need a reply allocate the space to accept reply when the request is generated.
    Replier can free the reply buffer.
  Any controller can reject any request with a NAK, but never NAK a reply.
  Any request that receives a NAK is simply retried.

## Slide 89: Multithreaded directory to handle multiple blocks
Directory controller must be reentrant.
  Handle incoming requests for independent blocks before the previous one finished.
Control state need be saved and restored while a fetch(or fetch//invalidate) is outstanding
Owner node can provide the data directly to the requester as well as to the home node to reduce latency.
Can limit the outstanding transaction numbers via NAK to new requests.

## Slide 90: How to deal with NAK ?
How to know which is the original transaction ?
  1. processor keep track of its outstanding requests
  2. Pack the original request into NAK.
  3. The buffer holding the return slot for the request can also hold info about the request.
So that when receives NAK, the processor know to resend the request.

## Slide 91: Summary
Nov. 12 2008
Caches contain all information on state of cached memory blocks
Snooping and Directory Protocols similar; bus makes snooping easier because of broadcast (snooping => uniform memory access)
Directory has extra data structure to keep track of state of all cache blocks
Distributing directory => scalable shared address multiprocessor => Cache coherent, Non uniform memory access

## Slide 92: How about write through cache with write invalidate?
Nov. 12 2008
Invalid
Valid
PR
[ BR miss on bus]
PW
[ BW miss on bus]
BW
BR, PR
PW
[send BW]

## Slide 93: **Thinking： Are Coherence Protocol States Vulnerable to Information Leakage?

## Slide 94: Review: Cache Coherence Protocols
MSI Coherence Protocol
MESI Coherence Protocol
Exclusive State
Accelerate write-after-read accesses!
Notes: Cache coherence should be preserved on any multicore system such that different cores can access the same value for the same memory location.
In this paper, We focus mainly on directory-based coherence protocols as modern processors often adopt this design
The MSI protocol is seminal and all coherence protocols deployed on modern multicore chips inherit its three states—Modified, Shared, and Invalid
To optimize MSI protocol, The MESI protocol introduces an Exclusive state to make the S state more fine-grained and save coherence traffic.
So, Why the introduction of E state could be an optimization?
The E state helps accelerate write-after-read accesses [46], [65].
With E state, the cache knows it’s the only owner of the block, so it can write the cache line without notifying other cores.
However, Without the E state, MSI marks a clean data block with the S state. To serve a subsequent write request targeting the S-state block, the core needs to request ownership. This triggers further invalidation commands to other cores for avoiding potential stale copies.

## Slide 95: Review: Coherence-based Timing Channel
E
X
Directory
E
X
❶
❶ Core A request directory for memory location X
❷ Directory forwards request to Core B
❷
❸
❸ Core B sends response to Core A
core A
core B
core C
E-state coherence request
S
X
Directory
S
X
❶
❶ Core A requests Directory for memory location X
❷ LLC sends response to Core B
❷
core A
core B
core C
S-state coherence request
S
X
[HPCA’18] Are Coherence Protocol States Vulnerable to Information Leakage?
Notes: However, the optimization of E state brings security vulnerabilities: there is a coherence-based timing channel
it arises from different access latencies for fetching data blocks in E state and S state upon a cache miss.
Here we present the process to access an E-state or S-state block for memory location X in the LLC.
Firstly E state.
Since Core A has no copy of data in iits private caches, it sends a request to the directory (step 1).
The directory finds that the X-addressed data block is exclusively cached on core B.
Although the LLC also has a copy for X, the E state makes the directory hard to ensure whether the value in the LLC is obsolete. Therefore, the directory forwards the request to the owner—Core B (step 2). Upon receiving the forwarded request, Core B responds Core A with data.
In contrast, when the requested data block is in the S state , the directory ensures that the copy in the LLC holds the same value with that of other copies cached in some core’s private caches.
The directory thus more quickly returns the requested data block from the LLC.

## Slide 96: Review: S-MESI
EMA
X
E
X
Directory
E
X
Directory
M
X
M
X
1. write X
Private
Cache
LLC
2a. upgrade
2b. transition
3a. ack
3b. transition
4. transition
Notes: To defend against this attack, the state-of-the-art countermeasure, we name it S-MESI, returns the requestd data in both states E and S from the LLC
However, this nullifies the silent upgrade effect from E to M that the E state is supposed to offer.
When traditional silent upgrade updates the E-state block in private caches into state M, its corresponding copy in the LLC stays in state E.
Directly returning E-state data from the LLC likely results in accessing stale data.
Therefore, SMESI revokes silent upgrade and enforces the M state to be synchronized across both private caches and the LLC.
Let’s see the process
Upon receiving a write request for a private data block in state E (step 1)
the core sends a coherence request to the LLC for privilege upgrade (step 2a) and transits state E to a transient EMA state (step 2b).
It then waits for the LLC’s acknowledgement (step 3a)
The acknowledgement from the LLC triggers private caches to update the EMA state to the M state

## Slide 97: SwiftDir: Overview
We observe that
The coherence attack exploits only shared data.
S-MESI nullifies state E and complicates the E→M transition for all data.
So SwiftDir
Shrink protection scope to exploitable shared data which is actually write-protected.
Remove their redudant E state from coherence.
Chenlu Miao, Kai Bu, Mengming Li, Shaowu Mao, Jianwei Jia: SwiftDir: Secure Cache Coherence without Overprotection. MICRO 2022: 662-677
Notes: We observe that the inevitable overhead by nullifying the E state arises from overprotection.
Since the coherence attack exploits only shared data, protecting only shared data is sufficient.
However, S-MESI nullifies state E and complicates the E→M transition for unshared data.
We are motivated to minimize the protection scope.
We find that exploitable shared data belong to write-protected data, whose E state is redundant.
We can simply remove their E state from coherence to fundamentally throttle the exploited E/S timing difference.

## Slide 98: SwiftDir: Design
Identification of Shared Memory
  Exploited Shared Memory is Write-protected
  Write-protected Manifests in PTE R/W Field
Argumentation of Sharing Status
Modification of Coherence Protocol
Notes: We leverage the MMU to identify exploitable shared memory
It’s based on two observations.
First, we find that exploited shared memory is write-protected.
The coherence attack generates shared memory in two ways, first by using shared library, and the second by using memory deduplication. They are all write-protected.
Then, we find that write-protected manifests in page table entry’s read/write field.

## Slide 99: SwiftDir: Design
Identification of Shared Memory
Argumentation of Sharing Status
  PIPT/VIPT/VIVT L1
Modification of Coherence Protocol
Notes: With the write-protected information, next SwiftDir hitchhikes address translation to transmit the write-protected information from the MMU to the cache hierarchy for coherence maintenance.
Different cache architectures lead to respective complexities to this hitchhiking method.
VIVT, for example. It allows the core to send a virtual address to the L1 cache even prior to address translation. To address such a concern, we thoroughly investigate all the three cache architectures in commercial use—PIPT, VIPT, and VIVT
We find that SwfitDir suffices for the LLC to obtain the write-protected information of the requested data until the request arrives at the LLC. This requirement can be easily satisfied regardless of cache architecture, simply because that the LLC is a physical cache and address translation should have taken place before accessing the LLC

## Slide 100: SwiftDir: Design
Identification of Shared Memory
Argumentation of Sharing Status
Modification of Coherence Protocol
Notes: Finally, it’s about modification of coherence protocol.
SwiftDir imposes minimum modification on existing coherence protocols by narrowing down the protection scope to only write-protected data
Motivated by the observation that write-protected data are not supposed to be written, we consider it less necessary to maintain their E state.
SwiftDir thus directly sets an initial load of write-protected data in the S state instead of the E state
This way, write-protected data no longer transit to the E state and are immune from timing-channel attacks

## Slide 101: Evaluation
Notes: We did a series of experiments to evaluate the SwiftDir.
First for security issue, We measure the access latency of traditionally vulnerable shared data to show that SwiftDir successfully prevents the timing channel
This figure reports the cumulative distribution function (CDF) of Load WP(L1I&L2S) by SwiftDir, in comparison with that of Load(L1I&L2S) by MESI.
It can been seen that it leaves the attacker with no timing difference to exploit.

## Slide 102: Conclusion
SwiftDir is the first attempt to secure cache coherence with performance gains.
This promises a way of protection by simplification rather than complication.
Notes: We make the conclusion:
SwiftDir is the first attempt to secure cache coherence with performance gains.
This promises a way of protection by simplification rather than complication.