## Slide 1: Ch5-4 Models of Memory Consistency

## Slide 2: Cache coherence
Cache coherence ( Value, same location)
  “Common Sense”
    P1 Read[X] => P1 Write[X] => P1 Read[X] will return X
    P2 Read[X] => P1 Write[X] => will return value written by P1
    P1 Write[X] => P2 Write[X] => Serialized (all processor see the writes in the same order)

## Slide 3: Objective of Cache Coherence
Maintain the integrity of data in cache and memory
  What value can be returned by a read.
Keep the performance of multiple processors
Make cache transparent to the processors (not always true)
Haven’t solve the problem
  When must a processor see a value that has been updated by another processor ?

## Slide 4: Memory Consistency
Definition:
  When must a processor see a value that has been updated by another processor ?
  What properties must be enforced among reads and writes to different locations by different processors ?

## Slide 5: Example （ p243）
P1: A=0; P2: B=0;
… …
A=1; B=1;
L1: if ( B==0)… L2: if ( A==0)...
Assume: A,B are both cached by P1, P2 with the initial value of 0.
How about the if statement ?
Unknown, it depends !

## Slide 6: Analyze the result:
P1: A=0; P2: B=0;
… …
A=1; B=1;
L1: if ( B==0)… L2: if ( A==0)...
If the write result can be seen immediately by other processors, then ….
If the write can be delayed, then …

## Slide 7: Objectives of Memory Consistency Model
Defines the behavior and correctness of a program.
Impose ordering constraints
Balance programming complexity and performance

## Slide 8: Sequential Consistency
Memory accesses executed by each processor were kept in order
Memory accesses among different processors were interleaved.
P1: A=0; P2: B=0;
… …
A=1; B=1;
L1: if ( B==0)… L2: if ( A==0)...
False True/false
True/false False
No way to see True Ture !

## Slide 9: Sequential Consistency
Characteristic: Delay next memory access until the previous one is completed.
Simple programming paradigm
Long latency, bad performance
  Even write buffer is not permitted.
  Nonblocking cache ?

## Slide 10: Performance analysis for Sequential Consistency
Assume
  50 cycles to establish ownership when write miss；
  10 cycles to issue each invalidation;
  80 cycles for an invalidation to complete and be acknowledged.
  4 other processors share a cache block.
Question：How long does a write miss stall the processor is SC is used？
Answer：
  50 +（10+10+10+10）+ 80 = 170 （CC）

## Slide 11: How to improve performance ?
Latency-hiding techniques
Less restrictive memory consistency model

## Slide 12: The programmer’s View
Simple programming model
High performance implementation
Simple Programming model:
  synchronized programs:
  All access to shared data are ordered by synchronization operations.
  A synchronized program will behave as if the hardware implemented sequential consistency.
  No Data Race !

## Slide 13: Synchronized program
A program is synchronized if all access to shared data are ordered by synchronization operations.
For any shared data x,
write( Pi, x)
Release(Pi, x)
Acquire(Pj, x)
access(Pj, x)

## Slide 14: Relaxed Consistency Model
Objective:
  simple programming & high performance
Key idea:
  allow read and writes to complete out of order, but to use synchronization operations to enforce ordering, so that a synchronized program behave as if the processor were sequentially consistent with a better performance.
Orders:
  RW, RR, W R, WW
  SaR, Sa W, SrR, SrW, SS

## Slide 15: Memory consistency model
WSA, RSA,
SRW,SRR

## Slide 16: What to decide R.W order ?
If there is data dependence, then keep the sequential order
Otherwise decided by Memory Consistency Model

## Slide 17: Total Store Order (IBM370)

## Slide 18: TSO: FIFO write buffer
P1
Store buffer
P1
Store buffer
Memory

## Slide 19: TSO vs. SC
TSO both can get old values
SC at least one has to get the value of new

## Slide 20: Partial Store Order (sparc)

## Slide 21: Weak ordering (PowerPC)

## Slide 22: Release consistency (Alpha, MIPS)

## Slide 23
Thank you !