## Slide 1
Ch3-- ILP & its exploration
Ch3-2
Dynamic scheduling
--Tomasulo Algorithm
Scoreboard + Register Renaming
3.4， 3.5

## Slide 2: Scoreboard vs. Tomasulo
特点
  Multiple multiplier, etc. Funcs
  Issue in order, Complete OOO
  IF Issue, Ro
  4 stages pipeline
  Scoreboare centralized control
缺点
  Stall when WAW, WAR
  Fewer Func, unpipelined
  Issue in order, Complete OOO
  FP op. queue, Reservation station, LD/ST buffer, CDB
  Reg. RenameNo WAW, WAR
  Reduce structural hazard
  RAW detection decentralized—reservation
  CDB forwarding path

## Slide 3: Dynamic Scheduling with Tomasulo’s Algorithm
For IBM 360/91 (before caches!)
Goal: High Performance without special compilers
Small number of floating point registers (4 in 360) prevented interesting compiler scheduling of operations
  This led Tomasulo to try to figure out how to get more effective registers — renaming in hardware!
Why Study 1966 Computer?
The descendants of this have flourished!
  Alpha 21264, HP 8000, MIPS 10000, Pentium III, PowerPC 604, …

## Slide 4: Tomasulo Algorithm
Control & buffers distributed with Function Units (FU)
  FU buffers called “reservation stations”; have pending operands
Registers in instructions replaced by values or pointers to reservation stations(RS); called register renaming ;
  avoids WAR, WAW hazards
  More reservation stations than registers, so can do optimizations compilers can’t
Results to FU from RS, not through registers, over Common Data Bus that broadcasts results to all FUs
Load and Stores treated as FUs with RSs as well
Integer instructions can go past branches, allowing FP ops beyond basic block in FP queue

## Slide 5: Tomasulo Organization
FP adders
Add1
Add2
Add3
FP multipliers
Mult1
Mult2
From Mem
FP Registers
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP Op
Queue
Load Buffers
Store
Buffers
Load1
Load2
Load3
Load4
Load5
Load6
From Intruction unit
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 6: Reservation Station Components
Reservation station:
Op: Operation to perform in the unit
Vj, Vk: Value of Source operands
  Store buffers has V field, result to be stored
Qj, Qk: Reservation stations producing source registers (value to be written)
  Note: Qj,Qk=0 => ready
  Store buffers only have Qi for RS producing result
A: hold info. for memory address calculation
Busy: Indicates reservation station or FU is busy
Register result status—Indicates which functional unit will write each register, if one exists. Blank when no pending instructions that will write that register.
Notes: What you might have thought
1. 4 stages of instruction executino
2.Status of FU: Normal things to keep track of (RAW & structura for busyl):
Fi from instruction format of the mahine (Fi is dest)
Add unit can Add or Sub
Rj, Rk - status of registers (Yes means ready)
Qj,Qk - If a no in Rj, Rk, means waiting for a FU to write result; Qj, Qk means wihch FU waiting for it
3.Status of register result (WAW &WAR)s:
which FU is going to write into registers
Scoreboard on 6600 = size of FU
6.7, 6.8, 6.9, 6.12, 6.13, 6.16, 6.17
FU latencies: Add 2, Mult 10, Div 40 clocks

## Slide 7: Three Stages of Tomasulo Algorithm
Issue—get instruction from FP Op Queue
  If reservation station free (no structural hazard), control issues instr & sends operands (renames registers).
Execute—operate on operands (EX)
  When both operands ready then execute; if not ready, watch Common Data Bus for result
Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting units; mark reservation station available

## Slide 8: Data path
Normal data bus: data + destination (“go to” bus)
Common data bus: data + source (“come from” bus)
  64 bits of data + 4 bits of Functional Unit source address
  Write if matches expected Functional Unit (produces result)
  Does the broadcast
Example speed: 3 clocks for Fl .pt. +,-; 10 for * ; 40 clks for /

## Slide 10: Tomasulo Example
Clock cycle counter
FU count
down
Instruction stream
3 Load/Buffers
3 FP Adder R.S.
2 FP Mult R.S.

## Slide 11: Tomasulo Example Cycle 1

## Slide 12: Tomasulo Example Cycle 2
Note: Can have multiple loads outstanding

## Slide 13: Tomasulo Example Cycle 3
Note: registers names are removed (“renamed”) in Reservation Stations; MULT issued
Load1 completing; what is waiting for Load1?

## Slide 14: Tomasulo Example Cycle 4
Load2 completing; what is waiting for Load2?

## Slide 15: Tomasulo Example Cycle 5
Timer starts down for Add1, Mult1

## Slide 16: Tomasulo Example Cycle 6
Issue ADDD here despite name dependency on F6?

## Slide 17: Tomasulo Example Cycle 7

## Slide 18: Tomasulo Example Cycle 8
Add1 (SUBD) completing; what is waiting for it?

## Slide 19: Tomasulo Example Cycle 9

## Slide 20: Tomasulo Example Cycle 10

## Slide 21: Tomasulo Example Cycle 11

## Slide 22: Tomasulo Example Cycle 12
Add2 (ADDD) completing; what is waiting for it?

## Slide 23: Tomasulo Example Cycle 13
All simple operation are end here.

## Slide 24: Tomasulo Example Cycle 14

## Slide 25: Tomasulo Example Cycle 15
Mult1 (MULTD) completing; what is waiting for it?

## Slide 26: Tomasulo Example Cycle 16
Just waiting for Mult2 (DIVD) to complete

## Slide 27: Tomasulo Example Cycle 17

## Slide 28: Tomasulo Example Cycle 55

## Slide 29: Tomasulo Example Cycle 56
Mult2 (DIVD) is completing; what is waiting for it?

## Slide 30: Tomasulo Example Cycle 57
Once again: In-order issue, out-of-order execution and out-of-order completion.

## Slide 31: Tomasulo’s scheme offers 3 major advantages
The distribution of the hazard detection logic
  distributed reservation stations and the CDB
  If multiple instructions waiting on single result, & each instruction has other operand, then instructions can be released simultaneously by broadcast on CDB
  If a centralized register file were used, the units would have to read their results from the registers when register buses are available.
The elimination of stalls for WAW and WAR hazards

## Slide 32: Tomasulo Drawbacks
Complexity
  delays of 360/91, MIPS 10000, Alpha 21264, IBM PPC 620 in CA:AQA 2/e, but not in silicon!
Many associative stores (CDB) at high speed
Performance limited by Common Data Bus
  Each CDB must go to multiple functional units high capacitance, high wiring density
  Number of functional units that can complete per cycle limited to one!
    Multiple CDBs  more FU logic for parallel assoc stores
Non-precise interrupts!
  We will address this later

## Slide 33: Why can Tomasulo overlap iterations of loops?
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall that we saw in the scoreboard.
Other perspective: Tomasulo building data flow dependency graph on the fly.

## Slide 34: Tomasulo overlap iterations of loops
Register renaming
  Multiple iterations use different physical destinations for registers (dynamic loop unrolling).
Reservation stations
  Permit instruction issue to advance past integer control flow operations
  Also buffer old values of registers - totally avoiding the WAR stall that we saw in the scoreboard.
Other perspective: Tomasulo building data flow dependency graph on the fly.

## Slide 35: Loop Example

## Slide 36: Tomasulo Loop Example
Loop: LD F0 0 R1
MULTD F4 F0 F2
SD F4 0 R1
SUBI R1 R1 #8
BNEZ R1 Loop
Assume Multiply takes 4 clocks
Assume first load takes 8 clocks (cache miss), second load takes 1 clock (hit)
To be clear, will show clocks for SUBI, BNEZ
Reality: integer instructions ahead

## Slide 37: Loop Example Cycle 1

## Slide 38: Loop Example Cycle 2

## Slide 39: Loop Example Cycle 3
Implicit renaming sets up “DataFlow” graph

## Slide 40: Loop Example Cycle 4
Dispatching SUBI Instruction

## Slide 41: Loop Example Cycle 5
And, BNEZ instruction

## Slide 42: Loop Example Cycle 6
Notice that F0 never sees Load from location 80

## Slide 43: Loop Example Cycle 7
Register file completely detached from computation
First and Second iteration completely overlapped

## Slide 44: Loop Example Cycle 8

## Slide 45: Loop Example Cycle 9
Load1 completing: who is waiting?
Note: Dispatching SUBI

## Slide 46: Loop Example Cycle 10
Load2 completing: who is waiting?
Note: Dispatching BNEZ

## Slide 47: Loop Example Cycle 11
Next load in sequence

## Slide 48: Loop Example Cycle 12
Why not issue third multiply?

## Slide 49: Loop Example Cycle 13

## Slide 50: Loop Example Cycle 14
Mult1 completing. Who is waiting?

## Slide 51: Loop Example Cycle 15
Mult2 completing. Who is waiting?

## Slide 52: Loop Example Cycle 16
16

## Slide 53: Loop Example Cycle 17
16
17

## Slide 54: Summary of Tomasulo Algorithm
Reservations stations: implicit register renaming to larger set of registers + buffering source operands
  Prevents registers as bottleneck
  Avoids WAR, WAW hazards of Scoreboard
  Allows loop unrolling in HW
Not limited to basic blocks
  (integer units gets ahead, beyond branches)
Lasting Contributions
  Dynamic scheduling
  Register renaming
  Load/store disambiguation
360/91 descendants are Pentium III; PowerPC 604; MIPS R10000; HP-PA 8000; Alpha 21264

## Slide 55: What about Precise Interrupts?
Tomasulo had: In-order issue, out-of-order execution, and out-of-order completion
Need to “fix” the out-of-order completion aspect so that we can find precise breakpoint in instruction stream.
 Speculation，Reorder buffer ! (later )

## Slide 56: Scoreboard vs. Tomasulo
特点
  Multiple multiplier, etc. Funcs
  Issue in order, Complete OOO
  IF Issue, Ro
  4 stages pipeline
  Scoreboare centralized control
缺点
  Stall when WAW, WAR
  特点
    Fewer Func, unpipelined
    Issue in order, Complete OOO
    FP op. queue, Reservation station, LD/ST buffer, CDB
    3 stages pipeline
    Reg. RenameNo WAW, WAR
    Reduce structural hazard
    RAW detection decentralized—reservation
    CDB forwarding path
Can Scoreboard avoid WAW, WAR with Reg. Rename?

## Slide 57: Scoreboard Pipeline stage description
Issue: a instruction is issued when
  The functional unit is available and
  No other active instruction has the same destination register.
  Avoid strutural hazard and WAW hazard
Read Operands (RD)
  The read operation is delayed until both the operands are available.
  This means that no previously issued but ncompleted instruction has the operand as its destination.
  This resolves RAW hazards dynamically
Execution (EX)
  Notify the scoreboard when completed so the functional unit can be reused.
Write result (WB)
  The scoreboard checks for WAR hazards and stalls the completing instruction if necessary.

## Slide 58: The scoreboard algorithm
Scoreboard-takes full responsibility for instruction issue and execution
  Create the dependence records
  Decide when to fetch the operand
  Decide when to enter execution
  Decide when the result can be written into the register file
Three data structure
  Instruction status:
    which of the four steps the instruction is in
  Functional unit status: buzy,op,Fi, Fj,Fk,Qj,Qk ,Rj,Rk
  Register result status:
    which functional unit will write that register

## Slide 59: Explicit Register Renaming
Make use of a physical register file that is larger than number of registers specified by ISA
Key insight: Allocate a new physical destination register for every instruction that writes
  Very similar to a compiler transformation called Static Single Assignment (SSA) form — but in hardware!
  Removes all chance of WAR or WAW hazards
  Like Tomasulo, good for allowing full out-of-order completion
  Like hardware-based dynamic compilation?
Mechanism? Keep a translation table:
  ISA register  physical register mapping
  When register written, replace entry with new register from freelist.
  Physical register becomes free when not used by any active instructions

## Slide 60: Advantages of Explicit Renaming
Decouples renaming from scheduling:
  Pipeline can be exactly like “standard” MIPS pipeline (perhaps with multiple operations issued per cycle)
  Or, pipeline could be Tomasulo-like or a scoreboard, etc.
  Standard forwarding or bypassing could be used
Allows data to be fetched from single register file
  No need to bypass values from reservation station or reorder buffer
  This can be important for balancing pipeline

## Slide 61: Adv. Explicit Renaming (cont.)
Many processors use a variant of this technique:
  R10000, Alpha 21264, HP PA8000
Another way to get precise interrupt points:
  All that needs to be “undone” for precise break point is to undo the table mappings
  Provides an interesting mix between reorder buffer and future file
    Results are written immediately back to register file
    Registers names are “freed” in program order (by ROB)
What’s Future File ?

## Slide 62: Explicit Renaming Support Includes:
Rapid access to a table of translations
A physical register file that has more registers than specified by the ISA
Ability to figure out which physical registers are free.
  No free registers  stall on issue
Thus, register renaming doesn’t require reservation stations. However:
  Many modern architectures use explicit register renaming + Tomasulo-like reservation stations to control execution.
Two Questions:
  How do we manage the “free list”?
  How does Explicit Register Renaming mix with Precise Interupts?

## Slide 63: Explicit register renaming: (R1000 Style)
Physical register file larger than ISA register file
On issue, each instruction that modifies a register is allocated new physical register from freelist
Done?
Oldest
Newest
P0
P2
P4
F6
F8
P10
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P32
P34
P36
P38

P60
P62
Current Map Table
Freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 64: Explicit register renaming: (R1000 Style)
Note that physical register P0 is “dead” (or not “live”) past the point of this load.
  When we go to commit the load, we free up
F0
P0
LD P32,10(R2)
N
Done?
Oldest
Newest
P32
P2
P4
F6
F8
P10
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P34
P36
P38
P40

P60
P62
Current Map Table
Freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 65: Explicit register renaming: (R1000 Style)
F10
F0
P10
P0
ADDD P34,P4,P32
LD P32,10(R2)
N
N
Done?
Oldest
Newest
P32
P2
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P36
P38
P40
P42

P60
P62
Current Map Table
Freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 66: Explicit register renaming: (R1000 Style)
--
--
F2
F10
F0
P2
P10
P0
BNE P36,<…>
N
DIVD P36,P34,P6
ADDD P34,P4,P32
LD P32,10(R2)
N
N
N
Done?
Oldest
Newest
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Current Map Table
Freelist
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Checkpoint at BNE instruction
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 67: Explicit register renaming: (R1000 Style)
--
F0
F4
--
F2
F10
F0
P32
P4
P2
P10
P0
ST 0(R3),P40
ADDD P40,P38,P6
Y
Y
LD P38,0(R3)
Y
BNE P36,<…>
N
DIVD P36,P34,P6
ADDD P34,P4,P32
LD P32,10(R2)
N
y
y
Done?
Oldest
Newest
P40
P36
P38
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P42
P44
P48
P50

P0
P10
Current Map Table
Freelist
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Checkpoint at BNE instruction
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 68: Explicit register renaming: (R1000 Style)
F2
F10
F0
P2
P10
P0
DIVD P36,P34,P6
ADDD P34,P4,P32
LD P32,10(R2)
N
y
y
Done?
Oldest
Newest
Current Map Table
Freelist
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Checkpoint at BNE instruction
P32
P36
P4
F6
F8
P34
P12
P14
P16
P18
P20
P22
P24
p26
P28
P30
P38
P40
P44
P48

P60
P62
Speculation error fixed by restoring map table and freelist
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 69: Can we use explicit register renaming with scoreboard?
Rename
Table
Functional Units
Registers
FP Mult
FP Mult
FP Divide
FP Add
Integer
Memory
SCOREBOARD

## Slide 70: Four Stages of Scoreboard Control With Explicit Renaming
Issue—decode instructions & check for structural hazards & allocate new physical register for result
  Instructions issued in program order (for hazard checking)
  Don’t issue if no free physical registers
  Don’t issue if structural hazard
Read operands—wait until no hazards, read operands
  All real dependencies (RAW hazards) resolved in this stage, since we wait for instructions to write back data.
Execution—operate on operands
  The functional unit begins execution upon receiving operands. When the result is ready, it notifies the scoreboard
Write result—finish execution
Note: No checks for WAR or WAW hazards!

## Slide 71: Scoreboard With Explicit Renaming
Initialized Rename Table

## Slide 72: Renamed Scoreboard 1
Each instruction allocates free register
Similar to single-assignment compiler transformation

## Slide 73: Renamed Scoreboard 2

## Slide 74: Renamed Scoreboard 3

## Slide 75: Renamed Scoreboard 4
Next step Int1 will write result, where need
the value?

## Slide 76: Renamed Scoreboard 5
Next step Int2 will write result, where need
the value?

## Slide 77: Renamed Scoreboard 6
Why ADDD not issue ? Structure hazard ! Adder is occupied by with SUBD.

## Slide 78: Renamed Scoreboard 7

## Slide 79: Renamed Scoreboard 8
Next step Adder will complete execution

## Slide 80: Renamed Scoreboard 9
Next step Adder will write result, where need the value?

## Slide 81: Renamed Scoreboard 10
Adder is cleared, so ADDD can be issued next cycle.

## Slide 82: Renamed Scoreboard 11
WAR Hazard gone!
Notice that P32 not listed in Rename Table
  Still live. Must not be reallocated by accident
WAR dependence

## Slide 83: Renamed Scoreboard 12

## Slide 84: Renamed Scoreboard 13

## Slide 85: Renamed Scoreboard 14

## Slide 86: Renamed Scoreboard 15

## Slide 87: Renamed Scoreboard 16

## Slide 88: Renamed Scoreboard 17

## Slide 89: Renamed Scoreboard 18

## Slide 90: Renamed Scoreboard 19

## Slide 91: Summary #2
Explicit Renaming: more physical registers than needed by ISA.
  Separates renaming from scheduling
    Opens up lots of options for resolving RAW hazards
  Rename table: tracks current association between architectural registers and physical registers
  Potentially complicated rename table management