## Slide 1: Computer Architecture Experiment
Topic 5. Pipelined CPU supporting
multi-cycle operations (Out of Order Ver.)
浙江大学计算机学院
2022年11月

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of pipelines that support multicycle operations.
Master the design methods of pipelines that support multicycle operations supporting out of order issuing.
Master verification methods of pipelined CPU supporting multicycle operations.

## Slide 4: Experiment Task
Redesign the pipelines with IF/ID/FU/WB stages and FU stage supporting multicycle operations.
Redesign of CPU Controller.
Verify the Pipelined CPU with program and observe the execution of program.

## Slide 6: Pipelines resolving Data Hazards
FU units: ALU, MEM, MUL, DIV, JUMP

## Slide 7: Methods of resolving Control hazards
Predict-not-taken
Condition and Addr. Calculation in FU

## Slide 8: Out of order issue
Make CPU much efficient
Motivation: Different operations take different cycles:
  ALU: 1 cycle 1
  MEM: 2 cycles 2
  MUL: 7 cycles 3
  DIV: 24 cycles 4
  JUMP: 2 cycles 5
IF
IF
ID
FU-MUL
WB
ID
FU-ALU
WB
IF
ID
FU-MUL
WB

## Slide 9: Method: Reservation Register
A reservation register to record the running information of instructions issued (Why?)
  Writing Competition
Other associated registers to record other information
0
2
5
0
0
… …
reg[2:0] reservation_reg [0:31]
// shift per cycle
reg[5:0] FU_status // if some FU unit is in use
reg[4:0] FU_write_to [5:0] // rd of the instruction that use some FU unit
reg[5:0] FU_writeback_en // write enable signal of the instruction that use some FU unit
reg[4:0] FU_delay_cycles [5:0] (const value) // the ex cycles of some FU unit

## Slide 10: Method: Reservation Register
Basic Method:
  Every time trying to issue a operation that using some FU unit, detect if there exists any hazard and branch firstly and record its information into reservation registers secondly.
Hazard:
  Writing Competition
  Structure Hazard(FU unit busy)
  WAW
  RAW
Method for solve hazard: stall (No forwarding)

## Slide 11: Thinking Questions
Answer Following Questions in your report.
  Will there be WAR hazard? Why?
  Why the register reg_ID_flush_next is needed in CtrlUnit.v?
  Is there any progress that you think can make to this lab design? (Open question for 2022)

## Slide 12: Code to Fill in

## Slide 13: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00100093 | 0 | __start: | addi x1, x0, 1 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | FU unit hazard
3 | 004100b3 | C |  | add x1, x2, x4 | RAW
4 | fff08193 | 10 |  | addi x3, x1, -1 | FU unit hazard && RAW
5 | 00c02283 | 14 |  | lw x5, 12(x0) | 
6 | 01002303 | 18 |  | lw x6, 16(x0) | FU unit hazard
7 | 01402383 | 1C |  | lw x7, 20(x0) | FU unit hazard
8 | 40220433 | 20 |  | sub x8,x4,x2 | Reservation hazard
9 | ffd50493 | 24 |  | addi x9,x10,-3 | 
10 | 00520c63 | 28 |  | beq x4,x5,label0 | Branch Not taken
11 | 00420a63 | 2C |  | beq x4,x4,label0 | Reservation hazard, taken
12 | 03000a13 | 30 |  | addi x20,x0,48 | Reservation hazard
13 | 03400a13 | 34 |  | addi x20,x0,52 | 
14 | 03800a13 | 38 |  | addi x20,x0,56 | 

## Slide 14: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 03c00a13 | 3C |  | addi x20,x0,60 | 
16 | 00004537 | 40 | label0: | lui x10,4 | 
17 | 014005ef | 44 |  | jal x11,20 | 
18 | 04800a13 | 48 |  | addi x20,x0,72 | 
19 | 04c00a13 | 4C |  | addi x20,x0,76 | 
20 | 05000a13 | 50 |  | addi x20,x0,80 | 
21 | 05400a13 | 54 |  | addi x20,x0,84 | 
22 | ffff0617 | 58 |  | auipc x12, 0xffff0 | 
23 | 0223d6b3 | 5c |  | divu x13, x7, x2 | 
24 | 025206b3 | 60 |  | mul x13, x4, x5 | WAW
25 | 022687b3 | 64 |  | mul x15, x13, x2 | FU hazard && RAW
26 | 00400813 | 68 |  | addi x16, x0, 4 | WB quicklier
27 | 000008e7 | 6C |  | jalr x17,0(x0) | 
28 | 00000013 | 70 |  | addi x0, x0, 0 | 
29 | 00000013 | 74 |  | addi x0, x0, 0 | 
30 | 00000013 | 78 |  | addi x0, x0, 0 | 

## Slide 15: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 16: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;

## Slide 17: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 18
Thanks!