## Slide 1: Computer Organization & Design —The Hardware/Software Interface
Chapter 4-2 Processor Design
Pipelining CPU

## Slide 2: Instruction format
R-type: ALU rd, rs1, rs2
I-type: ALU rd, rs1, imm，LW rd, imm(rs1)
S-type: SW rs2, imm(rs1)
B-type: if rs1 op rs2 then pcpc + imm else pcpc+4
U-type: LUI rd, imm
J-type: JAL lable

## Slide 3: Function of Instructions
Instruction Fetch
IR InstMem[PC], PC4PC+4
Instruction decode & Read Oprand
A Reg[Rs], BReg[Rt], imm immgenerator, decode,
Execution
ALU： ALUoutA op B; ALUout  A op imm;
LW/SW： ALUout  A + imm; （address calculation）
Branch： cond  A compare B, PC PC + imm <<1 if taken;
Access Memory
LW： LMDR DataMem[ALUout] ; SW: B DataMem[ALUout]
Write Back
ALU： Rd  ALUout； LW：Rd  LMDR
Used Function Units
Instrction Mem, Adder
Register File(read), immgenerator
controller
ALU, comparator
Data Mem
Register File(write)

## Slide 4: Review
I-Memory and D-Memory are used in different stage.
PC+4, PC+4+imm<<2, ALU operation are calculated in different stages.
So memory and ALU can be shared in different stages.
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 5: Multicycle Approach (seldom used now)
We will be reusing functional units
  ALU used to ( A op B), compute address, increment PC,
  Memory used for instruction and data
We will use a finite state machine（FSM） for control

## Slide 6: Review: Finite state machines
Finite state machines:
  a set of states
  next state function (determined by current state and the input)
  output function (determined by current state and possibly input)

## Slide 7: Multi-cycle CPU datapath
ALU used for pc+4, pc+imm<<1, A op B，
separate comparator for condition comparing for Branch instruction

## Slide 8: Multicycle Approach
Break up the instructions into steps, each step takes a cycle
  balance the amount of work to be done
  restrict each cycle to use only one major functional unit
At the end of a cycle
  store values for use in later cycles
  introduce additional internal registers

## Slide 9: Multicycle Approach
a Multicycle datapath
shared unit

## Slide 10: How to use one memory to implement Inst. fetch and data access?
Address
Data out
Data
PC
PC
PC
ALUout
MUX
IorD
Instruction fetch
Can load data from memory
Can store data to Memory
B
WriteMem
ReadMem
IR
WriteIR
DR
WriteDR

## Slide 11: How to implement Adders and ALU ops using one ALU
ALU
Operation
A
ALUout
B
Only ALU operation
Can do PC+4 too
Can also do A+imm
(ALU-R-I)operation
Mem Address calculation
A
A
PC
B
B
4
imm generator
Can also do
PC + imm< <１
<<1

## Slide 12: Data path in detail
Imm
generator
<<1

## Slide 13
How does it control in Multicycle Approach
Imm
generator
<<1

## Slide 14: Graphical Specification of FSM
R-type
jump
beq
lw
sw

## Slide 15: The truth table for the datapath control outputs, which depend only on the state inputs.

## Slide 16: The logic equations for the control unit shown in a shorthand form

## Slide 17: Implemented using a block of combinational logic and a register to hold the the current state
Combinational
Control logic
State register
Datapath control output
Next state
Outputs
Inputs

## Slide 18: Contents
Introduction & Logic Design Conventions
Building a datapath
A Simple Implementation Scheme
Pipelining
  Why pipelining
  Pipelined datapath and control
Pipeline Hazards
Exceptions

## Slide 19: 4.6 An Overview of Pipelining
What is Pipelining:
    “A technique designed into some computers to increase speed by starting the execution of one instruction before completing the previous one.”
  ----Modern English-Chinese Dictionary
  implementation technique whereby different instructions are overlapped in execution at the same time.
  implementation technique to make fast CPUs

## Slide 20: Pipeline Analogy
pipelined laundry: overlapping execution
  Parallelism improves performance
Four loads:
  Speedup = 8/3.5 = 2.3
Non-stop:
  Speedup = 2n/(0.5n + 1.5) ≈ 4 = number of stages
Notes: 每个30分钟

## Slide 21: 4.6.1 Why pipelining : overlapped, more faster
Latches, called pipeline registers’ break up computation into 5 stages
Deal 5 tasks at the same time.
Can launch a new computation every 20ns in pipelined structure
Can finish 5×107 computations per second
Only deal one task each time.
This task takes “ such a long time”
Can “launch” a new computation every 100ns in this structure
Can finish 107 computations per second

## Slide 22: Why pipelining : conclusion
The key implementation technique used to Make fast CPU: decrease CPUtime.
Improving of Throughput ( rather than individual execution time)
Improving of efficiency for resources (functional unit)

## Slide 23: What is a pipeline ?
A pipeline is like an auto assemble line
A pipeline has many stages
Each stage carries out a different part of instruction or operation
The stages, which cooperates at a synchronized clock, are connected to form a pipe
An instruction or operation enters through one end and progresses through the stages and exit through the other end
Pipelining is an implementation technique that exploits parallelism among the instructions in a sequential instruction stream

## Slide 24: Pipeline Characteristics -- latency vs. Throughput
Latency
  Each instruction takes a certain time to complete. This is the latency for that operation.
  It's the amount of time between when the instruction is issued and when it completes.
Throughput
  Number of items (cars, instructions) exiting the pipeline per unit time.
  The throughput of the assembly line is the number of products completed per hour.
  The throughput of a CPU pipeline is the number of instructions completed per second.

## Slide 25: Pipeline Characteristics – clock cycle vs. Machine cycle
Clock cycle
  Everything in a CPU moves in lockstep, synchronized by the clock ( The Heartbeat of CPU )
Machine cycle (Processor cycle, Stage time)
  time required to complete a single pipeline stage.
  The pipeline designer’s goal is to balance the length of each pipeline stage.
  In many instances, machine cycle = max ( times for all stages).
  A machine cycle is usually one, sometimes two, clock cycles long, but rarely more.

## Slide 26: RISC-V Pipeline
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access data memory operand
  WB: Write result back to register

## Slide 27: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 28: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 29: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructions pipelined =
  Ideal speedup is Number of pipe stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
Time between instructions nonpipelined
Number of stages

## Slide 30: 4.6.2 Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 17-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
Notes: The abbreviation cf. (short for the Latin: confer/conferatur, both meaning "compare")

## Slide 31: Pipelining RISC-V instruction set
Since there are five separate stages, we can have a pipeline in which one instruction is in each stage.
CPI is decreased to 1, since one instruction will be issued (or finished) each cycle.
During any cycle, one instruction is present in each stage.
Ideally, performance is increased five fold !

## Slide 32: Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards
RISC-V Pipelined Datapath

## Slide 33: Pipeline registers
Need registers (or latch) between stages
  To hold information produced in previous cycle

## Slide 34: What should be latched ?
Is register PC a latch ？
What are stored in latch IF/ID ?
  IR, anything else ?
What are stored in latch ID/EX ?
  A, B, imm, anything else ?
What are stored in latch EX/MEM ?
  ALUoutput, anything else ?
What are stored in latch MEM/WB ?
  LMDR, ALUoutput, Wreg, anythingelse ?

## Slide 35: Why not just make a 50-stage pipeline?
Some computations just won’t divide into any finer (shorter in time) logical implementation.
5 stages OK
50 stages NO. Sorry!

## Slide 36: Why not just make a 50-stage pipeline?
Those latches are NOT free, they take up area, and there is a real delay to go THRU the latch itself.
  Machine cycle > latch latency + clock skew
In modern, deep pipeline (10-20 stages), this is a real effect
Typically see logic “depths” in one pipe stage of 10-20 “gates”.
At these speeds, and with this few levels of logic, latch delay is important

## Slide 37: performance issues in pipelining
Latency: The execution time of each instruction in pipelining does not decrease, instead, always longer than that of unpipelined machine.
Imbalance among stages reduces performance
Overhead rise from register delay and clock skew also contribute to the lower limit of machine cycle.
Pipeline hazards are the major hurdle of pipeline, which prevent the machine from reaching the ideal performance.
Time to “fill” pipeline and time to “drain” it reduces speedup

## Slide 38: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 39: IF for Load, Store, …

## Slide 40: ID for Load, Store, …

## Slide 41: EX for Load

## Slide 42: MEM for Load

## Slide 43: WB for Load
Wrong register number

## Slide 44: Corrected Datapath for rd

## Slide 45: EX for Store

## Slide 46: MEM for Store

## Slide 47: WB for Store

## Slide 48: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 49: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 50: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 51: Pipelined Control (Simplified)

## Slide 52: Review of Control Signals

## Slide 53: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 54: Pipelined Control

## Slide 55: Important Notes:
What should be buffered in every stage register ?
  Data need to be used in the next stages.
  Control signals need to be used in the next stages
  Debug info when used in duration of design
The memory bandwidth changes !
  1 instruction read + 1 data access / 5 cycle (multi-cycle implementation)
  1 instruction read + 1 data access / cycle

## Slide 56: Problems that pipeline introduces
Right-to-left flow leads to hazards

## Slide 57: Hazards
Hazards: Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction
Notes: Hazard 冒险，竞争

## Slide 58: Structure Hazards
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
Notes: Instruction mem和data mem是同一个

## Slide 59: A Single Memory Would Be a Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ld
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory or writeing data to memory
Reading instruction from memory
Fix with separate instr and data memories (I$ and D$)
Notes: 冯诺伊曼体系结构： 指令和数据共存于同一个内存

## Slide 60: The conflict about the registers !
R10
An instruction depends on completion of data access by a previous instruction ( Data hazard )

## Slide 61: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix register file access hazard by doing reads in the second half of the cycle and writes in the first half
add x1,
add x2,x1,
clock edge that controls register writing
clock edge that controls loading of pipeline state registers
Notes: Define register reads to occur in the second half of the cycle and register writes in the first half

## Slide 62: Conflict occurs when PC update
Must increment and store the PC every clock.
What happens when meet a branch ?
  Branches change the value of the PC -- but the condition is not evaluated until ID !
  If the branch is taken, the instructions fetched behind the branch are invalid !
This is clearly a serious problem ( Control hazard ) that needs to be addressed. We will deal it later.

## Slide 63: Hazards can always be resolved by Stall
The simplest way to "fix" hazards is to stall the pipeline.
Stall means suspending the pipeline for some instructions by one or more clock cycles.
The stall delays all instructions issued after the instruction that was stalled, while other instructions in the pipeline go on proceeding.
A pipeline stall is also called a pipeline bubble or simply bubble.
No new instructions are fetched during a stall .

## Slide 64: How to stall ? -- interlock
Stall = control hazard || structural hazard || data hazard
  Control hazard:
    Instruction in EX or MEM is a Branch or JMP
  Data hazard:
    rd of Instruction in EX == rs1 or rs2 of instruction in ID
    rd of Instruction in MEM == rs1 or rs2 of instruction in ID

## Slide 65: How do we stall ? Insert nop by compiler
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble
Bubble

## Slide 66: Insert stall by compiler
Data hazard
  ADD Rx, Ry, Rz
  NOP
  NOP
  AND Rl, Rx, Rw
Control hazard
  Beq/Bne Rx, Ry, Label
  NOP
  …
Pipelining Performance is ate up by inserting NOP by compiler

## Slide 67
Add extra hardware to detect stall situations
  Watches the instruction field bits
  Looks for “read versus write” conflicts in particular pipe stages
  Basically, a bunch of careful “case logic”
Add extra hardware to push bubbles throught pipe
  Actually, relatively easy
  Can just let the instruction you want to stall GO FORWARD through the pipe…
  …but, TURN OFF the bits that allow any results to get written into the machine state
  So, the instruction “executes” (it does the work), but doesn’t “save”
How do we stall ? Add hardware Interlock!

## Slide 68: How to Stall ? Add a stall control logic !
PC IF/ID ID/EX EX/MEM MEM/WB
F.Inst
D.Inst
E.Inst
M.Inst
Stall control logic
rs1
rs2
Wreg
Branch
Bubble
Wreg
Branch
Bubble
rd
rd
stall
To produce a stall signal. If stall ==1 then
Use stall to disable writing PC write and IF/ID latch.
Push a bubble into next stage.
  Bubble = 1 and disable control signal Wreg and Wmem.
  Puch a nop forward into ID/EX

## Slide 69: Control signals
 | Output Signal | Meaning When 1 | Meaning When 0
1 | Cu_branch | Branch Instr. | Non-Branch Instr.
2 | Cu_wmem | Write Mem. | Not Write Mem.
3 | Cu_Mem2Reg | From Mem. To Reg | From ALUOut To Reg
4 | Cu_sext | Sign-extend the imm. | No sign extended the imm.
5 | Cu_aluc | ALU Operation | 
6 | Cu_aluimm | Imm. | Register data2
7 | Cu_wreg | Write Reg. | Not Write Reg.

## Slide 70: Something about control signals
How to know the instruction in EXE/MEM is a Branch?
  EXE.branch ==1 or Mem.branch == 1
How to know the instruction in EXE/MEM is a ALU or LW instruction ( has a destination reg.) ?
  EXE.Wreg ==1 or Mem.Wreg == 1
How to know the instruction in EXE/MEM is a LW ?
  EXE.Wreg==1 and Mem2Reg == 1
Which instruction has no rd?
  Sw, Branch
Which instruction has no rs ?
  JAL, LUI
Which instruction has rs2 as source register?
  ALU r-r, Branch, SW

## Slide 71: How to stall ?
If stall == 0 //stop the latter ones
  then PC  new PC; IF/ID.IR  IF.IR
  IF/ID.NPC  PC + 4
If stall == 1 // push bubble forward
  then ID/EX.nop 1 else ID/EX.nop 0
When initial
  ID/EX.nop 0, EX/MEM.nop  0, Mem.WB.nop 0
Are the stalls the same for
Data hazard / control hazard ?

## Slide 72: Performance of pipeline with stalls
Pipeline stalls decrease performance from the ideal
Recall the speedup formula:

## Slide 73: Assumptions for calculation
The ideal CPI on a pipelined processor is almost always 1. (may less than or greater than )
So
Ignore the overhead of pipelining clock cycle.
Pipe stages are ideal balanced.

## Slide 74: Case of single-cycle implementation
CPI unpipelined = 1
Clock cycle pipelined =
Clock cycle unpipelined
pipeline depth

## Slide 75: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
  Stalls reduce performance
    but are required to get correct results
  Compiler can arrange code to avoid hazards and stalls
    requires knowledge of the pipeline structure
Instruction set design affects complexity of pipeline implementation
The BIG Picture

## Slide 76: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction
Notes: Hazard 冒险，竞争

## Slide 77: Structural hazard: Pipe Stage Contention
Structural hazards
  Occurs when two or more instructions want to use the same hardware resource in the same cycle
  Causes bubble (stall) in pipelined machines
  Overcome by replicating hardware resources
    Multiple accesses to memory
    Multiple accesses to the register file
    Not fully pipelined functional units

## Slide 78: Multi access to a Single Memory
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
ld
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory
Reading instruction from memory
Fix with separate instr and data memories
Notes: 冯诺伊曼体系结构： 指令和数据共存于同一个内存

## Slide 79: Multi access to the register file
Simply insert a stall , speedup will be decreased.

## Slide 80: double bump(双重触发) works
allow WRITE-then-READ in one clock cycle (double bump)
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix register file access hazard by doing reads in the second half of the cycle and writes in the first half
add x1,
add x2,x1,
clock edge that controls register writing
clock edge that controls loading of pipeline state registers

## Slide 81: Not fully pipelined function unit : may cause structural hazard

## Slide 82: Machine without structural hazards will always have a lower CPI
Example
  Data reference constitute 40% of the mix
  Ideal CPI ignoring the structural hazard is 1
  The processor with the structural hazard has a clock rate that is 1.05 times higher than that of a processor without structural hazard.
Answer
  Average instruction time = CPIClock cycle time
  =(1+0.4 1) CCideal/1.05
  = 1.3  Ccideal
  Clearly, the processor without the structural hazard is faster.

## Slide 83: Why allow machine with structural hazard ?
To reduce cost .
  i.e. adding split caches, requires twice the memory bandwidth.
  also fully pipelined floating point units costs lots of gates.
  It is not worth the cost if the hazard does not occur very often.
To reduce latency of the unit.
  Making functional units pipelined adds delay
  (pipeline overhead -> registers.)
  An unpipelined version may require fewer clocks per operation.
  Reducing latency has other performance benefits, as we will see.

## Slide 84: Example: impact of structural hazard to performance
Example
  Many machines have unpipelined float-point multiplier.
  The function unit time of FP multiplier is 6 clock cycles
  FP multiply has a frequency of 14% in a SPECfp benchmark
  Will the structural hzard have a large performance impact on the SPECfp benchmark?

## Slide 85: Answer to the example
In the best case: FP multiplies are distributed uniformly.
  There is one multiply in every 7 clock. 1/14%
  Then there will be no structural hazard,then there is no performance penalty at all.
In the worst case: the multiplies are all clustered with no intervening instructions.
  Then every multiply instruction have to stall 5 clock cycles to wait for the multiplier be released.
  The CPI will increase 70% to 1.7, if the ideal CPI is 1.
Experiment result:
  This structural hazard increase execution time by less than 3%.

## Slide 86: Summary: solutions for structural hazard
Multiple accesses to memory
  Split instruction and data memory / multiple memory port / instruction buffer
  Memory bandwidth need to be imporved by 5 folds.
Multiple accesses to the register file
  Double bump
Not fully pipelined functional units
  Fully pipeline the functional unit
  Using multiple functional unites
Real machine often with structural hazards.

## Slide 87: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction
Notes: Hazard 冒险，竞争

## Slide 88: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add x19, x0, x1 sub x2, x19, x3

## Slide 89: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 90: Data Hazards: Forwarding vs. Stalling ALU Instructions
Consider this sequence:
  sub x2, x1,x3 and x12,x2,x5 or x13,x6,x2 add x14,x2,x2 sd x15,100(x2)
We can resolve hazards with forwarding
  How do we detect when to forward?

## Slide 91: Dependencies & Forwarding

## Slide 92: Hardware Change for Forwarding
MEM/WR
ID/EX
EX/MEM
Data
Memory
ALU
mux
mux
Registers
NextPC
Immediate
mux
Source  sink
EX/Mem.ALUoutput  ALU input
MEM/WB.ALUoutput  ALU input
MEM/WB.LMD  ALU input
When to use the red. Blue
purple forwording path ?

## Slide 93: When to use the forwarding path ?
EX/Mem.ALUoutput  ALU input
    The previous instruction in EX/MEM is ALU
    The instruction in ID/EX has Rs1 or Rs2 source register
    EX/MEM.Rd == ID/EX.Rs1 or EX/MEM.Rd ==ID/EX.Rs2
MEM/WB.ALUoutput  ALU input
    The previous instruction in MEM/WB is ALU
    The instruction in ID/EX has Rs1 or Rs2 source register
    MEM/WB.Rd == ID/EX.Rs1 or MEM/WB.Rd == IF/ID.Rs2
MEM/WB.LMD  ALU input
    The previous instruction in MEM/WB is Load
    The instruction in ID/EX has Rs1 or Rs2 source register
    MEM/WB.Rd == ID/EX.Rs1 or MEM/WB.Rd == ID/EX.Rs2

## Slide 94: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1 = register number for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRs2
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 95: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0
Notes: （1）必须是写的冲突， 否则的话，还有情形是？ branch
（2）？？ 默认无法读写的

## Slide 96: Forwarding Paths

## Slide 97: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 98: Double Data Hazard
Consider the sequence:
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 99: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs1)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs2)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 100: Datapath with Forwarding

## Slide 101: Load-Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 102: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
ld x1, 0(x31)
ld x2, 8(x31)
add x3, x1, x2
sd x3, 24(x31)
ld x4, 16(x31)
add x5, x1, x4
sd x5, 32(x31)
stall
stall
ld x1, 0(x31)
ld x2, 8(x31)
ld x4, 16(x31)
add x3, x1, x2
sd x3, 24(x31)
add x5, x1, x4
sd x5, 32(x31)
7 cycles
9 cycles
Notes: B的值放到 x1中
E的值放到 x2中
x3中放 A
F的值放到 x4中
x5中放 A
主要是前面的load-use data hazard

## Slide 103: Detect when should use Load Stall
situation | Example code sequence | Action
No dependence | LD R1, 45(R2) DADD R5,R6,R7 DSUB R8,R6,R7 OR R9,R6,R7 | No hazard possible because of no dependence
Dependence requiring stall | LD R1, 45(R2) DADD R5,R1,R7 DSUB R8,R6,R7 OR R9,R6,R7 | Comparators detect the use of R1 in the DADD and stall the DADD (and DSUB and OR ) before the DADD begins EX
Dependence overcome by forwarding | LD R1, 45(R2) DADD R5,R6,R7 DSUB R8,R1,R7 OR R9,R6,R7 | Comparators detect the use of R1 in DSUB and forward result of load to ALU in time for DSUB to begin EX
Dependence with accesses in order | LD R1, 45(R2) DADD R5,R6,R7 DSUB R8,R6,R7 OR R9,R1,R7 | No action required because read of R1 by OR occurs in the second half of the ID phase, while the write of the loaded data occurred in the first half.

## Slide 104: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs1, IF/ID.RegisterRs2
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRs1) or (ID/EX.RegisterRd = IF/ID.RegisterRs2))
If detected, stall and insert bubble

## Slide 105: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently forward to EX stage

## Slide 106: Datapath with Hazard Detection

## Slide 107: Example of Forwarding and Load Stall
Why forwarding?
  ADD R4, R5, R2
  LW R15, 0(R4)
  SW R15, 4(R2)
Why load delay?
  ADD R4, R5, R2
  LW R15, 0(R4)
  SW R15, 4(R2)

## Slide 108: Solution (without forwarding)

## Slide 109: Solution (with forwarding)
EX/MEM.ALUoutput  ALU input port
MEM/WB.LDMR DM data write port

## Slide 110: performance influence of load stall
Example
  Assume 30% of the instructions are loads.
  Half the time, instruction following a load instruction depends on the result of the load.
  If hazard causes a single cycle delay, how much faster is the ideal pipeline ?
Answer
  CPI = 1+30%50% 1=1.15
  The performance decrease about 15% due to load stall.

## Slide 111: Fraction of load that cause a stall

## Slide 112: Summary of Data Hazards
Instruction depends on result of prior computation which is not ready yet
  Not computed
  Not stored
Solutions
  Double bump
  Forwarding
  Compiler scheduling
  Stall

## Slide 113: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazards
    A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction
Notes: Hazard 冒险，竞争

## Slide 114: Example: Branches
R3, 24

## Slide 115: Recall: Basic Pipelined Datapath

## Slide 116: Control hazard

## Slide 117: Dealing with the control hazard
Four simple solutions
  Stall
  Prediction
    Predict-untaken: treat every branch as not taken
    Predict-taken: treat every branch as taken
Note:
  Fixed hardware
  Compile time scheme using knowledge of hardware scheme and of branch behavior

## Slide 118: Recall: solve the hazard by inserting stalls
24
48 or 72

## Slide 119: Flushing the pipeline
Simplest hardware:
  Holding or deleting any instruction after branch until the branch destination is know.
  Penalty is fixed.
  Can not be reduced by software.

## Slide 120: Stalls greatly hurt the performance
Problem:
  With a 30% branch frequency and an ideal CPI of 1, how much the performace is by inserting stalls ?
Answer:
  CPI = 1+30%３＝1.9
  this simple solution achieves only about half of the ideal performance.

## Slide 121: Always Stall Hurts the Not- taken case
24

## Slide 122: How about assume Branch Not Taken

## Slide 123: How to do with the branch taken ?
24

## Slide 124: Predict –not-taken
Hardware:
  Treat every branch as not taken (or as the formal instruction)
    When branch is not taken, the fetched instruction just continues to flow on. No stall at all.
    If the branch is taken, then restart the fetch at the branch target, which cause 3 stall.(should turn the fetched instruction into a no-op)
    Perf = 1+ br% * take%* 3
Compiler:
  Can improve the performance by coding the most frequent case in the untaken path.

## Slide 125: Which code segment is better ?
If cond=(malloc(..))
  Then statements_taken
  Else statements_not_taken
If not cond
  Then statements_not_taken
  Else statements_taken

## Slide 126: Alternative is assuming the branch always taken
Most branches(60%) are taken, so we should make the taken branch more faster. Why not try assuming the branch always taken?

## Slide 127: Predict –taken
Hardware
  Treat every branch as taken (evidence: more than 60% braches are taken)
  As soon as the branch target address is computed, assume the branch to be taken and begin fetching and executing at the target.
  Only useful when the target is known before the branch outcome.
  No advantage at all for RISC-V 5-stage pipeline.
Compiler
  Can improve the performance by coding the most frequent case in the taken path.

## Slide 128: Pipeline status for predict-taken
Branch is taken: 1 stall perf=1+Br%*( taken%*1+untaken%*3)
44 BEQ R1, 24 | IF | ID | EX | MEM | WB |  | 
48 AND R12, R2, R5 |  | IF | idle | idle | idle | idle | 
72 LW R4, 50(R7) |  |  | IF | ID | EX | MEM | WB
76 |  |  |  | IF | ID | EX | MEM
80 |  |  |  |  | IF | ID | EX
Branch is not taken: 3 stall
44 BEQ R1, 24 | IF | ID | EX | MEM | WB |  | 
48 AND R12, R2, R5 |  | IF | idle | idle | idle | idle | 
72 LW R4, 50(R7) |  |  | IF | ID | idle | idle | idle
76 |  |  |  | IF | idle | idle | idle
48 AND R12, R2, R5 |  |  |  |  | IF | ID | EX

## Slide 129: Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
In RISC-V pipeline
  Need to compare registers and compute target early in the pipeline
  Add hardware to do it in ID stage

## Slide 130: Control Hazards – Branch Instruction
If branch outcome determined in MEM
PC
Flush these instructions
(Set control values to 0)

## Slide 131: Move the Branch Computation Forward

## Slide 132: Move the Branch Computation more Forward
store
load

## Slide 133: Result: New & Improved MIPS Datapath
Need just 1 extra cycle after the BEQ branch to know right address
48 or 72

## Slide 134: Flushing : need only to insert 1 stall to resolve control hazard
48 or 72
40 ADD R30,R30,R30 | IF | ID | EX | MEM | WB |  | 
44 BEQ R1, 24 |  | IF | ID | EX | MEM | WB | 
48 AND R12, R2, R5 |  |  | IF | idle | idle | idle | idle
48 or 72 |  |  |  | IF | ID | EX | MEM

## Slide 135: Why “waste” the fetched instruction ?
We have fetched the instruction 48, why we fetch the second time if the branch not taken at last ?
48 or 72

## Slide 136: RISC-V with Predict Not Taken
Prediction correct
Prediction incorrect

## Slide 137: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: sub x10, x4, x8 40: beq x1, x3, 16 //PC-relative branch to 40+16*2=72 44: and x12, x2, x5 48: or x13, x2, x6 52: add x14, x4, x2 56: sub x15, x6, x7 ... 72: ld x4, 50(x7)

## Slide 138: Example: Branch Taken

## Slide 139: Example: Branch Taken

## Slide 140: Data Hazards for Branches
If a comparison register is a destination of 2nd or 3rd preceding ALU instruction
…
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
add x4, x5, x6
add x1, x2, x3
beq x1, x4, target
Can resolve using forwarding

## Slide 141: Data Hazards for Branches
If a comparison register is a destination of preceding ALU instruction or 2nd preceding load instruction
  Need 1 stall cycle
beq stalled
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
ID
EX
MEM
WB
add x4, x5, x6
ld x1, addr
beq x1, x4, target

## Slide 142: Data Hazards for Branches
If a comparison register is a destination of immediately preceding load instruction
  Need 2 stall cycles
beq stalled
IF
ID
EX
MEM
WB
IF
ID
ID
ID
EX
MEM
WB
beq stalled
ld x1, addr
beq x1, x0, target

## Slide 143: More-Realistic Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 144: Accuracy of prediction based on profile

## Slide 145: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 146: 1-bit predictor
Branch History Table: Lower bits of PC address index table of 1-bit values
  Says whether or not branch taken last time
  No address check (saves HW, but may not be right branch)
0/1
Low bits of PC
预测行为
0：not taken
1：taken
Complement when mispredict

## Slide 147: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 148: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 149: An alternative 2-bit predictor
It can be implemented using a 2-bit counter
T
T
NT
Predict Taken
Surely
Predict Not
Taken
Predict Taken
Predict Not
Taken surely
T
NT
T
NT
NT

## Slide 150: Accuracy of the 2-bit predictor
4096 entries, 2-bit predictor
SPEC89
Accuracy : 99%~82%
Misprediction: 1%~18%

## Slide 151: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 152: Summary for control hazard
    branch condition and the branch PC are not available in time to fetch an instruction on the next clock
      OK, we did these, calculate the destination address and condition asap, Flushing the pipeline, predict-not-taken, predict-taken, delayed branc
Control hazards can cause a greater performance loss than do data hazards.
In general, the deeper the pipeline, the worse the branch penalty in clock cycles.
A higher CPI processor can afford to have more expensive branches.
The efficiency of the three schemes greatly depends on the branch prediction.

## Slide 153: 4.9 Exceptions
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 154: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V : Cause register (SCAUSE)
  We’ll assume 1-bit
    0 for undefined instruction, 1 for system error
Jump to handler at 0000 0000 1C09 0000

## Slide 155: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Example:
  Undefined instruction: 00 0100 0000
  System error: 01 1000 0000
  …: 11 1000 0000
Jump to real handler by the cause of the exception

## Slide 156: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use SEPC to return to program
Otherwise
  Terminate program
  Report error using SEPC, cause, …

## Slide 157: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add x1, x2, x1
  Prevent x1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and SEPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware
Notes: Clobber 重复打击，重复出错

## Slide 158: Pipeline with Exceptions

## Slide 159: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in SEPC register
SCAUSE register records the highest priority exception

## Slide 160: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!
Notes: Precise exceptions 课本321页

## Slide 161: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 162: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice

## Slide 163: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 164: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated
Notes: Speculation 是和乱序执行 直接相关的
静态时候也可以做 speculation

## Slide 165: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 166: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 167: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 168: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 169: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 170: RISC-V with Static Dual Issue

## Slide 171: Hazards in the Dual-Issue RISC-V
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add x5, x0, x1 load x2, 0(x5)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 172: Scheduling Example
Schedule this for dual-issue RISC-V
Loop: ld x31, 0(x20) // x31=array element add x31, x31, x21 // add scalar in x21 sd x31, 8(x20) // store result addi x20, x20,–8 // decrement pointer blt x22, x20, Loop // branch if x20 > x22
 | ALU/branch | Load/store | cycle
Loop: | nop | ld x31, 0(x20) | 1
 | addi x20, x20, –8 | nop | 2
 | Add x31, x31, x21 | nop | 3
 | blt x22, x20, Loop | sd x31, 8(x20) | 4
  IPC = 5/4 = 1.25 (c.f. peak IPC = 2)

## Slide 173: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name
Notes: Loop unfolding
寄存器重命名技术在乱序执行流水线中有两个作用。一是消除指令之间的寄存器读后写相关（WAR），和写后写相关（WAW）；二是当指令执行发生例外或转移指令猜测错误而取消后面的指令时可以保证现场的精确。寄存器重命名的思路很简单：就是当一条指令写一个结果寄存器时不直接写到这个结果寄存器，而是先写到一个中间寄存器过渡一下，当这条指令提交的时候再写到结果寄存器中。
Anti Dependence[edit]
An anti dependence occurs when a location in memory is read before that same location is written to.[1][2][3] This introduces write-after-read (WAR) hazards because the instruction that writes the data into a memory location has to wait until that memory location has been read by the previous instruction or else the reading instruction would read the wrong value.[2] An example of an anti dependence is:

## Slide 174: Loop Unrolling Example
IPC = 14/8 = 1.75
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | addi x20, x20,–32 | ld x28, 0(x20) | 1
 | nop | ld x29, 24(x20) | 2
 | add x28, x28, x21 | ld x30, 16(x20) | 3
 | add x29, x29, x21 | ld x31, 8(x20) | 4
 | add x30, x30, x21 | sd x28, 32(x20) | 5
 | add x31, x31, x21 | sd x29, 24(x20) | 6
 | nop | sd x30, 16(x20) | 7
 | blt x22, x20, Loop | sd x31, 8(x20) | 8

## Slide 175: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU
Notes: Superscalar 超标量处理器

## Slide 176: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  ld x31, 0(x21) add x1, x31, x2 sub x23, x23, x3 andi x5, x23, 20
  Can start sub while add is waiting for ld

## Slide 177: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 178: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required

## Slide 179: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared

## Slide 180: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 181: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 182: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 183: ARM处理器体系结构
ARM内核工作模式：
  用户模式（user）：正常程序执行模式；
  快速中断模式（FIQ）：高优先级的中断产生会进入该种模式，用于高速通道传输；
  外部中断模式（IRQ）：低优先级中断产生会进入该模式，用于普通的中断处理；
  特权模式（Supervisor）：复位和软中断指令会进入该模式；
  数据访问中止模式（Abort）：当存储异常时会进入该模式；
  未定义指令中止模式（Undefined）：执行未定义指令会进入该模式；
  系统模式（System）：用于运行特权级操作系统任务；
  监控模式（Monitor）：可以在安全模式和非安全模式之间切换；

## Slide 184: ARM处理器体系结构
ARM体系结构的指令集（Instruction Set）：
  ARM指令集
  Thumb指令集
  Thumb-2指令集

## Slide 185: ARM处理器体系结构
ARM的微体系结构（Micro-architecture）：
  ARM处理器内核（Processor Core）
  ARM处理器（Processor）
  基于ARM架构处理器的片上系统（SoC）

## Slide 186: ARM公司授权体系
ARM目前在全球拥有大约1000个授权合作商、320家伙伴，但是购买架构授权的厂家不超过20家，中国有华为、飞腾获得了架构授权。
只能按照ARM设计好的处理器类型、在指定的代工厂进行生产。
处理器优化包/物理IP包授权（POP）
处理器授权
架构/指令集授权
提供RTL代码，处理器的核数、缓存可以自己配置。自主设计主频、工艺、代工厂等。
按照所授权的架构和指令集（如ARMv8）自行编写代码、设计芯片。
Notes: 寄存器传输级（Register-Transfer Level, RTL）是通过硬件描述语言来描述实际电路的一种高层次模型。
处理器优化包 (Processor Optimization Pack, POP)。

## Slide 187: ARM处理器体系结构
ARM流水线的执行顺序：
  取指令（Fetch）：从存储器读取指令；
  译码（Decode）：译码以鉴别它是属于哪一条指令；
  执行（Execute）：将操作数进行组合以得到结果或存储器地址；
  缓冲/数据（Buffer/data）：如果需要，则访问存储器以存储数据；
  回写：（Write-back）：将结果写回到寄存器组中；

## Slide 188: 基于ARMv8的鲲鹏流水线技术
Branch预测和取指流水线解耦设计，取指流水线每拍最多可提供32Bytes指令供译码，分支预测流水线可以不受取指流水停顿影响，超前进行预测处理；
定浮点流水线分开设计，解除定浮点相互反压，每拍可为后端执行部件提供4条整型微指令及3条浮点微指令；
整型运算单元支持每拍4条ALU运算（含2条跳转）及1条乘除运算；
浮点及SIMD运算单元支持每拍2条ARM Neon 128bits 浮点及SIMD运算；
访存单元支持每拍2条读或写访存操作，读操作最快4拍完成，每拍访存带宽为2x128bits读及1x128bits写；

## Slide 189: ARM处理器体系结构
ARM处理器的分类：
  ARM经典处理器（Classic Processors）；
  ARM Cortex应用处理器；
    面向复杂操作系统和用户应用的Cortex-A（Applications，应用）系列
    针对实时处理和控制应用的Cortex-R（Real-time，实时）系列
    针对微控制器与低功耗应用优化的Cortex-M（Microcontroller）系列
  ARM Cortex嵌入式处理器；
  ARM专业处理器

## Slide 190: ARM 处理器系列命名规则
命名格式：ARM {x} {y} {z} {T} {D} {M} {I}
  x：处理器系列，是共享相同硬件特性的一组处理器，如：ARM7TDMI、ARM740T 都属于 ARM7 系列
  y：存储管理 / 保护单元
  z：Cache
  T：Thumb，Thumb16 位译码器
  D：Debug，JTAG 调试器
  M：Multipler，快速乘法器
  I：Embedded ICE Logic，嵌入式跟踪宏单元

## Slide 191: ARM架构发展史 (1)

## Slide 192: ARM架构发展史 (2)

## Slide 193: ARM架构发展史 (3)
从ARM v7开始，CPU命名为Cortex，并划分为A、R、M三大系列，分别为不同的市场提供服务；
  A (Application)系列：应用型处理器，面向具有复杂软件操作系统的面向用户的应用，为手机、平板、AP等终端设备提供全方位的解决方案；
  R (Real-Time)系列：实时高性能处理器，为要求可靠性、高可用性、容错功能、可维护性和实时响应的嵌入式系统提供高性能计算解决方案；
  M (Microcontroller)系列：高能效、易于使用的处理器，主要用于通用低端，工业，消费电子领域微控制器。

## Slide 194: ARM架构发展史 (4)

## Slide 195: ARM服务器处理器的优势
低功耗一直以来都是ARM架构芯片最大的优势；
ARM架构的芯片在成本、集成度方面也有较大的优势；
端、边、云全场景同构互联与协同；
更高的并发处理效率；
多元化的市场供应

## Slide 196: 4.15 Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.15 Concluding emarks

## Slide 197: END