## Slide 1: Chapter 1
Computer Abstractions
and Technology

## Slide 2: Topics
1.1 Introduction
1.2 Eight Great Ideas in Computer Architecture
1.3 Below Your Program
1.4 Under the covers
1.5 Technologies for building Processors and Memory
1.6 Performance
1.7 The Three Walls
1.8 Switch from Uniprocessors to Multiprocessors
1.9 Benchmarking the intel Core i7
1.10 fallacies and Pitfalls

## Slide 3: 1.1 Introduction

## Slide 4: Computers are pervasive
Computers have led to a 3rd revolution for civilization

## Slide 5: 基于微处理器的HPC的典型应用场景
气象科学
卫星测绘
能源勘探
航空航天
基础科学研究
生命科学
汽车电子
分子动力学
Notes: 高性能计算是跨行业跨应用领域的计算学科，通常将最前沿的计算机技术用于最复杂、尖端的科学计算和求解，驱动着各行各业的技术进步。高性能计算广泛应用于超算中心、大学高校、科研机构、制造工程、地球物理、气象环境预测、油气勘探、生物分析、生命科学、天体物理、动漫渲染、能源及材料等各行业各领域。
高性能计算机在密集计算、海量数据处理等领域不可或缺，对于保障国防安全、促进科学研究及产业发展具有直接推动作用。在国防安全方面，核武器设计、核爆炸模拟、空气动力学、反导弹武器系统、空间技术的开发等需要在高性能计算机上进行模拟；在科学研究方面，长期气候预测、高精度天气预报、海洋环流计算、空气与水污染的模拟分析、洪水与地震等灾害的预报等都需要进行海量数据处理和大规模计算；在产业发展方面，发动机设计、模具设计、生物新药设计、风洞试验仿真、石油地质勘探以及新材料研究等都离不开高端计算。

## Slide 6: Class of Computers
Different design requirements
Employ the core hardware technologies in different ways
The basic principles are the same !
Classes | PC/Desktop | Server | Embedded | SuperComputers
Features | General purpose, variety of software Subject to cost/performance tradeoff | Network based High capacity, performance, reliability Range from small servers to building sized | Hidden as components of systems Stringent power/performance/cost constraints | High-end scientific and engineering calculations Highest capability but represent a small fraction of the overall computer market

## Slide 7: The PostPC Era
Personal Mobile Device (PMD)
  Battery operated
  Connects to the Internet
  Hundreds of dollars
  Smart phones, tablets, electronic glasses
Cloud computing
  Warehouse Scale Computers (WSC)
  Software as a Service (SaaS)
  Portion of software run on a PMD and a portion run in the Cloud
  Amazon and Google

## Slide 8: Computer Generations
Pre-computer – ~ 1946
  Non-electrical, non-programmable (非电子，不可编程)
First Generation – 1946 ~ 1956
  Vacuum tubes, programmable (电子管，可编程，图灵完全)
Second Generation – 1956 ~ 1964
  Transistor, programming languages (晶体管，编程语言开始应用)
Third Generation – 1964 ~ 1971
  Integrated Circuit, OS (集成电路，操作系统开始应用)
Fourth Generation – 1971 ~ now
  Microprocessor, GUI, Personal Computer (大规模集成微处理器, 图形用户界面, 个人电脑兴起)
Fifth Generation – future
  Still in development … …

## Slide 9: Pre-computers：计数的辅助工作
Digit: Latin for fingers
Tally sticks
Asian abacus
Roman abacus
Notes: 经考古研究表明：人类的计算是从计数开始．最早的计数工具从自身的双手开始到学会用小树枝、小木棍、小石子等工具进行计数。到了我国的唐代，人们发明了算盘，同时发明了一整套基于算盘的引算口诀，算盘应该是出现最早的较为成熟的计算工具，所以也有观点认为算盘可以看作是最早的计算机，而珠算口诀则是最早的算法。

## Slide 10: Pre-computer
Cash Register
Babbage difference engine ( http://libai.math.ncu.edu.tw/bcc16/pool/3.01.shtml )
Card sorter
Enigma Cipher machine

## Slide 11: The First Mechanical Calculating Machine
The 17th century: the beginning of mechanical calculators
17世纪：机械式计数器开始出现
Pascaline (Pascal’s calculator)
Invented by Blaise Pascal in 1642-1645 (19-22岁！)
Addition and Subtraction: Two basic operations
两个基本操作：加与减
Multiplication and division: through repeated addition or subtraction
乘与除这两个操作通过重复地加或减间接实现
Blaise Pascal (1623-1662)
Pascaline (1645)
Pascal编程语言取名就是为了纪念Blaise Pascal
Notes: 17世纪法国科学家布莱斯•帕斯卡(B．Pascal)发明基于齿轮传动技术的机械式计算机。它的特点是利用人工手动作为计算机动力，利用齿轮、杠杆等机械装置来自动传送十进制数进行计算。随后的机电式计算机就是在机械式计算机的基础上用电力作动力，但计算原理仍然是机械式的。

## Slide 12: Turing Machine (1936)
Alan Turing described a theoretical device called the Turing machine, formalized the concepts of computation and algorithms in 1936
A.M. Turing (1936), On Computable Number
A.M.Turing (1912-1954)
Turing machine as a mechanical device
Notes: 阿兰·麦席森·图灵 Alan Mathison Turing ,是英国著名的数学家和逻辑学家,被称为计算机科学之父、人工智能之父,是计算机逻辑的奠基者,提出了“图灵机”和“图灵测试”等重要概念.人们为纪念其在计算机领域的卓越贡献而设立“图灵奖”.
1936年5月，图灵向伦敦权威的数学杂志投了一篇论文，题为《论数字计算在决断难题中的应用》。该文于1937年在《伦敦数学会文集》第42期上发表后，立即引起广泛的注意。在论文的附录里他描述了一种可以辅助数学研究的机器，后来被人称为“图灵机”，这个设想最有变革意义的地方在于，它第一次在纯数学的符号逻辑，和实体世界之间建立了联系，后来我们所熟知的电脑，以及还没有实现的“人工智能”，都基于这个设想。这是他人生第一篇重要论文，也是他的成名之作

## Slide 13: Electromechanical Calculators
Early 20th century technology
Special-purpose system
  Motor-driven mechanical calculators
  Cache registers
  Enigma cipher machine
Programmable systems
  Punched-card sorters
    Punched cards
  Machines using relays to construct logic gates
    Konrad Zuse’s Z3
    Howard Aiken’s Mark-I(Harvard)

## Slide 14: First electronic digital computing device
First electronic digit computing device 第一台纯电子的数字计算设备
Invented by Professor John Atanasoff and graduate student Clifford Berry at Iowa State College between 1939 and 1942
Special purpose. neither programmable, nor Turing-complete
非常接近现代计算机，但不可编程、非图灵完全
Atanasoff-Berry Computer(ABC) 1942
对现代计算机发展的重要贡献
  使用二进制数表示
  用纯电子实现算术与逻辑运算
  计算和存储分离
John Atanasoff (1903-1995)
Clifford Berry (1918-1963)
Atanasoff-Berry Computer (1942)
Add-subtract module
加减运算模块
Notes: 阿塔纳索夫-贝瑞计算机（Atanasoff-Berry Computer，简称ABC）是法定的世界上第一台电子计算机，是爱荷华州立大学的约翰·文森特·阿塔纳索夫（John Vincent Atanasoff）和他的研究生克利福特·贝瑞（Clifford Berry）在1937年设计，不可编程，仅仅设计用于求解线性方程组，并在1942年成功进行了测试。而“埃尼阿克（ENIAC）”标志着计算机正式进入数字的时代。；
使用二进制数表示所有的数值和数据
使用电子器件进行所有计算操作，而不是滚轮、棘轮或者机械开关
计算和存储在系统中分离成两部分

## Slide 15: MarkI (Harvard) – IBM(ASCC) --1944 Automatic Sequence Controlled Calculator
“the beginning of the era of the modern computer” and "the real dawn of the computer age”.

## Slide 16: MarkI (Harvard) -- ASCC (IBM)
765,000 components and 500 miles (800 km) of wire with three million connections
volume of 51 feet (16 m) in length, eight feet (2.4 m) in height, and two feet (~61 cm) deep.
weight of about 10,000 pounds (4500 kg).
The basic calculating units had to be synchronized mechanically, so they were run by a 50-foot (~15.5 m) shaft driven by a five-horsepower (4 kW) electric motor
the industry's largest electromechanical calculator
Howard Hathaway Aiken

## Slide 17: Electronic Computers --1st Generation （1946-1956）
Dominant technologies:
  Processors: Vacuum tubles
  Memory: Acoustic delay line, magnetic drum
Special-purpose system
  John Atanasoff’s experimental machine
  Colossus , ( decrypt the German Enigma cipher)
  Hoffman’s computer (decrypt the Japanese Enigma cipher)
Programmable systems
  ENIAC I-IV
Store-program systems
    Experimental projects: EDVAC,
    Commercial products: UNIVAC I, IBM701, 704(fp hardware)

## Slide 18: First general-purpose electronic digital computer
First general-purpose electronic computer 第一台通用电子计算机
Designed by John Mauchly and J. Presper Eckert of the University of Pennsylvania
General-purpose instruction set, decimal, programmable & Turing-complete
通用指令集、十进制、可编程、图灵完全
But NOT stored program 没有程序存储能力
ENIAC (Electronic Numerical Integrator and Computer) in 1946
ENIAC很多方面借鉴了1942年ABC计算机的设计
Decimal (not binary)
20 accumulators of 10 digits
Programmed manually by switches
18,000 vacuum tubes
30 tons
15,000 square feet
140 kW power consumption
5,000 additions per second
Notes: 1946年2月14日，世界上第一台电脑“埃尼阿克”ENIAC在美国宾夕法尼亚大学诞生。 第二次世界大战期间，美国军方要求宾州大学莫奇利（Mauchly）博士和他的学生埃克特（Eckert） 设计以真空管取代继电器的“电子化”电脑--ENIAC“埃尼阿克”（Electronic Numerical Integrator and Calculator）， 电子数字积分计算机）， 目的是用来计算炮弹弹道。
“埃尼阿克”长30.48米，宽1米，占地面积170平方米，30个操作台，约相当于10件普通房间的大小，重达30吨，耗电量150千瓦，造价48万美元。它使用18000个电子管，70000个电阻，10000个电容，1500个继电器，6000多个开关，每秒执行5000次加法或400次乘法，是继电器计算机的1000倍、手工计算的20万倍。

## Slide 19: Von Neumann architecture (1945)
Stored Program concept
Main memory storing programs and data
ALU operating on binary data
Control unit interpreting instructions from memory and executing
Input and output equipment operated by control unit
Computation and memory are separated
计算与存储分离
Memory that stores data and instructions
数据与指令保存在同一个存储器
“First Draft of a Report on the EDVAC”
冯诺依曼提出体系结构的著名报告1945
John von Neumann (1903-1957)
Notes: 约翰·冯·诺依曼（ John von Neumann,1903－1957）,“现代电子计算机之父”,美籍匈牙利人,物理学家、数学家、发明家,“现代电子计算机之父”即电脑（即EDVAC,它是世界上第一台现代意义的通用计算机）的发明者.

## Slide 20: The first computer with stored-program
Inspired by John von Neumann's seminal "first draft of a report on the EDVAC"
Constructed by Maurice Wilkes at the University of Cambridge Mathematical Lab.
Binary, stored-program (used a mercury delay line memory) 二进制、存储程序
EDSAC：Electronic delay storage automatic calculator (1949)
Maurice Wilkes (1913-2010)
mercury delay line memory
Turing Award 1967

## Slide 21: 1st Commercial Computers
1947 - Eckert-Mauchly Computer Corporation
UNIVAC I (Universal Automatic Computer)
US Bureau of Census 1950 calculations
Became part of Sperry-Rand Corporation
Late 1950s - UNIVAC II
  Faster
  More memory

## Slide 22: IBM
Punched-card processing equipment
1952.4 - the 701
  IBM’s first stored program computer
  Scientific calculations
  First mass-produced mainframe
1955 - the 702
  Business applications
Lead to 700/7000 series

## Slide 23: Electronic Computers -- 2nd Generation (1956-1964)
Dominant technologies
  Processors: Discrete transistors
  Smaller, faster, less power, more reliable
  Memory: Magnetic cores
  Programming: binary machine language
  symbolic languages
  I/O: Punched cards for input/output.
Examples:
  UNIVAC III, RCA 501, Philco TransactS-2000,
  NCR 300 series, IBM7030 Stretch
General-purpose computers
  IBM System/360
  Minicomputers: Digital Equipment PDP-8
Supercomputers
  Control Data 6600
    Innovations: Load-store architecture, pipeline

## Slide 24: IBM 1401 (1959)
announced by IBM on October 5, 1959.
a variable-wordlength decimal computer (可变字长、十进制)
installed more than 10,000 units between 1960 and 1964. 商业上大获成功
IBM 1401 system
IBM 1401
1401 Processing Unit
1402 Card Read-Punch
1403 Printer
Notes: 1951年：UNIVAC-1 ——第一台商用计算机系统诞生，设计者是J.Presper Eckert和John Mauchly。被美国人口普查部门用于人口普查，标志着计算机进入了商业应用时代; UNIVAC-III 采用Tranisitor； UNIVAC-III；

## Slide 25: UNIVAC III (1962)
UNIVersal Automatic Computer III (1962)
Designed by John Perper Eckert and John Mauchly (ENIAC designers)
An improved transistorized replacement for UNIVAC I and UNIVAC II
Notes: 1951年：UNIVAC-1 ——第一台商用计算机系统诞生，设计者是J.Presper Eckert和John Mauchly。被美国人口普查部门用于人口普查，标志着计算机进入了商业应用时代; UNIVAC-III 采用Tranisitor； UNIVAC-III；

## Slide 26: 高级编程语言出现：FORTRAN (1957)
John Backus
developed FORTRAN in 1957 for the IBM 704 computer
inventor of the Backus–Naur form (BNF)
National Medal of Science in 1975
John Backus (1924-2007)
The first widely-used high-level programming language
第一个广泛使用的高级编程语言
IBM 704 computer
Turing Award 1977
Notes: 高级编程语言 FORTRA 也是在第二代计算机的这个时候开始发展

## Slide 27: Electronic Computers -- 3rd Generation (1964-1971)
Dominant technologies:
  Processors: Integrated circuits
  Memory:
    Early: Magnetic cores
    Later: Integrated circuits(SRAM, DRAM)
  OS: run many different applications at one time
  General-purpose computers
    Minicomputers: PDP-11, VAX11-780
    IBM system/360
  Supercomputer s
    Control Data 7600
    Cray-1

## Slide 28: IBM System/360 Family (1964)
Announced in 1964, delivered in 1965
  Model 30: up to 34,500 instructions per second, with memory from 8 to 64 KB.
  Model 91 in 1967: up to 16.6 million instructions per second, with memory from 1M to 4M
  Extremely successful in the market 商业上极为成功
Gene Amdahl (1922-2015)
IBM System/360 Model 30
Mainframe
Disk drive
Tape drive
First planned “family”
  Similar or identical instruction sets
  Similar or identical O/S
  Increasing speed
  Increasing number of I/O ports
  (i.e. more terminals)
  Increased memory size
  Increased cost
Backward compatibility 向前兼容
  Computer System Architecture Specification
  Chief Architect: Gene Amdahl (NAE in 1967)
  A Single Operating System for All: OS/360
  Dynamic address translation (virtual memory) 虚拟内存
  Time-sharing 分时

## Slide 29: IBM Compatibility Problem in Early 1960s
By early 1960’s, IBM had 4 incompatible lines of computers !
  701  7094
  650  7074
  702  7080
  1401  7010
Each system has its own
  Instruction set architecture
  I/O system and secondary storage
  Assemblers, compilers, libraries, …
  Market niche: business, scientific, real time, …

## Slide 30: DEC PDP-8
1964
First minicomputer (after miniskirt!)
Did not need air conditioned room
Small enough to sit on a lab bench
$16,000
  $100k+ for IBM 360
Embedded applications & OEM
BUS STRUCTURE

## Slide 31: UNIX (1960s) & C programming language (1972)
Ken Thompson & Dennis Ritchie at Bell Labs
Designed and implemented Unix OS in 1960s
Thompson invented B programming language
Ritchie invented C programming language in 1972-1973
Ken Thompson (1943-)
Dennis M. Ritchie (1941-2011)
DEC PDP-7
as used for initial work on Unix
Turing Award 1983
UNIX又孵育了Linux，及安卓Android
Ritchie & Thompson
at a PDP-11
Notes: 高级编程语言 FORTRA 也是在第二代计算机的这个时候开始发展

## Slide 32: Pascal programming language (1970)
designer of the programming languages Euler, Algol W, Pascal, Modula, Oberon
Pascal programming language: 1970.
提出：Algorithms + Data Structures = Programs
Niklaus Wirth (Turing Award 1984 )
Niklaus Wirth (1934- ) 瑞士
《Algorithms + Data Structures = Programs》
1976
Pascal语言的论文(1970)

## Slide 33: Electronic Computers -- 4th Generation (1971- )
Dominant technologies
  Processors:
  Custom LSI or VLSI modules on PC board
  Memory: SRAM, DRAM
  Microprocessor: : Texas Instruments, Intel, and Garrett AiResearch
General-purpose computers
  IBM 3xxx, 43xx series
  Minicomputers: VAX8400
Minisupercomputers:
  Convex C-1, C-2, C-3
Vector supercomputers
  Cray-2, Cray X-MP, Cray Y-MP
  Fujitsu, Hitachi, NEC

## Slide 34: Computer Mouse (1968)
NLS system (or “oN-Line System”) 1960s
  A revolutionary computer collaboration system developed in the 1960s.
  Designed by Douglas Engelbart
  Publicly demonstrated at the AFIP Fall Joint Conference in 1968
Douglas Engelbart (1925-2013)
Turing Award 1997
1968年大会演示：用鼠标进行文档编辑
光标
鼠
标
Main features
  The mouse
  Multiple windows
  hypermedia
  modern word processing
  shared files
  electronic messaging
  shared displays with multiple pointers
  audio/video conferencing
  ideas of an Internet

## Slide 35: Dynabook vision (1972)
Dynabook
  In 1972 Alay Kay’s article “A personal computer for children of all ages”
  Conceptual vision of a laptop/tablet computer.
  提出了便携电脑与平板电脑的原型设计
Turing Award 2003
Alan Kay (1940- )
Also:
Smalltalk面向对象程序设计思想提出者
overlapping windowing GUI提出者
Notes: Dynabook in his 1972 proposal "A personal computer for children of all ages",[1] outlines the requirements for a conceptual portable educational device that would offer similar functionality to that now supplied via a laptop computer or (in some of its other incarnations) a tablet or slate computer

## Slide 36: The first modern personal computer (首台现代个人电脑)
Xerox Alto in 1973 at Xerox PARC
  designed mostly by Charles P. Thacker
  Mouse-driven Graphical User Interface
Charles Thacker (1943-2017)
Turing Award 2009
Xerox Alto (1973)
Alto Mouse
Xerox Star (1981)

## Slide 37: Commercial Personal Computer
IBM PC：with an Intel CPU & Microsoft’s DOS in 1981
  Price started at $1,565
  300,000 sold in 1981
  3,274,000 sold in 1982
TIME named in 1982
Machine of the year
Apple (Steve Jobs) developed Macintosh OS with GUI in 1984
Microsoft (Bill Gates) released Windows 1.0 in 1985, the first version.

## Slide 38: RISC Architecture (1980s) ：更高的性能
RISC (Reduced Instruction Set Computer): a computer instruction set
  fewer cycles per instruction (CPI) than a Complex Instruction Set Computer (CISC).
  指令执行用尽量少的时钟周期、指令编码长度定长等  提高CPU与编译效率
  Now used in 99% of new computer chips, e.g. smartphones
John Cocke (1925-2002)
Turing Award 1987
1975-1980: IBM 801
The 1st RISC system
 IBM PowerPC
spent his entire career as an industrial researcher for IBM in1956-1992.
Turing Award 2017
John L. Hennessy (1952-)
David Patterson (1947-)
MIPS project of a Stanford graduate course in 1981
 found MIPS company in 1985
President of Stanford Univ. (2000-2016)
Chairman of Alphabet
Turing Award 2017
Berkeley RISC project from 1980
 commercialized as the SPARC.
one of the innovators of RAID in 1989-1993
现在绝大部分芯片已采用RISC架构，如ARM芯片、智能手机

## Slide 39: RISC
Dominant technologies
  Processors: Mass-produced microprocessors
  Memroy: SRAM, DRAM
  Compiler optimization
RISC processors
  MIPS (Silicon Graphics)
  PA-RISC (Hewlett Packard)
  SPARC ( Sun Microsystems)
  Alpha ( Digital Equipment)
  PowerPC( Apple, Motorala, IBM)
  Motorala 88000
  I860, i960 (Intel)
CISC processors:
  80x86, Pentium, Penium Pro, Pentium II & III (Intel)

## Slide 40: Speeding it up
Pipelining
On board cache
On board L1 & L2 cache
Out Of Order execution
Branch prediction
Data flow analysis
Speculative execution
Multiple issue: Superscaler, VLIW

## Slide 41: The 5th Generation？
Quantum Computer 量子计算机
Neuromorphic Computer 类脑计算机
Wearable Computer 穿戴计算机
Intelligence Computer 人智计算机

## Slide 42: What is a computer？
Computer is an electronic device that manipulates data according to a list of instructions (program), with capability of Turing machine.
  Electronic realization 电子化的实现方式
  A set of instructions in a well-defined manner 有指令集  general-purpose
  Execution of a pre-recorded list of instructions 可执行指令  program-controlled
  Memory that can store instructions and data 可存储指令与数据  stored program
  Turing-complete in theory 计算能力上是图灵完全  equivalent to Turing machine

## Slide 43: What lessons we learned from the history ?
Technological improvements more steady than progress in computer architecture, greatly promotes the improvement of computer performance
After RISC emergence, computer design emphasized both architectural innovation and efficient use of technology improvements.
Software advances can inspire architecture innovations
Raising the hardware/software interface creates opportunities for architecture innovation
Ultimately the marketplace settles architecture debates

## Slide 44: 1.2 Eight Great Ideas in Computer Architecture

## Slide 45: Eight Great Ideas
Design for Moore’s Law （设计紧跟摩尔定律）
Use Abstraction to Simplify Design (采用抽象简化设计)
Make the Common Case Fast (加速大概率事件)
Performance via Parallelism (通过并行提高性能)
Performance via Pipelining (通过流水线提高性能)
Performance via Prediction (通过预测提高性能)
Hierarchy of Memories (存储器层次结构)
Dependability via Redundancy (通过冗余提高可靠性)

## Slide 46: Idea1：Design for Moore’s law
Increased density of components on chip
Number of transistors on a chip will double every year
Since 1970’s development has slowed a little
  Number of transistors doubles every 18 months
Cost of a chip has remained almost unchanged
Higher packing density means shorter electrical paths, giving higher performance
Smaller size gives increased flexibility
Reduced power and cooling requirements
Fewer interconnections increases reliability

## Slide 47: Idea1：Design for Moore’s law
One constant for computer designer is rapid change.
Design for where it will be when finishes rather than design for where it starts.
Gordon Moore, a cofounder of Intel, predicts that the number of transistors which can be placed on a single chip will double every 2 year. It has held steady and was dubbed “Moore’s Law” around 1970
Smaller Transistor, more function on same chip area;
Smaller Transistor, low power
Smaller Transistor, smaller area for same function, low cost;
Why Moore’s law?
Notes: 在高性能芯片，特别是处理器的设计中，如果没有紧跟摩尔定律的企业就会被淘汰。

## Slide 48: Pitfall
Ignoring the inexorable progress of hardware when planning a new machine.
Example
  The machine introduce in three years will be a terrific seller because it’s three times as fast as anything available today.
  Machine x will be 1.53x = 3.4x

## Slide 49: Idea2: Use abstraction to simplify design
Lower-level details are hidden to offer a simple model at higher level
Notes: 在考虑通俗易懂的例子。

## Slide 50: Eight Great Ideas --3 in Computer Architecture
Make the common case fast
  Common case is often simple
vs

## Slide 51: Idea3：Make the common case fast
Making the common case fast will tend to enhance performance better than optimizing the rare case
for(i=0;i<2;i++){
洗衣半小时
}
for(i=0;i<1000;i++){
上班走路1小时
}
for(i=0;i<2;i++){
做饭半小时
}
I think I should buy a car first.
Notes: Principle 1

## Slide 52: Pitfall on Performance
Expecting the improvement of one aspect of a computer to increase overall performance by an amount proportional to the size of the improvement.
Example

## Slide 53: Amdahl’s law
Amdahl's law defines the speedup
If we know two factors:
  Fraction enhanced : Fraction of computation time in original machine that can be converted to take advantage of the enhancement.
  Speedup enhanced in enhanced mode : Improvement gained by enhanced execution mode:

## Slide 54: Idea4:Performance via parallelism
Get more performance by performing operation in parallel

## Slide 55: Idea5: Performance via pipelining
A, B, C, D all have some clothes to wash, dryer and fold
Wash: 30minuts
Dryer: 40minuts
Fold: 20minuts
Total time ?
(30+40+20)x4 = 360
Notes: 四抱衣服总的时间: (30+40+20)x4 = 360

## Slide 56: Idea5 :Performance via pipelining
30+40*4+20=210
Extra Cost？
Notes: Extra：B的洗衣服的步骤也变成40分钟，因为需要等待烘干器烘干，导致洗衣机有10分钟浪费； 所以流水线最好的状态的每一个步骤时间都一样；

## Slide 57: Idea6 :Performance via prediction
To guess and start working rather than waiting until you know for sure
The mechanism to recover from a misprediction is not too expensive and prediction is relatively accurate
Notes: 飞碟射击

## Slide 58: Idea7 :Hierarchy of memories
Hierarchy of Memory
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger
Size / speed
1000B/300ps
64KB/1ns
256KB/3-10ns
2-4MB/10-20ns
4-16GB/50-100ns
4-16TB/5-10ms

## Slide 59: Idea8: Dependability via redundancy
Not only be fast, also to be dependable.
Any physical device can fail.
Make systems dependable by including redundant components that can take over when a failure occurs and to help detect failures
Notes: 大货车采用双排轮胎

## Slide 60: Idea8: Dependability via redundancy
Dependability via Redundancy

## Slide 61: 1.3 Below your program computer Software system

## Slide 62: Computer organization
Decomposability of computer systems
Computer System
Hardware
Software
Application software(应用软件): word, PPT, office
System software
Operation system：Linux, macos
Compiler(编译器)：GCC
Firmware(Driver software):例如：网卡驱动
Notes: 首先介绍Hardware ， 这里对Hardware进行展开；

## Slide 63: Software categorization
Categorize software by its use
  Systems software ---- aimed at programmers
  Applications software ---- aimed at users
Operating system
  Handing basic input and output operations
  Allocating storage and memory
  Sharing the computer among multiple applications using it simultaneously
Compiler: Translation of a program written in HLL(高级编程语言)
Firmware(驱动): Software specially designed for a piece of hardware

## Slide 64: Levels of program code
High-level programming language(高级编程语言)
  Notations more closer to the natural language ex. A + B
  The compiler translates into assembly language
  Advantages over assembly language
    Think in a more natural language
    Programs can be independent of hardware
Assembly language(汇编语言)
  Symbolic notations ex. add A, B
  The assembler translates them into machine instruction
Machine language(机器语言)
  Computers only understands electrical signalson/off
  Binary numbers express machine instructions
  ex. 1000110010100000 means to add two numbers

## Slide 65
The HW/SW Interface
Compiler
lw $15, 0($2)
add $16, $15, $14
add $17, $15, $13
lw $18, 0($12)
lw $19, 0($17)
add $20, $18, $19
sw $20, 0($16)
a[i] = b[i] + c;
Hardware
Systems software
(OS, compiler)
Application software
Assembler
000000101100000
110100000100010
…

## Slide 66: From a High-Level Language to the Language of Hardware
Lower-level details are hidden to higher levels
  Instruction set architecture（指令集） ---- the interface between hardware and lowest-level software
  Many implementations of varying cost and performance can run identical software
Notes: 指令集将处理器的硬件抽象化(Abstraction); 核心；

## Slide 67: Program execution
Object
model
Byte
Code
Source
Code
Editor
Executable
File
Excute
Compile
Run
Interpreter
编
译
Link
interpreter
Static
Libary
Dynamic
Link Libary
C、C++
Pascal
Fortran
Basic
ASP
JS
Java

## Slide 68: Start a C program in a file on disk to run 1
Compiling
  C program  assembly language program
Assembling
  Assembly language program  machine language module
Linking
  Object modules (including library routine)  executable program
  6 pieces of the object file for Unix systems:
    object file header
    text segment
    data segment
    relocation information
    symbol table
    debugging information
  Place code and data modules symbolically in memory
  Determine the addresses of data and instruction labels
  Patch both the internal and external references

## Slide 69: Start a C program in a file on disk to run 2
Loading
  Determine size of text and data segments
  Create an address space large enough
  Copy instructions and data from executable file to memory
  Copy parameters (if any) to the main program onto the stack
  Initialize registers and set $sp to the first free location
  Jump to a start-up routine

## Slide 70: A translation hierarchy

## Slide 71: MIPS memory allocation for program and data
Access data by
$gp +/- offset(16bit)
10000000x
~ 1000FFFFx
Notes: 静态数据：那些不随时间或其它数据变化而变化的数据.其中又可分为结构参数和功能参数.
动态数据：

## Slide 72: 1.4 Under the covers computer hardware system

## Slide 73: Touchscreen
PostPC device
Supersedes keyboard and mouse
Resistive and Capacitive types
  Most tablets, smart phones use capacitive
  Capacitive allows multiple touches simultaneously

## Slide 74: Through the Looking Glass
LCD screen: picture elements (pixels)
  Mirrors content of frame buffer memory

## Slide 75: Computer organization
Decomposability of computer systems
Computer System
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU: adder, multiplier
Registers
……
Hardware
Software
Input: keyboard
Bidirectional: RS-232,USB
Output: VGA，LCD
Notes: 首先介绍Hardware ， 这里对Hardware进行展开；

## Slide 76: Von Neumann’s Architecture

## Slide 77: Five classic components of hardware
I/O: input data
I/O: output data
Memory: store data
Memory: store program
CPU: process data
Notes: 此图围绕数据展开：input ,output ,process, store, 说明hardware的5个关键；
I/O三种类型， input， output，双向；
Memory 两种类型，程序存储和数据存储；
CPU：处理数据；

## Slide 78: Opening the Box
Components of Apple iPad
Logical Board (main board:主板)
Integrated Circuit on it
Central Processor Unit (CPU)

## Slide 79: I/O Interfaces
Components of Apple iPad
I/O dominates this device.
Input device: A mechanism through which the computer is fed information
  Multitouch LCD(触摸屏)
  Front/near facing camera(前置摄像头)
  Microphone, headphone(麦克风)
  Gyroscope(陀螺仪)
  WIFI, Bluetooth(蓝牙)
Output device: A mechanism that conveys the result of a computer to a user, such as a displayer, or to another computer
  Speaker(扬声器)
  Multitouch LCD
  WIFI, Buluetooth
Multitouch LCD
Logical Board
Front/near facing camera
Microphone
WIFI, Bluetooth
Notes: 拆解；找一张彩照， 能够在涂上标注出这些， 一个框，加箭头， 然后这些器件； IPAD 任何都可以

## Slide 80: Logical board(主板)
Composed of integrated circuits:
  CPU(Apple A5): Dual ARM processor, 1GHZ, 512MB DDR inside package.
  Flash(闪存): 32GB Flash.
  Power controller: start up(启动), shutdown(关机), standby(待机)
  I/O controller: e.g. Control Touchscreen , control microphone
Composed of integrated circuits (chips：集成电路，芯片): A device combining dozens of millions of transistors.
Power
Controller
CPU
Flash
I/O Controller
Power
Controller
Flash
Notes: Logical board 均为Integrated circuit;
主要的集成电路是： CPU(A5), Memory，分别介绍CPU和Memory的功能；
这页主要介绍CPU， 并引出集成电路；

## Slide 81: CPU (Processor)
CPU(Processor): active part of the computer, which contains the datapath and control and which adds numbers, tests numbers, signals I/O devices to activate, and so on.
  Datapath (数据通路): performs arithmetic operation
  Control (控制通路): commands the datapath, memory, and I/O devices according to the instructions of the program

## Slide 82: 华为Tianshan 服务器内部视图
内存
PCIe 扩展插槽
风扇
电源
CPU
硬盘
Notes: CPU
  CPU是Central Processing Unit的缩写，即中央处理器。由控制器，运算器，寄存器和内部总线构成，是整个计算机系统中最重要的部分。
内存
  内存是介于CPU 和外部存储之间，是CPU 对外部存储中程序与数据进行高速运算时存放程序指令、数据和中间结果的临时场所，它的物理实质就是一组具备数据输入输出和数据存储功能的高速集成电路。
硬盘
  服务器上使用的硬盘，有区别于普通硬盘。目前服务器市场上采用的硬盘主要有三种，SATA硬盘、SCSI硬盘以及SAS硬盘。如果说服务器是网络数据的核心，那么服务器硬盘就是这个核心的数据仓库，所有的软件和用户数据都存储在这里。
电源
  服务器电源和个人电脑电源一样，都是一种开关电源。服务器电源按照标准可以分为ATX电源和SSI电源两种。ATX标准使用较为普遍，主要用于台式机、工作站和低端服务器；而SSI标准是随着服务器技术的发展而产生的，适用于各种其他档次的服务器。
网卡
  又称网络适配器或网络接口卡（NIC），英文名为Network Interface Card。适用于服务器与交换机等网络设备之间的连接。

## Slide 83: 华为TaiShan 服务器物理结构
1 | IO模组1 | 2 | IO模组2
3 | 电源模块 | 4 | 机箱
5 | IO模组3 | 6 | 超级电容支架
7 | 导风罩 | 8 | 前置硬盘背板
9 | 风扇支架 | 10 | 风扇模块
11 | 前置硬盘 | 12 | 理线架
13 | 散热器 | 14 | DIMM
15 | 主板 | 16 | RAID扣卡
17 | 灵活IO卡1（CPU 1） | 18 | iBMC插卡
19 | 灵活IO卡2（CPU 2） | - | -
TaiShan 200服务器（型号2280）

## Slide 84: Memory: A safe place for data
Memory |  | Price | Speed | Capacity | Used for
SRAM | volatile | / | Fastest | KB~MB | Cache
DRAM | volatile | $3~4/GB | Fast | MB~GB | Main memory
Hard disk | nonvolatile | $0.05~1/GB | Slow | TB~PB | PC Storage
Flash Memory | nonvolatile | $0.75~$1/GB | Medium | GB~TB | PMD Storage
Memory(存储): the storage area programs are kept and that contains the data needed by the running programs
Main Memory(主存): volatile; used to hold programs while they are running.( DRAM in computers)
Second memory: nonvolatile; used to store programs and data between runs. (Flash in PMD, magnetic disks)
Volatile (易失性)
  DRAM (Dynamic Random-Access Memory):动态随机存储器
  SRAM (Static Random Access Memory)：静态随机存储器
Nonvolatile (非易失性)
  Solid state memory (Flash Memory):固态硬盘 or 闪存
  Magnetic disk (Hard disk) ：硬盘

## Slide 85: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory
  Optical disk (CDROM, DVD)

## Slide 86: Networks
Communication, resource sharing, nonlocal access
Local area network (LAN): Ethernet
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 87: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface
  The ISA plus system software interface
Implementation
  The details underlying and interface
The BIG Picture

## Slide 88: 1.5 Technologies for building Processors and memory

## Slide 89: Integrated circuits
Integrated circuits the kernel components of the logic boards: driving our advancing technology.
(主板核心由集成电路/芯片构成，集成电路驱动我们技术的进步)
Both processor and memory are made of integrated circuits.
Power
Controller
CPU
Flash
I/O Controller
Power
Controller
Flash
How to build ?
Notes: 引出集成电路

## Slide 90: The semiconductor silicon and the chip manufacturing process (集成电路制造流程)
芯片设计
Chip design
晶圆生产
Wafer production
芯片封装
Chip package
芯片测试
Chip test
Wire Bond(焊线)
Package(封装)
Slicing(晶圆切片)
Final test(成品测试)
Finished chip(芯片成品)
Photo resist(光刻)
Ingot cutting(铸锭切割)
Wafer(晶圆)
Wafer test(晶圆测试)
Circuit design(电路设计)
Layout design(版图设计)
Mask(掩膜)

## Slide 91: Sand(沙子) to wafer (晶圆)
Sand(沙子)
Silicon melting(硅熔炼)
Silicon ingot(硅锭)
Ingot cutting(硅锭切割)
Wafer(晶圆)
从沙子中提取约99.9999%的以上的高纯度硅（11个9）
将高纯度硅制作成硅锭
钻石刀将硅晶柱切成圆片
抛光后便形成Wafer(晶圆)
芯片的地基——晶圆
11个9纯度的硅锭

## Slide 92: Photo resist(光刻)
Photo Resist(光刻胶)
Photolithography(光刻)
Dissolving photoresist
(溶解光刻胶)
紫外线透过掩模照射光刻胶，掩膜上印着预先设计好的电路图案
进入50-200纳米尺寸微观视角
用化学物质溶解掉暴露出来的晶圆部分，剩下的光刻胶保护着不应该蚀刻的部分。
光刻过程中曝光在紫外线下的光刻胶被溶解掉，清除后留下的图案和掩模上的一致
Etching(蚀刻)
掩膜(Mask)
蚀刻完成后，清除全部光刻胶，露出一个个凹槽
硅片上涂光刻胶
1
2
3
4
重复20～40次
芯片

## Slide 93: Package(封装) and Test (测试)
Slicing
(晶圆切片)
Packing
(包装)
Test
(测试)
Package
(封装)
用精细的切割器将芯片从晶圆上切下来
经过测试后就可以包装销售了
焊接到基片上，装壳密封
散热片
内核(die)
衬底基片
1
4
2
3

## Slide 94: IC procedures

## Slide 95: Integrated Circuit Cost
300mm wafer, 280 chips, 32nm technology
Each chip is 20.7 x 10.5 mm
Intel Core i7 Wafer
Nonlinear relation to area and defect rate
  Wafer cost and area are fixed
  Defect rate determined by manufacturing process
  Die area determined by architecture and circuit design

## Slide 96: IC technique evolution
1962, SSI（Small-Scale Integration） 12 transistors
1966, MSI（Medium-Scale Integration）,100－1k transistors
1967－1973年， LSI（Large-Scale Integration），1k~100k transistors
1977，VLSI（Very Large-Scale Integration），30m2, 150k transistors
1993, ULSI (Ultra Large-Scale Integration) 16M FLASH and 256M DRAM which integrate 10M transistors
1994， GSI（Giga Scale Integration） 1G DRAM which integrate 100M transistors
2007: 2T flops 80core CPU

## Slide 97
Development of integrated circuits (集成电路发展)
Relative performance per unit cost of technologies used in computers over time
Notes: 集成大幅度降低了电子产品的成本，说明集成电路的重要性；（更加能体现出集成度；)

## Slide 98
Processor Technology Trends
Shrinking of transistor sizes: 250nm (1997) 
130nm (2002)  70nm (2008)  35nm (2014)  5nm (2020)
Transistor density increases by 35% per year and die size
increases by 10-20% per year… functionality improvements!
Transistor speed improves linearly with size (complex
equation involving voltages, resistances, capacitances)
Wire delays do not scale down at the same rate as
transistor delays

## Slide 99
Memory and I/O Technology Trends
DRAM density increases by 40-60% per year, latency has
reduced by 33% in 10 years (the memory wall!), bandwidth
improves twice as fast as latency decreases
Disk density improves by 100% every year, latency
improvement similar to DRAM
Networks: primary focus on bandwidth; 10Mb  100Mb
in 10 years; 100Mb  1Gb in 5 years

## Slide 100: Real staff: Intel
1971 - 4004
  First microprocessor
  All CPU components on a single chip
  4 bit
Followed in 1972 by 8008
  8 bit
  Both designed for specific applications
1974 - 8080
  Intel’s first general purpose microprocessor

## Slide 101: Growth in CPU Transistor Count

## Slide 102: Pentium Evolution (1)
8080
  first general purpose microprocessor
  8 bit data path
  Used in first personal computer – Altair
8086
  much more powerful
  16 bit
  instruction cache, prefetch few instructions
  8088 (8 bit external bus) used in first IBM PC
80286
  16 Mbyte memory addressable
  up from 1Mb
80386
  32 bit
  Support for multitasking

## Slide 103: Pentium Evolution (2)
80486
  sophisticated powerful cache and instruction pipelining
  built in maths co-processor
Pentium
  Superscalar
  Multiple instructions executed in parallel
Pentium Pro
  Increased superscalar organization
  Aggressive register renaming
  branch prediction
  data flow analysis
  speculative execution

## Slide 104: Pentium Evolution (3)
Pentium II
  MMX technology
  graphics, video & audio processing
Pentium III
  Additional floating point instructions for 3D graphics
Pentium 4
  Note Arabic rather than Roman numerals
  Further floating point and multimedia enhancements
Itanium
  64 bit
See Intel web pages for detailed information on processors

## Slide 105: Challenges of integrated circuits manufacturing
The integration of SoC increases rapidly(1billions transistor on single chip), and complexity augments increasingly.
(集成度越来越高，复杂度快速增加)
The size of the IC process reaches physical limitation(5nm now). More and more precision requirements and more and more difficult to manufacture.
(工艺尺寸达到物理极限，加工精度越来越高， 制造难度越来越大)
Involved many technologies: Electronics, optics, Mechanics, computer science… Each technology is hard to break through.
(多个技术的集成：电子，光学，机械，计算机，每一个技术都能难突破)

## Slide 106: 1.6 Performance

## Slide 107: Defining Performance
Which airplane has the best performance?

## Slide 108: Defining Performance
Response (Execution) time
  user perception
  system performance
  the only unimpeachable measure of performance
  Mobile devices
CPU time
  designer perception
  CPU performance
Throughput
  administrator perception
  server
改进性能的方法 | Response time | Throughput
Replacing a faster processor | ↑ | ↑
Adding additional processors for a system use MP for independent task | - | ↑

## Slide 109: Performance Metrics
Response (Execution) time
  The total time required for the computer to complete a task, including disk accesses, memory accesses, I/O activities, operating system overhead, CPU execution time.
CPU time
  The actual time the CPU spends computing for a specific task.
Throughput(Bandwidth)
  The total work done in a given time.
  The number of tasks completed per unit time.

## Slide 110: CPUtime—CPU performance
CPU time is further divided into:
  User time - time spent in user mode
  System time - time spent in the operating system (OS)
Unix time command reports CPU time as:
  90.7u 12.9s 2:39 65%
  90.7 user CPU seconds (in the user’s program)
  12.9 system CPU seconds (in the system calls e.g. printf)
  2 minutes, 39 seconds wall-clock time
  65% of the wall clock time was spent running on the CPU

## Slide 111: Relative Performance
“Performance of P1 is better than P2 ” is, for a given work load L, P1 takes less time to execute L than P2 does
performance(P1) > Performance(P2)
 Execution Time(P1, L) < Execution Time(P2, L)
“Processor X is n times fast than Y” is

## Slide 112: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period: duration of a clock cycle
  e.g., 250ps = 0.25ns = 250×10–12s
Clock frequency (rate): cycles per second
  e.g., 4.0GHz = 4000MHz = 4.0×109Hz
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 113: CPU Time Example
Computer A: 2GHz clock, 10s CPU time
Designing Computer B
  Aim for 6s CPU time
  Can do faster clock, but causes 1.2 × clock cycles
How fast must Computer B clock be?

## Slide 114: Instruction Count and CPI
Instruction Count for a program
  Determined by program, ISA and compiler
Average cycles per instruction
  Determined by CPU hardware
  If different instructions have different CPI
    Average CPI affected by instruction mix

## Slide 115: CPI in More Detail
If different instruction classes take different numbers of cycles
Weighted average CPI
Relative frequency

## Slide 116: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 117: Example：Which is fast and by how much ?
 | clock period | CPI | CPU clock cycles | CPU time
A | 250 ps | 2.0 | I 2.0 | 500 I ps
B | 500 ps | 1.2 | I 1.2 | 600 I ps
 | clock period | CPI | CPU clock cycles | CPU time
A | 250 ps | 2.0 |  | 
B | 500 ps | 1.2 |  | 
Answer: CPU PerformanceA Execution TimeB 600 * I ps
--------------------------- = -------------------------- = ------------------- = 1.2
CPU PerformanceB Execution TimeA 500 * I ps
Notes: 考虑依赖指令数的执行时间
CPI
两种性能度量转换

## Slide 118: Question:
Suppose that the clock rate of your favorite microprocessor was doubled by the manufacturer. Does this imply that the CPU time of your favorite program will be reduced by 50% on the new microprocessor? If so, under what conditions? If not, why not?

## Slide 119: Iron Law—CPU performance
Architecture --> Implementation --> Realization
Compiler Designer Processor Designer Chip Designer
CPU time = Instructions * CPI * Clock cycle time
= Instructions * CPI / Clock rate
Hardware / Software | Affects what ? | How?
Algorithm | IC, possibly CPI | Favoring instructions
Programming language | IC, CPI | Java : indirect calls
Compuiler | IC, CPI | 
Instruction set Architecture | IC, CPI, CC | 
Organization | CPI, CC | 
IC | CC | 

## Slide 120: Incredible performance improvement

## Slide 121: Conclusions
25%: Technological improvements contributes a lot in computer performance
52%: After RISC emergence, computer design emphsized both architecutural innovation and efficient use of technology improvments.
  CA plays an important role in perf. Improvement
Why 20% ?
Three Walls !

## Slide 122: Challenges of the processor
处理器和存储器性能的提高不成比例，“内存墙”问题日趋严重，“冯诺依曼”架构面领挑战。
单位面积功耗增大，散热问题日趋严峻，“功耗墙”问题凸显。
受物理规律限制，摩尔定律面临失效，靠工艺进步获得的性能红利逐渐减弱。
Memory Wall（内存墙）
工艺发展限制
Power Wall(功耗墙)

## Slide 123: ILP Wall
“ILP wall” refers to increasing difficulty to find enough parallelism in the instructions stream of a single process to keep higher performance processor cores busy.
20%: little ILP left to exploit due to power dissipation and memory gap
  Faster uniprocessor => multiple processor on chip
  ILP => TLP and DLP
  Implicity, compiler and hardware => Explicity, programmer

## Slide 124: Factors that affect performance ?
Hardware or software component | How this component affects performance | Where is this topic covered?
Algorithm | Determines both the number of source-level statements and the number of I/O operations executed | Other books!
Programming language,compiler, and architecture | Determines the number of machine instructions for each source-level statements | Chapter 2 and 3
Processor and memory system | Determines how fast instructions can be executed | Chapter 4,5 and 6
I/O system(hardware and operating system) | Determines how fast I/O operations may be executed | Chapter 4,5，and 6

## Slide 125: The sea change
Parallelism
Hardware  Hardware and compiler  compiler and programmer
ILP, Loop-level Parallism  TLP, DLP

## Slide 126: Concluding Remarks
Cost/performance is improving
  Due to underlying technology development
Hierarchical layers of abstraction
  In both hardware and software
Instruction set architecture
  The hardware/software interface
Execution time: the best performance measure
Power is a limiting factor
  Use parallelism to improve performance

## Slide 127: Challenges for the Hardware Designers
Major concerns:
  The performance problem (especially scientific workloads)
  The power dissipation problem (especially embedded processors)
  The temperature problem
  The reliability problem
New trend
  DSA (Domain Specfic Architecture)
  GP-GPU ( parallel computing using GPU )
  Heterogeneous multicore structure/ Hardware software co-design
  TPU –Abstraction level is going up

## Slide 128: Real staff： Benchmarking the intel Corei7--CPUtime

## Slide 129: Benchmarking the intel Corei7 -- perf/watt

## Slide 130: What you can learn from this course ?

## Slide 131: What You Will Learn
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
What is parallel processing

## Slide 132: Content
Chapter1: Computer Abstraction and Technology
Chapter2: Instructions: Language of the Computer
Chapter3: Arithmetic for Computers
Chapter4: The Processor：Datapath and Control
Chapter5: Large and Fast: Exploiting Memory Hierarchy
Chapter 6: Parallel processor from client to Cloud (选讲，非考试内容)
Appendix: Storage, Networks, and Other Peripherals (Ch8 of Version 3,了解概念)
核心内容

## Slide 133: Instructions: Language of the computer
Operations of the computer hardware (计算机硬件的操作)
Operands of the computer hardware(计算机硬件的操作数)
Signed and unsigned numbers (有符号和无符号数)
Representing instructions in the computer(计算机中指令的表示)
Logical operations(逻辑操作)
Instructions for making decision(决策指令)
Supporting procedures in computer hardware(计算机对过程的支持)
Instruction addressing (指令的寻址)
Assembler (汇编): add $t0, $s1, $s2
  | 000000 | 10001 | 10010 | 01000 | 00000 | 100000 |
  6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Translate
Machine Code （机器码）
Notes: 上完这一章，将知道MIPS架构处理器的指令架构，如何把汇编转换成机器码；

## Slide 134: Arithmetic for computers
Addition and Subtraction(加减)
Logical operations(逻辑操作)
Constructing a simple ALU(简单ALU设计)
Multiplication(乘法)
Division(除法)
Floating point arithmetic(浮点操作)
Adding all parts to get an ALU(ALU设计)
ALU示意图
Notes: 介绍CPU支持的各种算术操作，以及ALU的设计；

## Slide 135: The processor：datapath and control
Logic conventions (逻辑设计的一般方法)——数字逻辑课程
Building a datapath (建立数据通路)
A simple implementation scheme (处理器的一种简单实现机制)
A pipeline implementation (流水线处理器的实现)
这章结束，你需要熟悉处理器的各个模块(如图所示)
Notes: 介绍CPU设计的每个部件的实现方式

## Slide 136: Exploiting memory hierarchy
Memory Technology (存储技术)
The Basics of Cache (缓存的基本原理)
Measuring and Improving Cache Performance (缓存性能的评估和改进)
Virtual Memory(虚拟存储)
Temporal Locality(时间局部性): If a data location if referenced then it will tend to be referenced again soon
Spatial Locality(空间局部性): if a data location is referenced, data location with nearby addresses will tend to be referenced soon

## Slide 137: After the course, you should know
The internal organization of computers and its influence on the performance of programs (处理器内部组织结构及其性能影响)
The hierarchy of software and hardware
  How are programs written in high-level language translated into the language of the hardware, and how does it run?
  (高级语言编写的程序如何变成硬件的语言， 它是如何工作的？)
  What is the interface between the software and the hardware, and how does software instruct the hardware to perform?
  (软硬件之间的接口是什么， 软件如何指导硬件工作)
  What determines the performance of a program, and a programmer improve the performance?(什么决定了一个程序的性能)
  What techniques can used to improve performance?
  (什么技术我们可以用来提高性能)

## Slide 138: Questions for you
哪个程序占了计算机那么多资源，为啥响应那么慢
我设置桌面图片对计算机性能有影响么
我能让计算机跑得更快么
病毒原理是什么
为什么上网本2K+，品牌笔记本6K+（配置差不多）
怎么判断一台计算机的性能
四核比单核快么？ AMD与Intel的四核哪个好？
酷睿2过时在哪里，微架构的作用有多大
GPU运行机制，GPGPU的未来

## Slide 139: Questions for you
磁道坏了，怎么办
2、哪个磁盘最快
  C盘快还是E盘快
3、怎么设计undelete软件
  Easy recover软件
4、硬盘格式化为什么可以恢复
  手机通讯录格式化了，怎么恢复
5、flash是U盘、SD、SSD的基础器件，读写10-100万次就坏了，为什么能作为笔记本硬盘
6、硬盘容量一样，性能一样么？
7、硬盘灯为啥经常闪

## Slide 140
End