## Slide 1: Computer Organization & Design —The Hardware/Software Interface
Chapter 4-1 Processor Design

## Slide 2: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
  Single cycle CPU
  Multiple cycle CPU
4.5 Pipelining

## Slide 3: 4.1 Introduction
CPU performance factors
  Instruction count
    Determined by ISA and compiler
  CPI and Cycle time
    Determined by CPU hardware
We will examine two RISC-V implementations
  A simplified version
  A more realistic pipelined version
Simple subset, shows most aspects
  Memory reference: ld, sd
  Arithmetic/logical: add, sub, and, or, slt
  Control transfer: beq，jal
    实现不少于下列指令
    R-Type：add, sub, and, or, xor, srl, sra；
    I-Type：addi, andi, ori, xori, slti, slli, srli,
    lb, lh, lw, lbu, lhu, lwu; Jalr
    S-Type：sb, sh, sw；
    B-Type：beq,bne, blt, bge,bltu, bgeu
    UJ-Type： Jal；
    U-type: Lui;

## Slide 4
Generic Implementation:
  use the program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do

## Slide 5: Instruction Execution Overview
For every instruction, the first two steps are identical
    Fetch the instruction from the memory
    Decode and read the registers
  Next steps depend on the instruction class
    Memory-reference Arithmetic-logical branches
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch comparison
  Access data memory for load/store
  PC  target address or PC + 4

## Slide 6: An abstract view of the implementation of MIPS

## Slide 7: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
4.5 An Overview of Pipelining

## Slide 8: Single implementation

## Slide 9: State Elements
Unclocked vs. Clocked
Clocks used in synchronous logic
  when should an element that contains state be updated?
cycle time
rising edge
falling edge

## Slide 10: Our Implementation
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 11: REGISTER
Register
  State element。
  Can be controled by Write signal.
Register
In
Out
Register
In
Out
Write
Read：
Out=Register
Write：
Register=In
(PC, register file, )
Clock cycle

## Slide 12: Memory
  Instruction memory : ROM, input address, get instruction
  Data memory: RAM.
    Can read or write controlled by signal MemRead and MemWrite.
    Read: input address, get instruction if MemRead=1
    Write: input address & datain, write into memory if MemWrite =1
Instruction
Instruction
Address
Instruction
memory
MemWrite
Read
data
Address
Data
memory
Write
data
MemRead

## Slide 13: D 触发器
C
D
Q
Q
D
Q
C
Q
Symbol of Latch
C | D | Q(t + 1)
0 | X | hold
1 | 0 | Q=0：reset
1 | 1 | Q=1：set
C | D | S | R | Q(t + 1)
0 | X | X | X | hold
1 | 0 | 0 | 1 | Q=0：reset
1 | 1 | 1 | 0 | Q=1：reset
S
R
Truth table

## Slide 14: Register File
  32 64-bit Registers；
  Input: 2 5-bit register number/ one 5-bit register number and 64-bit data;
  Output: 64-bit data;
  Register write control。

## Slide 15: Register File: Read-Output
  Output from the register
5 bits
5 bits
5 bits
64 bits
64 bits
64 bits
Reg. address
Reg. address
Data output

## Slide 16: Register File: Write-Input
  Written to the register
64 bits
rd
5 bits
Reg. address
Write signals

## Slide 17: Register File
Write Register:
  we still use the real clock to determine when to write
Register
C
C
D
D
C
C
D
D
0
1
n-1
n
Register 1
Register n-1
Register n
Register number
Register data
Write
decoder

## Slide 18: Register File 32 X 32 bits

## Slide 19
Description: 32×64bits Register files
Module regs( input clk, rst, RegWrite,
input [4:0] Rs1_addr, Rs2_addr, Wt_addr,
input [63:0] Wt_data,
output [63:0] Rs1_data, Rs2_data
);
reg [63:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (Rs1_addr== 0) ? 0 : register[Rs1_addr]; // read
assign rdata_B = (Rs2_addr== 0) ? 0 : register[Rs2_addr]; // read
always @(posedge clk or posedge rst)
begin if (rst==1)
for (i=1; i<32; i=i+1) register[i] <= 0; // reset
else if ((Wt_addr != 0) && (RegWrite == 1))
register[Wt_addr] <= Wt_data; // write
end
endmodule

## Slide 20: The other elements
Immediate generation unit：
  输入指令产生立即数的逻辑功能
    根据指令类型（加载，存储或者分支指令），产生相应的立即数
  转移指令偏移量左移位的功能
    立即数字段符号扩展为64位结果输出
Immediate generation
  Load:
  0000011
  Save:
  0100011
  Branch:
  1100011
  Jal:
  1101111
S_imm = {{52{inst[31]}}, Inst[31:25], inst[11:7]};
SB_imm = {{51{inst [31]}}, inst[31], inst [7], inst[30:25], inst[11:8],1'b0};
UJ = {{43{inst[31]}}, inst [31], inst[19:12], inst[20], inst[30:21],1'b0};
L_imm = {{52{inst[31]}}, Inst[31:20]};

## Slide 21: CPU Overview

## Slide 22: Multiplexers
Can’t just join wires together
  Use multiplexers

## Slide 23: Control

## Slide 24: Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 25: Clocking Methodology
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 26: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
  Single cycle CPU
  Multiple cycle CPU
4.5 Pipelining

## Slide 27: Contents
Introduction & Logic Design Conventions
Building a datapath
A Simple Implementation Scheme
Pipelining
Exceptions

## Slide 28: 4.3 Building a datapath
Datapath
  Elements that process data and addresses in the CPU
    Registers, ALUs, mux’s, memories, …
We will build a RISC-V datapath incrementally
  Refining the overview design

## Slide 29: RISC-V fields (format)
opcode：basic operation of the instruction.
rs1： the first register source operand.
rs2： the second register source operand.
rd： the register destination operand.
funct： function,this field selects the specific variant of the operation in the op field.
Immediate: address or immediate

## Slide 30
Name | Register name | Usage | Preserved On call?
x0 | 0 | The constant value 0 | n.a.
x1(ra) | 1 | Return address(link register) | yes
x2(sp) | 2 | Stack pointer | yes
x3(gp) | 3 | Global pointer | yes
x4(tp) | 4 | Thread pointer | yes
x5-x7 | 5-7 | Temporaries | no
x8-x9 | 8-9 | Saved | yes
x10-x17 | 10-17 | Arguments/results | no
x18-x27 | 18-27 | Saved | yes
x28-x31 | 28-31 | Temporaries | no
Name | Example | Comments
32 registers | x0-x31 | Fast locations for data. In RISC-V, data must be in registers to perform arithmetic. Register x0 always equals 0.
261 memory words | Memory[0], Memory[8] , …… , Memory[18446744073709551608] | Accessed only by data transfer instructions. RISC-V uses byte addresses, so sequential doubleword accesses differ by 8. Memory holds data structures, arrays, and spilled registers.

## Slide 31: RISC-V assembly language
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add x5,x6,x7 | x5=x6 + x7 | Add two source register operands
 | subtract | sub x5,x6,x7 | x5=x6 - x7 | First source register subtracts second one
 | add immediate | addi x5,x6,20 | x5=x6+20 | Used to add constants
Data transfer | load doubleword | ld x5, 40(x6) | x5=Memory[x6+40] | doubleword from memory to register
 | store doubleword | sd x5, 40(x6) | Memory[x6+40]=x5 | doubleword from register to memory
Logical | and | and x5, x6, 3 | x5=x6 & 3 | Arithmetic shift right by register
 | inclusive or | or x5,x6,x7 | x5=x6 ¦ x7 | Bit-by-bit OR
Conditional Branch | branch if equal | beq x5, x6, 100 | if(x5 == x6) go to PC+100 | PC-relative branch if registers equal
 | branch if not equal | bne x5, x6, 100 | if(x5 != x6) go to PC+100 | PC-relative branch if registers not equal
Unconditional Branch | jump and link | jal x1, 100 | x1 = PC + 4; go to PC+100 | PC-relative procedure call
 | jump and link register | jalr x1, 100(x5) | x1 = PC + 4; go to x5+100 | procedure return; indirect call

## Slide 32: Instruction execution in RISC-V
Fetch :
  Take instructions from the instruction memory
  Modify PC to point the next instruction
Instruction decoding & Read Operand:
  Will be translated into machine control command
  Reading Register Operands, whether or not to use
Executive Control:
  Control the implementation of the corresponding ALU operation
Memory access:
  Write or Read data from memory
  Only ld/sd
Write results to register:
  If it is R-type instructions, ALU results are written to rd
  If it is I-type instructions, memory data are written to rd
Modify PC for branch instructions

## Slide 33: Instruction fetching three elements
PC
Add
Instruction memory
Program counter
Adder
How to connect? Who?
Data Stream of Instruction fetching
Read address
Instruction
Instruction
Memory

## Slide 34: Instruction fetching unit
PC
4
CPU
Read address
Instruction
Instruction
Memory
add
Instruction
Instruction Register
  Can you omit it?

## Slide 35: How simple is!
Why PC+4?

## Slide 36: More Implementation Details
Abstract / Simplified View:

## Slide 37: Path Built using Multiplexer
R-type instruction Datapath
I-type instruction Datapath
  For ALU
  For load
S-type (store) instruction Datapath
SB-type (branch) instruction Datapath
UJ-type instruction Datapath
  For Jump
First, Look at the data flow within instruction execution
Data Stream of Instruction executing

## Slide 38: R type Instruction & Data stream
op(7)
rd(5)
func3
rs1(5)
rs2(5)
func7
rs1
rs2
rd
ins20-24
ins15-19
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
4
RegWrite
ALU operation
ins7-11
control
64bits data
ALUC
add x9, x20, x21
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 39: I type (load) Instruction & Data stream
rs1
rs2
rd
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
4
RegWrite
ALU operation
control
address
Write data
Read data
Imm
Gen
ins7-11
ins0-31
MemWrite
MemRead
32
64
64bits data
ld x1, 200(x2)
Data
Memory
ALUC
ALUop
op(7)
rd(5)
func3
rs1(5)
Immediate(12)
ins15-19
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Read memory and update register
addi x1, x2，4？

## Slide 40: S-type (store) Instruction & Data stream
rs1
rs2
rd
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
4
RegWrite
ALU operation
control
address
Write data
Read data
Imm
Gen
ins0-31
MemWrite
MemRead
32
64
sd x1, 200(x2)
Data
Memory
ALUC
ALUop
ins15-19
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Write register value to memory
op(7)
imm5
func3
rs1(5)
rs2(5)
imm7
ins20-24

## Slide 41: B type Instruction & Data stream of beq
rs1
rs2
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Imm
Gen
32
64
PC
ADD
To PC
control
ALUC
Branch
ALUop
op(7)
imm5
func3
rs1(5)
rs2(5)
imm7
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value
beq x1, x2，200
ins15-19
ins20-24
ins0-31
PC+4
Shift
Left 1

## Slide 42: J type Instruction
rs
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Imm
Gen
ins0-31
ins7-11
16
32
ADD
To PC
control
Branch
PC+4
Jump
Op(7)
rd(5)
Target address(20)
jal x1, procedure
PC
Shift
Left 1

## Slide 43: Composing the Elements
First-cut data path does an instruction in one clock cycle
  Each datapath element can only do one function at a time
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 44: R-Type/Load/Store Datapath

## Slide 45: Full Datapath

## Slide 46: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Imm
Gen
ins0-31
ins15-19
ins20-24
MenWrite
MenRead
32
64
64bits data
MUX
ins7-11
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
R

## Slide 47: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Imm
Gen
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
I-ld
ins15-19
ins20-24
ins7-11
ins0-31
Notes: 立即数指令也是这种情况，addi

## Slide 48: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Imm
Gen
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
S-sd
ins15-19
ins20-24
ins7-11
ins0-31

## Slide 49: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Imm
Gen
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
B-beq
ins15-19
ins20-24
ins7-11
ins0-31

## Slide 50: Full datapath
Registers
Read address1
Read address2
Write address
Write data
Read data1
Read data2
ALU
result
Zero
ALU
3
RegWrite
address
Write data
Read data
Imm
Gen
MenWrite
MenRead
32
64
64bits data
MUX
MUX
ALU operation
Shift
left 1
MUX
ADD
ADD
PC
Data
Memory
Read address
Instruction
Instruction
Memory
4
Instruction
J-jal
ins15-19
ins20-24
ins7-11
ins0-31
MUX

## Slide 51: Contents
Introduction & Logic Design Conventions
Building a datapath
A Simple Implementation Scheme
Pipelining

## Slide 52: Building the Datapath & Controller
There are 7+4 signals
Branch
jump

## Slide 53: Building Controller
Analyse for cause and effect
Information comes from the 32 bits of the instruction
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
ALU's operation based on instruction type and function code

## Slide 54: What should ALU do ?
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on opcode
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
Operation | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Slt
opcode | ALUOp | Operation | Funct7 | funct3 | ALU function | ALU control
ld | 00 | load register | XXXXXXX | xxx | add | 0010
sd | 00 | store register | XXXXXXX | xxx | add | 0010
beq | 01 | branch on equal | XXXXXXX | xxx | subtract | 0110
R-type | 10 | add | 0000000 | 000 | add | 0010
 |  | subtract | 0100000 | 000 | subtract | 0110
 |  | AND | 0000000 | 111 | AND | 0000
 |  | OR | 0000000 | 110 | OR | 0001
 |  | SLT | 0000000 | 010 | Slt | 0111

## Slide 55: The ALU control is where and other signals(6)
Output signals

## Slide 56: Scheme of Controller
2-level decoder
First
Main
decoder
ALU
Decoder
Second
Control Signals (7)
opcode(7)
rd
funct(3)
rs1
rs2
funct(7)
ALU operation(4)
ALU op(2)
Defined
Defined
instruction opcode
(7)

## Slide 57: Signals for datapath Defined 7 control signals
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScr | The second ALU operand come from the second register file output (Read data 2) | The second ALU operand is the sign-extended lower 16 bits of the instruction..
Branch （PCSrc） | The PC is replaced by the output of the adder that computers the value PC+4 | The PC is replaced by the output of the adder that computers the branch target.
Jump | The PC is replaced by PC+4 or branch target | The PC is updated by jump address computed by adder
MemRead | None | Data memory contents designated by the address input are put on the Read data output.
MemWrite | None | Data memory contents designated by the address input are replaced by value on the Write data input.
MemtoReg (2位) | 00：The value fed to register Write data input comes from the Alu | 01：The value fed to the register Write data input comes from the data memory.
 |  | 10：The value fed to the register Write data input comes from PC+4

## Slide 58: Controller Implementation
And
SrcB=
MRead=LW+LH+LB
MWrite=SW+SH+SB
M2Reg=LW+LH+LB
RegDes=ALURI+LW+LUI (rt)
Wreg=ALURR+ALURI+Load
+JAL+LUI+shift
=~(Branch + J + JR + Store)
Taken=Beq*Zero + Bne*~Zero
SrcA=SLL + SRL = shift
…
ALUop
opcode7
Func7
Or
ALU-R-R
ALU-R-I
LW
SW
BEQ
BNE
J
JAL
JR
LUI
SHIFT
controller
Zero
ALURI+LW+SW+SHIFT
Func3

## Slide 59: Our Simple Control Structure
All of the logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce right answer? right away
  we use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
Instruction n
Instruction n+1
控制器
时钟下触发下一条指令
Datapath
Memory
We are ignoring some details like setup and hold times

## Slide 60: Designing the Main Control Unit First level
Main Control Unit function
  ALU op (2)
  Divided 6 control signals into 2 groups
    4 Mux
    3 R/W
control
Instruction opcode (7)
ALU op (2)
Mux (4)
R/W (3)
ALUScr
Branch
MemtoReg Jump
MemRead
MemWrite
RegWrite
ld | 00
sd | 00
Beq | 01
R-type | 10

## Slide 61: Truth Table for Main decoder
jump
Instruction | ALUSrc | MemtoReg | Reg Write | Mem Read | Mem Write | Branch | Jump | ALU Op1 | ALU Op2
R-format |  |  |  |  |  |  |  |  | 
Ld |  |  |  |  |  |  |  |  | 
Sd |  |  |  |  |  |  |  |  | 
beq |  |  |  |  |  |  |  |  | 
Jal |  |  |  |  |  |  |  |  | 

## Slide 62: Truth tables & Circuitry of main Controller
输入 |  | 输出 |  |  |  |  |  |  |  | 
Instruction | OPCode | ALUSrcB | Memto-Reg | Reg Write | Mem Read | Mem Write | Branch | Jump | ALUOp1 | ALU Op0
R-format | 0110011 | 0 | 00 | 1 | 0 | 0 | 0 | 0 | 1 | 0
Ld(I-Type) | 0000011 | 1 | 01 | 1 | 1 | 0 | 0 | 0 | 0 | 0
sd(S-Type) | 0100011 | 1 | X | 0 | 0 | 1 | 0 | 0 | 0 | 0
beq(SB-Type) | 1100111 | 0 | X | 0 | 0 | 0 | 1 | 0 | 0 | 1
Jal(UJ-Type) | 1101111 | X | 10 | 1 | 0 | 0 | 0 | 1 | X | X

## Slide 63: Main Controller Code
指令译码器参考描述
`define CPU_ctrl_signals {ALUSrc_B,MemtoReg,RegWR,MemWrite,Branch,Jump,ALUop}
always @* begin
case(OPcode)
5‘b01100: begin CPU_ctrl_signals = ?; end //ALU
5’b00000: begin CPU_ctrl_signals = ?; end //load
5’b01000: begin CPU_ctrl_signals = ?; end //store
5’b11000: begin CPU_ctrl_signals = ?; end //beq
5’b11011: begin CPU_ctrl_signals = ?; end //jump
5’b00100: begin CPU_ctrl_signals = ?; end //ALU(addi;;;;)
……
default: begin CPU_ctrl_signals = ?; end
endcase
end

## Slide 64: Design the ALU Decoder second level
ALU operation is decided by 2-bit ALUOp derived from opcode, and funct7 & funct3 fields of the instruction
  Combinational logic derives ALU control
opcode | ALUOp | Operation | Funct7 | funct3 | ALU function | ALU control
ld | 00 | load register | XXXXXXX | xxx | add | 0010
sd | 00 | store register | XXXXXXX | xxx | add | 0010
beq | 01 | branch on equal | XXXXXXX | xxx | subtract | 0110
R-type | 10 | add | 0000000 | 000 | add | 0010
 |  | subtract | 0100000 | 000 | subtract | 0110
 |  | AND | 0000000 | 111 | AND | 0000
 |  | OR | 0000000 | 110 | OR | 0001
 |  | SLT | 0000000 | 010 | Slt | 0111

## Slide 65: ALU Controller Code
ALU Control HDL Description
assign Fun = {Fun3,Fun7};
always @* begin
case(ALUop)
2’b10: ALU_Control = ? ; //add计算地址
2’b11: ALU_Control = ? ; //sub比较条件
2’b00:
case(Fun)
4'b0000: ALU_Control = 3'b010 ; //add
4’b0001: ALU_Control = ? ; //sub
4’b1110: ALU_Control = ? ; //and
4’b1100: ALU_Control = ? ; //or
4’b0100: ALU_Control = ? ; //slt
4’b1010: ALU_Control = ? ; //srl
4’b1000: ALU_Control = ? ; //xor
……
default: ALU_Control=3'bx;
endcase
2’b01:
case(Fun3)
………………………………………
endcase

## Slide 66: R-Type Instruction
jump
add x9, x20, x21
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 67: Load Instruction
jump
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Read memory and update register
ld x1, 200(x2)

## Slide 68: Save Instruction
jump
sd x1, 200(x2)
Read register operands
Calculate address using 12-bit offset
  Use ALU, but sign-extend offset
Write register value to memory

## Slide 69: BEQ Instruction
jump
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value and update PC
beq x1, x2，200
imm[12] | imm[10:5] | rs2 | rs1 | funct3 | imm[4:1] | imm[11] | opcode

## Slide 70: Jal Instruction
jump
jal x1, procedure
imm[20] | imm[10:1] | imm[11] | imm[19:12] | rd | opcode
Write PC+4 to rd
Calculate target address
  Sign-extend displacement
  Shift left 1 place (halfword displacement)
  Add to PC value and update PC

## Slide 71: Single Cycle Implementation performance for lw
Calculate cycle time assuming negligible delays except:
  memory (200ps), ALU and adders (200ps), register file access (100ps)
200ps
200ps
200ps
100+100=200ps
jump

## Slide 72: Performance in Single Cycle Implementation
Let’s see the following table:
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 73: Performance Issues
Longest delay determines clock period
  Critical path: load instruction
  Instruction memory  register file  ALU  data memory  register file
Wasteful of area. If the instruction needs to use some functional unit multiple times.
  E.g., the instruction ‘mult’needs to use the ALU repeatedly. So, the CPU will be very large.
Violates design principle
  Making the common case fast
We will improve performance by pipelining

## Slide 74: 4.6 Interruption & Exception
What’s Interruption & Exception ？
Why need interruption & exception？
How to deal with interruption & Exception in RISC V ?
  Transfer control to exception handler & return from exception
  Control status registers
  CSR instructions
  How to write an exception handler ?

## Slide 75: Interruption & Exception
The cause of changing CPU’s work flow :
  Control instructions in program (bne/beq, jal , etc)
  It is foreseeable in programming flow
  Something happen suddenly (Exception and Interruption)
  It is unpredictable
    Call Instructions triggered by hardware
Exception
  Arises within the CPU when execute
  instruction
  e.g., overflow, undefined opcode, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 76: Why we need interrupt ?
When you double click the mouse ……
When a network package arrives ……
When you want to print a sentence on screen ……
Event external to the running program can interrupt the processor : ex Interruption driven I/O
  polling ----waste a lot of processor time
  Interruption driven I/O
  DMA ---- direct memory access

## Slide 77: Why we need exception ?
Processor can be interrupted by exceptional events that occur while the program is running that are caused by the program itself.
Example:
  Page fault:
    need OS to load the page into the memory from disk, then resume the program
  Memory address fault ( segmentation fault )
  Undefined opcode
    The OS will stop the program and then transfer to other process.

## Slide 78: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
  64 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
Jump to handler
  Assume at 0000 0000 1C09 0000hex
  Entry address in a special register :Suptervisor Trap Vector (STVEC), which can be loaded by OS.

## Slide 79: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Exception vector address to be added to a vector table base register:
  Undefined opcode 00 0100 0000two
  Hardware malfunction: 01 1000 0000two
  …: …
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 80: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use SEPC to return to program (mret)
Otherwise
  Terminate program
  Report error using SEPC, SCAUSE, …
  OS make the choice to transfer to another ready process

## Slide 81: Exceptions in RISC V
  Transfer control to exception handler & return from exception
  Control status registers
  CSR instructions
  How to write an exception handler ?

## Slide 82: Privileged Architecture
Software stack

## Slide 83: Privileged level
Privilege Level in RISC V
  Provide protection between different components of the software stack

## Slide 84: CSR Address Mapping Convention
CSR[11..0] 4096
12 bit encoding space
11: read only
00/01/10: read/write
The lowest privileged level that can access CSR

## Slide 85: 8 important CSR for exception handling
8 CSR :
mtvec ( Machine Trap Vector): jump to this address when exception
mepc (Machine Exception PC): the instruction raise the exception
mcause (Machine exception Cause): which kind of exception(cause)
mie (Machine Interrupt Enable): which exception can be handled or negleted
mip (Machine interrupt pending): pending interruptions (read only register)
mtval (Mahine trap value): error address , illegal instruction, or 0
mscratch ( Machine Scratch):
mstatus ( Machine status) : processor status

## Slide 86: mtvec
Store the interruption handler entrance address
The base can be explained according to mode code
  00: PC base
  x1： vector mode， PC  mtval – 1 + 4x ( not required)
base[31..2] mode

## Slide 87: mepc
Save the instruction address when exception raised or interruption happens.
  the PC indicate the instruction that raise the exception
  the instruction need to be executed after back from interruption
    next instruction

## Slide 88: Exception Causes
Address misaligned
Access fault
illegal instruction
Breakpoint
Environment call
Synchronization exception
Asynchronization exception
Software interrupt
Timer interrupt
External interrupt

## Slide 89: Machine Status Register

## Slide 90: CSR instructions
csrrw rd, csr, zimm[4..0]: tCSRs[csr], CSRs[csr]x[rs1], x[rd]t
csrrs rd, csr, rs1: tCSRs[csr], CSRs[csr] t | x[rs1], x[rd]t
csrrc rd, csr, rs1: tCSRs[csr], CSRs[csr] t & ~x[rs1], x[rd]t
csrrwi rd, csr, zimm[4..0]: x[rd] CSRs[csr], CSRs[csr]zimm
cssrrsi rd,csr,zimm[4..0]: tCSRs[csr], CSRs[csr]t | zimm; x[rd]t
csrrci rd, csr, zimm[4..0]: tCSRs[csr], CSRs[csr]t&~zimm; x[rd]t
Mret:

## Slide 91: How Control Checks for Exceptions (Hardware)
Add test logic
  illegal instruction, load address misaligned, store address misaligned
add control signal
  CauseWrite for mcause
  EPCWrite for mepc
  TVALWrite for mtval
process of control
  mepc  PC( exception) or PC + 4 (interruption)
  mcause  set correspondent bit
  mtval  memory address or illegal instruction
  mstatus.mpie Mstatus.mie; mstatus.mie 0; mstatus.mppmp; mp11
  PC←address of process routine ( mtvec, ex. c0000000 )

## Slide 92: When jump to exception handler ？
Jump to handler
  Assume at 0000 0000 1C09 0000hex
jump when
mstatus.MIE = 1 && mie[i] = 1 && mip [i]= 1

## Slide 93: Ex. Exception handler

## Slide 94: Ex. Exception handler （cont.)

## Slide 95: How to back to the exception breakpoint ?
mret
  PC  CSRs[mepc]
  mstatus.MIE mstatus.MPIE
  mp mstatus.MPP

## Slide 96: END