## Slide 1: Chapter 1
Computer Abstractions
and Technology
只需要掌握8个伟大思想和CPU评价那些

## Slide 2: 1.1 Introduction

## Slide 3: Class of Computers
基本原理一致
Classes | PC/Desktop | Server服务器 | Embedded 嵌入式 | SuperComputers
Features | General purpose, variety of software Subject to cost/performance tradeoff | Network based High capacity, performance, reliability可靠 Range from small servers to building sized | Hidden as components of systems Stringent power/performance/cost constraints | High-end scientific and engineering calculations Highest capability but represent a small fraction of the overall computer market

## Slide 4: Computer Generations 经历了4代
First Generation – 1946 ~ 1956
  Vacuum tubes, programmable (电子管，可编程，图灵完全)
Second Generation – 1956 ~ 1964
  Transistor, programming languages (晶体管，高级编程语言开始应用)
Third Generation – 1964 ~ 1971
  Integrated Circuit, OS (集成电路，操作系统开始应用)
Fourth Generation – 1971 ~ now
  Microprocessor, GUI, Personal Computer (大规模集成微处理器, 图形用户界面, 个人电脑兴起)
Fifth Generation – future
  Still in development … …
ENIAC 埃尼艾克

## Slide 5: Von Neumann architecture (1945) 冯诺伊曼模型
“存储程序“的概念，采用控制流驱动， 计算与存储分离
按地址访问并且顺序执行行指令
数据与指令保存在同一个存储器，形式上没有区别。指令由操作码和地址码组成
输入设备I
输出设备O
运算器：核心是ALU
控制器：计数器PC（存放下一条指令的地址）,指令寄存器IR（存放当前指令），控制单元PU组成
运算器+控制器=CPU， CPU+主存储器=主机
存储器 存储字长是B（8bit）的整数倍
  地址寄存器MAR：存放欲访问的存储单元地址
  数据寄存器MDR：存放从存储单元取来的数据
5个部分

## Slide 6
RISC processors
  MIPS (Silicon Graphics)
  PA-RISC (Hewlett Packard)
  SPARC ( Sun Microsystems)
  Alpha ( Digital Equipment)
  PowerPC( Apple, Motorala, IBM)
  Motorala 88000
  I860, i960 (Intel)
CISC processors复杂指令集:
  80x86, Pentium, Penium Pro, Pentium II & III (Intel)

## Slide 7: 加速
Pipelining 流水线
On board cache 片上寄存器
On board L1 & L2 cache 多级片上寄存器
———————————————————————以下为体系结构
Out Of Order execution 乱序执行
Branch prediction 转移预测（分叉）
Data flow analysis 数据流分析（与编译相关）
Speculative execution 猜测
Multiple issue: Superscaler, VLIW 多发式（一个时钟周期有多条指令）

## Slide 8: What is a computer？
Computer is an electronic device that manipulates data according to a list of instructions (program), with capability of Turing machine.
  Electronic realization 电子化的实现方式
  A set of instructions in a well-defined manner 有指令集  general-purpose
  Execution of a pre-recorded list of instructions 可执行指令  program-controlled
  Memory that can store instructions and data 可存储指令与数据  stored program
  Turing-complete in theory 计算能力上是图灵完全  equivalent to Turing machine

## Slide 9: 1.2 Eight Great Ideas in Computer Architecture

## Slide 10
Design for Moore’s Law （设计紧跟摩尔定律）
Use Abstraction to Simplify Design (采用抽象分层简化设计)
Make the Common Case Fast (加速大概率事件) 优先优化常用功能
Performance via Parallelism (通过并行提高性能:多个流水线并行，行波加法器)
Performance via Pipelining (通过流水线提高性能)
Performance via Prediction (通过预测提高性能)
Hierarchy of Memories (存储器层次结构)
Dependability via Redundancy (通过冗余提高可靠性)
Express elevators in buildings
Library reserve desk
Increasing the gate area on a CMOS tran，sistor to decrease its switching time
类似福特的工业流水线

## Slide 11: Idea3: Make the Common Case Fast
Amdahl's Law

## Slide 12: Idea5: Performance via pipelining
Wash: 30minuts
Dryer: 40minuts
Fold: 20minuts
(30+40+20)x4 = 360
30+40*4+20=210
Notes: 四抱衣服总的时间: (30+40+20)x4 = 360

## Slide 13: Idea7 :Hierarchy of memories
Hierarchy of Memory
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Xfer Unit
prog./compiler
1-8 bytes
cache cntl
8-128 bytes
OS
512-4K bytes
user/operator
Mbytes
Upper Level
Lower Level
faster
Larger
Size / speed
1000B/300ps
64KB/1ns
256KB/3-10ns
2-4MB/10-20ns
4-16GB/50-100ns
4-16TB/5-10ms
存储大，速度慢 -> 层次化设计

## Slide 14: 1.3 Below Your Program

## Slide 15: Computer organization
Decomposability of computer systems
Computer System
Hardware
Software
Application software(应用软件): word, PPT, office
System software
OS(操作系统)
Compiler(编译器)：GCC
Firmware(Driver software):例如：网卡驱动
DBMS
硬件和软件具有功能等价性（既可以由硬件实现，又可以由软件实现），硬件具有更高的执行条件，软件具有更好的灵活性

## Slide 16: Levels of program code
High-level programming language(高级编程语言)
Assembly language(汇编语言)
  Symbolic notations ex. add A, B
  The assembler translates them into machine instruction
Machine language(机器语言)
  二进制，计算机唯一能认识的语言
Compiler
lw $15, 0($2)
add $16, $15, $14
add $17, $15, $13
lw $18, 0($12)
lw $19, 0($17)
add $20, $18, $19
sw $20, 0($16)
a[i] = b[i] + c;
Assembler
000000101100000
110100000100010
…

## Slide 17: A translation hierarchy
编译器：高级语言  汇编
汇编器：汇编  机器语言

## Slide 18: Program execution
Object
model
Byte
Code
Source
Code
Editor
Executable
File
Excute
Compile
Run
Interpreter
编
译
Link
interpreter
Static
Libary
Dynamic
Link Libary
C、C++
Pascal
Fortran
Basic
ASP
JS
Java
解释器：将源程序语句逐条翻译为机器语言并且立刻执行
中间
执行器

## Slide 19: 1.4 Under the covers computer hardware system

## Slide 20: Computer organization
Computer System
CPU
Memory
I/O interface
Control unit
Datapath
Path: multiplexors
ALU: adder, multiplier
Registers
……
Hardware
Software
Input: keyboard
Bidirectional: RS-232,USB
Output: VGA，LCD
其中有控制器

## Slide 21: Memory: A safe place for data
Memory(存储): the storage area programs are kept and that contains the data needed by the running programs
Main Memory(主存): volatile; used to hold programs while they are running.( DRAM in computers)
Second memory: nonvolatile; used to store programs and data between runs. (Flash in PMD, magnetic disks)
Volatile (易失性)
  DRAM (Dynamic Random-Access Memory):动态随机存储器
  SRAM (Static Random Access Memory)：静态随机存储器
Nonvolatile (非易失性)
  Solid state memory (Flash Memory):固态硬盘 or 闪存
  Magnetic disk (Hard disk) ：硬盘
Memory |  | Price | Speed | Capacity | Used for
SRAM | volatile | / | Fastest | KB~MB | Cache
DRAM | volatile | $3~4/GB | Fast | MB~GB | Main memory
Hard disk | nonvolatile | $0.05~1/GB | Slow | TB~PB | PC Storage
Flash Memory | nonvolatile | $0.75~$1/GB | Medium | GB~TB | PMD Storage

## Slide 22: 1.6 Performance

## Slide 23: Defining Performance
Response (Execution) time 执行时间
  user perception
  system performance
  the only unimpeachable measure of performance 唯一无懈可击的业绩衡量标准
  Mobile devices
CPU time
  designer perception
  CPU performance
Throughput
  administrator perception
  server
改进性能的方法 | Response time | Throughput
Replacing a faster processor | ↑ | ↑
Adding additional processors for a system use MP for independent task | - | ↑

## Slide 24
Response (Execution) time
  计算机完成一项任务所需的总时间，包括磁盘访问、内存访问、I/O活动、操作系统开销、CPU执行时间
CPU time
  CPU用于特定任务的实际计算时间
Throughput(Bandwidth带宽)
  在给定时间内所做的总功
  单位时间内完成的任务数
CPU time is further divided into:
  User time - time spent in user mode
  System time - time spent in OS

## Slide 25: Relative Performance
“Performance of P1 is better than P2 ” is, for a given work load L, P1 takes less time to execute L than P2 does
performance(P1) > Performance(P2)
 Execution Time(P1, L) < Execution Time(P2, L)
“Processor X is n times fast than Y” is

## Slide 26: CPU Clocking
时钟周期 Clock Circle Time
主频的倒数
主频（时钟频率）Clock Rate
  主频越高完成一个指令所需要的时间越短
  CPI cycle per instruction
  执行一条指令所需的时钟周期数（时钟频率不影响CPI）
  CPU执行时间
Instructions指令条数

## Slide 27: CPI是执行所有指令的平均时间周期数

## Slide 28: CPI Example
Alternative compiled code sequences using instructions in classes A, B, C
Class | A | B | C
CPI for class | 1 | 2 | 3
IC in sequence 1 | 2 | 1 | 2
IC in sequence 2 | 4 | 1 | 1
Sequence 1: IC = 5
  Clock Cycles = 2×1 + 1×2 + 2×3 = 10
  Avg. CPI = 10/5 = 2.0
Sequence 2: IC = 6
  Clock Cycles = 4×1 + 1×2 + 1×3 = 9
  Avg. CPI = 9/6 = 1.5

## Slide 29: Example：Which is fast and by how much ?
 | clock period | CPI | CPU clock cycles | CPU time
A | 250 ps | 2.0 | I 2.0 | 500 I ps
B | 500 ps | 1.2 | I 1.2 | 600 I ps
 | clock period | CPI | CPU clock cycles | CPU time
A | 250 ps | 2.0 |  | 
B | 500 ps | 1.2 |  | 
Answer: CPU PerformanceA Execution TimeB 600 * I ps
--------------------------- = -------------------------- = ------------------- = 1.2
CPU PerformanceB Execution TimeA 500 * I ps

## Slide 30
Architecture --> Implementation --> Realization
Compiler Designer Processor Designer Chip Designer
Hardware / Software | Affects what ? | How?
Algorithm | IC, possibly CPI | Favoring instructions
Programming language | IC, CPI | Java : indirect calls
Compuiler | IC, CPI | 
Instruction set Architecture | IC, CPI, CC | 
Organization | CPI, CC | 
IC | CC | 

## Slide 31: Challenges of the processor
处理器和存储器性能的提高不成比例，“内存墙”问题日趋严重，“冯诺依曼”架构面领挑战。
单位面积功耗增大，散热问题日趋严峻，“功耗墙”问题凸显。
受物理规律限制，摩尔定律面临失效，靠工艺进步获得的性能红利逐渐减弱。
Memory Wall（内存墙）
工艺发展限制
Power Wall(功耗墙)