## Slide 1
Chapt3_1
Arithmetic for computer

## Slide 2: Contents
1 Signed and Unsigned Numbers-Possible Representations
2 Arithmetic--Addition & subtraction and ALU
3 Multiplication
4 Division (chap3_2)
5 Floating point numbers (chap3_2)

## Slide 3: Numbers and their representation
r进制数
MSD
LSD
原码、反码在数轴上对称，两者都存在+0和-0两个0
补码、移码在数周上不对称，0唯一，比原码、反码多一个数

## Slide 4
B转O,H
左右补0凑位
D转任意
整数除基取余，小数乘基取整
之后验证一下是不是对的
注意小数是离散的，所以不是每个十进制小数都可以有准确地用二进制表示

## Slide 5: Numbers and their representation
Representation
  ASCII - text characters
    简单的数字读写
    复杂算术(按字符计算)
  Binary number
    Natural form for computers
    Requires formatting routines for I/O
* ASCII--American Standard Code for Information Interchange
8bit

## Slide 6
真值转换为补码：对于正数，与原码的方式一样。对于负数，符号位取1，其余各位由真值“各位取反，末位加1”得到
补码转换为真值：若符号位为0，与原码的方式一样。若符号位为1，真值的符号为负，数值部分各位由补码“各位取反，末位加1”得到

## Slide 7: 补码
fraction
integer
如果字长为n+1
比原码多-1
比原码多

## Slide 8
补码的优势
  0唯一
  运算简单，符号位可以和数值位一起运算（加减法可以一起运算）
  可以多表示1个数

## Slide 9: Two‘s Biased notation 移码表示法
Negating Biased notation number:
2's Biased notation VS 2's complement
  X=＋1011 [X]c=01011 [X]b=11011
X=－1011 [X]c=10101 [X]b=00101
真值x的基础上加一个常数（置偏值），通常为
机器字长为n+1
补码和移码只差一个符号位
全是正的
移码方便浮点数科学计数法

## Slide 10: Compare operations
Different compare operations required for both number types
  Signed integer
    slt Set when less than 寄存器与寄存器，前小于后1
    slti Set when less than immediate寄存器与立即数，前小于后1
  Unsigned integer
    sltu Set when less than
    sltiu Set when less than immediate

## Slide 11: Example for Compare
Register s0
1111 1111 1111 1111 1111 1111 1111 1111
Register s1
0000 0000 0000 0000 0000 0000 0000 0001
Compared Operations
slt t0, s0, s1
sltu t0, s0, s1
Results
t0 = 1 (-1 < 1)
t0 = 0 (4,294,967,295ten > 1ten)
符号数
无符号数

## Slide 12: 3 Arithmetic

## Slide 13: Addition & subtraction
Adding bit by bit, carries -> next digit
Subtraction
  Directly
  Addition of 2's complement

## Slide 14: Overflow conditions
General overflow conditions
Operation | Operand A | Operand B | Result overflow
A+B | ≧0 | ≧0 | <0 (01)
A+B | <0 | <0 | ≧0 (10)
A-B | ≧0 | <0 | <0 (01)
A-B | <0 | ≧0 | ≧0 (10)
最高位和进位异或为1，则溢出

## Slide 15: Overflow process
Hardware detection in the ALU
Generation of an exception (interrupt)
Save the instruction address (not PC) in special register EPC
Jump to specific routine in OS 异常处理
  Correct & return to program
  Return to program with error code回到出错的指令那里
  Abort program

## Slide 16: Which instructions cause Overflow
Overflows in signed arithmetic instructions cause exceptions:
  add
  add immediate (addi)
  subtract (sub)
Overflows in unsigned arithmetic instructions don’t cause exceptions
  add unsigned (addu)
  add immediate unsigned (addiu)
  Subtract unsigned (subu)
Handle with care!

## Slide 17: Unsigned Binary Integers
Range: 0 to +2n – 1
Given an n-bit number
Notes: 最低有效位（least significant bit）: 最右边
最高有效位（most significant bit）：最左边

## Slide 18: 2’s-Complement Signed Integers
Range: –2n – 1 to +2n – 1 – 1
Given an n-bit number
–(–2n – 1) can’t be represented
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111
都是正数比负数少一位
Notes: 取反+1

## Slide 19: RISC V instructions
Byte instructions
  lbu: load byte unsigned 取无符号数字节
    Loads a byte into the lowest 8 bit of a register
    Fills the remaining bits with ‘0’ （一般32位计算机，8位需要补成32位）
  Lb: load byte (signed)
    Loads a byte into the lowest 8 bit of a register
    Extends the highest bit最高位 into the remaining 24 bits
Set instructions for conditional branches
  sltu: set on less than unsigned
  slti: set on less than immediate
  sltiu: set on less than unsigned immediate

## Slide 20
Logical shift operations逻辑移位
  right (srl)
  left (sll)
Filled with '0'
左移结果出错，右移精度下降
Arithmetic shift operations算术移位
 | 码制 | 添加码
正数 | 原码、补码、反码 | 0
负数 | 原码 | 0
 | 补码 | 左移添0，右移添1
 | 反码 | 1

## Slide 21: Logical operations
AND→bit-wise AND between registers
and register1, register2, register3
OR →bit-wise OR between registers
or register1, register2, register3
Example:
and $3, $10, $16
or $4, $10, $16
  R16: 0000 0000 0000 0000 1100 1000 0000 1111
  R10: 0000 0000 0000 0110 0100 0000 0111 1000
  R3: 0000 0000 0000 0000 0100 0000 0000 1000
  R4: 0000 0000 0000 0110 1100 1000 0111 1111

## Slide 22: 一位全加器
Full adder in 2-level design
+

## Slide 23: Basic 32 bit ALU
Inputs parallel
Carry is cascaded
Ripple carry adder
行波进位加法器
Slow, but simple
1st Carry In = 0

## Slide 24: Extended 1 bit ALU
Subtraction
a - b
  a-b = a + (~b+1)
  =a + (-b)
  Inverting b
  1st CarryIn= 1

## Slide 25: Extended 1 bit ALU to RISC V ALU
Functions
  AND、OR、
  Add、SUB
  SLT、
Missing: comparison
  Slt rd, rs1, rs2
  If rs1 < rs2, rd=1, else rd=0
  All bits = 0 except the least significant
  Subtraction (rs1 – rs2), if the result is negative -> rs1 < rs2
  Use of sign bit as indicator

## Slide 26: Most significant bit 检测溢出
Operation | Operand A | Operand B | Result overflow
A+B | ≧0 | ≧0 | <0 (01)
A+B | <0 | <0 | ≧0 (10)
A-B | ≧0 | <0 | <0 (01)
A-B | <0 | ≧0 | ≧0 (10)
Most
significant bit
least
significant bit

## Slide 27: Complete ALU
Input
  A
  B
Control lines
  Operation
  Binvert
  Carryin
Output
  Result
  Overflow

## Slide 28: Complete ALU
Add a Zero detector
输出比较结果

## Slide 29: ALU 算术逻辑单元
ALU Control Lines | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Set on less than
n位选择器，有 种操作

## Slide 30: Speed considerations
Previously used: ripple carry adder行波
Delay for the sum: two units
Delay for the carry: two - three units
Ai
Bi
Ci
Ci+1
Gi
Pi
Si

## Slide 31: 串行加法器
Delay of one adder
  2 time units
Total delay for
stages:
2n unit delays

## Slide 32: 并行进位加法器 (CLA)
And,we can further get:
C1=G0+P0*c0 ;
C2= G1+P1*C1 = G1+P1*G0+ P1* P0*c0
C3=G2+P2*C2 = G2+P2*G1 + P2* P1*G0+ P2* P1* P0*c0
C4=G3+P3*C3= G3+P3*G2+P3*P2*G1+P3*P2*P1*G0+P3*P2*P1*P0*c0
Ai
Bi
Ci
Ci+1
Gi
Pi
Si
i
i
i
i
i
i
B
A
G
B
A
P
=
Å
=
i
i
i
1
i
i
i
i
C
P
G
C
C
P
S
+
=
Å
=
+
Notes:   gi = ai * bi
  pi = ai + bi

## Slide 33
partial full adder

## Slide 34
CLA
CLA
CLA
CLA
CLA
内部并行，组间串行

## Slide 35: Carry-Skip Adders
With CMOS Implementation – Carry Skip Adder’s speed Comparable to CLA
Less Area/Power
Based on Observation that Carry Process Can “Skip” Stage for Which xi  yi (that is pi = xiyi = 1)
Adder of n stages Divided into Stages of Selected Lengths
With Simple Ripple Carry
Each Group Generates “Group Carry-Propagate”=1 if all pi=1 This Signal Allows Incoming Carry to “Skip” Stages within Group and Generate Carry-out

## Slide 36: What does it mean if ALL Pi = 1 ?
c1 = g0 + (p0 * c0)
c2 = g1 + p1*c1 = g1 + (p1 * g0) + (p1 * p0 * c0)
c3 = g2 + p2*c2 = g2 + (p2 * g1) + (p2 * p1 * g0) + (p2 * p1 * p0 * c0)
c4 = g3 + p3*c3 = g3 + (p3 * g2) + (p3 * p2 * g1)
+(p3 * p2 * p1 * g0) + (p3 * p2 * p1 * p0 * c0)
gi = ai * bi pi= ai + bi
If Pi = 1 then it can be know that Gi = 0
So, c4 = g3 + p3*c3 = g3 + (p3 * g2) + (p3 * p2 * g1)
+(p3 * p2 * p1 * g0) + (p3 * p2 * p1 * p0 * c0)
= c0

## Slide 37: Carry skip adder
Accelerating the carry by skipping the interior blocks
Optimal speed with no-equal distribution of block length

## Slide 38: Fixed Block Width Carry-Skip Adders

## Slide 39: Carry Select Adder (CSA)
多路选择器

## Slide 40: 3 Multiplication

## Slide 41: Multiplier V1
因为是两个 4 位数相乘 所以结果应该是四个数加和得到的 。 先判断 y 的最低位是 0 还是 1 如果是 1 则需要把 x 加到部分积上 若为 0 则需要把0 加到部分积上 实际上加 0 的这个过程计算机并不执行 因为加 0 对部分积没有任何影响 x 左移一位 之后再让 y 右移一位 若 y 为 0 则循环结束 否则继续此循环过程

## Slide 42: Multiplier V 2

## Slide 43: Multiplier V 3
Further optimization
At the initial state the product register contains only '0'
The lower 32 bits are simply shifted out
Idea:
use these lower 32 bits for the multiplier

## Slide 44: Multiplier V 3

## Slide 45: Signed multiplication符号数乘法
① 被乘数和乘数均取绝对值参与运算，看作无符号数，符号位为
②从乘数的最低位 开始判断，若 ，则部分积加上被乘数 ，然后右移一位；
  若 则部分积加上0，右移一位
原码一位乘法

## Slide 46: 另一个例子

## Slide 47: Booth's Algorithm
① 所有位都参与运算，结果也是补码
② 被乘数和部分积都取双符号位，初值为0，乘数取单符号位，并且末尾增设初值
③ 根据 来确定操作
④ 移位按照补码移位的规则
⑤ n+1次操作，n次右移
补码一位乘法
yn（高位） | yn+1（低位） | 部分积操作
0 | 0 | 右移1位
1 | 1 | 
0 | 1 | 加[x]补，右移1位
1 | 0 | 加[-x]补，右移1位

## Slide 49
Assumes： Z=y×10111100
Z=y(10000000+111100+100-100)
=y(1×27+1000000-100)
=y(1×27+1×26-22)
=y(1×27+1×26+0×25+0×24+0×23+0×22+0×21+0×20 -1×22 )
= y(1×27+1×26+0×25+0×24+0×23+0×22-1×22 +0×21+0×20)
= y×27+y×1×26+0×25+0×24+0×23 +0×22-y×22 +0×21+0×20)
Only shift
Only shift
add
sub
1 01 111 10 00
1比较多的时候好、0多的时候反而复杂了

## Slide 50: Booth's Algorithm
Idea: If you have a sequence of '1's
  subtract at first '1' in multiplier
  shift for the sequence of '1's
  add where prior step had last '1‘
Result:
  Possibly less additions and more shifts
  Faster, if shifts are faster than additions
找一串1

## Slide 51: Booth's Algorithm
Example
Logic required identifying the run

## Slide 52: Example with negative numbers
2 * (-3) = - 6
0010 * 1101 = 1111 1010
iteration | step | Multiplicand | product
0 | Initial Values | 0010 | 0000 1101 0
1 | 1.c:10→Prod=Prod-Mcand | 0010 | 1110 1101 0
 | 2: shift right Product | 0010 | 1111 0110 1
2 | 1.b:01→Prod=Prod+Mcand | 0010 | 0001 0110 1
 | 2: shift right Product | 0010 | 0000 1011 0
3 | 1.c:10→Prod=Prod-Mcand | 0010 | 1110 1011 0
 | 2: shift right Product | 0010 | 1111 0101 1
4 | 1.d: 11 → no operation | 0010 | 1111 0101 1
 | 2: shift right Product | 0010 | 1111 1010 1

## Slide 53: Faster Multiplication
分层设计