## Slide 1
Chapter 4-1
Processor Design
Notes: 重点

## Slide 2
PC
clk
Add
4
addr
Instr
ROM
Write data
rd
rs1
rs2
data1
data2
Reg
clk
[31:0}
[11:7}
[19:15}
[24:20}
[31:7}
Imm
Gen
RegWrite
Imm
Add
ALUsrcB
ALU
0
Res
Address
W data
Read
Mem
MemRW
MemtoReg
Branch
BranchN
Jump
SCPU_crtl
ALUop
Auipc
Slice
Slice
我画的实现了全部指令的数据通路
Notes: Load和store才会碰memory
RISCV 所有的写地址都是rd

## Slide 3
1 Introduction

## Slide 4
  取指IF：Fetch the instruction from the memory
  译码阶段ID： Decode and read the registers 同时进行
  执行阶段EX：Use ALU to calculate
    Arithmetic result
    Memory address for load/store内存地址
    Branch comparison
  访问和阶段MEM：Access data memory for load/store
  写回阶段WB:PC  target address or PC + 4（PC加4移动到吓一跳指令）
CPU performance factors
  Instruction count
    由编译器决定
  CPI and Cycle time
    由CPU决定

## Slide 5
2 Logic Design Conventions

## Slide 6: Memory
  Instruction memory : ROM, input address, get instruction
  Data memory: RAM.
    Can read or write controlled by signal MemRead and MemWrite.
    Read: input address, get instruction if MemRead=1
    Write: input address & datain, write into memory if MemWrite =1
Instruction
Instruction
Address
Instruction
memory
MemWrite
Read
data
Address
Data
memory
Write
data
MemRead

## Slide 7: Register File
  Output from the register
5 bits
5 bits
5 bits
64 bits
64 bits
64 bits
Reg. address
Reg. address
Data output

## Slide 8: The other elements
Immediate generation unit：
  输入指令产生立即数的逻辑功能
    根据指令类型（加载，存储或者分支指令），产生相应的立即数
  转移指令偏移量左移位的功能
    立即数字段符号扩展为64位结果输出
Immediate generation
  Load:
  0000011
  Save:
  0100011
  Branch:
  1100011
  Jal:
  1101111
S_imm = {{52{inst[31]}}, Inst[31:25], inst[11:7]};
SB_imm = {{51{inst [31]}}, inst[31], inst [7], inst[30:25], inst[11:8],1'b0};
UJ = {{43{inst[31]}}, inst [31], inst[19:12], inst[20], inst[30:21],1'b0};
L_imm = {{52{inst[31]}}, Inst[31:20]};
书上说，高两位不一样就不一样。但是我们要求多实现一个jal，所以前两位还不能判断

## Slide 9
3 Building a datapath

## Slide 10: RISC-V fields (format)
opcode：basic operation of the instruction.
rs1： the first register source operand.
rs2： the second register source operand.
rd： the register destination operand.
funct： 函数，该字段选择op字段中操作的具体变体
Immediate: address or immediate

## Slide 11
Func7 只有一位有用

## Slide 13: RISC-V assembly language
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add x5,x6,x7 | x5=x6 + x7 | Add two source register operands
 | subtract | sub x5,x6,x7 | x5=x6 - x7 | First source register subtracts second one
 | add immediate | addi x5,x6,20 | x5=x6+20 | Used to add constants
Data transfer | load doubleword | ld x5, 40(x6) | x5=Memory[x6+40] | doubleword from memory to register
 | store doubleword | sd x5, 40(x6) | Memory[x6+40]=x5 | doubleword from register to memory
Logical | and | and x5, x6, 3 | x5=x6 & 3 | Arithmetic shift right by register
 | inclusive or | or x5,x6,x7 | x5=x6 ¦ x7 | Bit-by-bit OR
Conditional Branch | branch if equal | beq x5, x6, 100 | if(x5 == x6) go to PC+100 | PC-relative branch if registers equal
 | branch if not equal | bne x5, x6, 100 | if(x5 != x6) go to PC+100 | PC-relative branch if registers not equal
Unconditional Branch | jump and link | jal x1, 100 | x1 = PC + 4; go to PC+100 | PC-relative procedure call
 | jump and link register | jalr x1, 100(x5) | x1 = PC + 4; go to x5+100 | procedure return; indirect call

## Slide 14: Signals for datapath Defined 7 control signals
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScr | The second ALU operand come from the second register file output (Read data 2) | The second ALU operand is the sign-extended lower 16 bits of the instruction..
Branch （PCSrc） | The PC is replaced by the output of the adder that computers the value PC+4 | The PC is replaced by the output of the adder that computers the branch target.
Jump | The PC is replaced by PC+4 or branch target | The PC is updated by jump address computed by adder
MemRead | None | Data memory contents designated by the address input are put on the Read data output.
MemWrite | None | Data memory contents designated by the address input are replaced by value on the Write data input.
MemtoReg (2位) | 00：The value fed to register Write data input comes from the Alu | 01：The value fed to the register Write data input comes from the data memory.
 |  | 10：The value fed to the register Write data input comes from PC+4

## Slide 15
PC
clk
Add
4
Read address
Instr
Instruction Memory
Write dara
Write register
Read rigister1
Read rigister2
Read data1
Read data2
Reg
File
clk
Inst[31:0}
Inst[11:7}
Inst[19:15}
Inst[24:20}
Inst[31:7}
Imm
Gen
RegWrite
ImmSel
Add
ALUsrcB
ALU
0
Res
Address
Write data
Read data
Data
Mem
MemRW
MemtoReg
Branch
BranchN
Jump
SCPU_crtl
ALUop
Auipc
Slice
Slice
我画的实现了全部指令的数据通路
Notes: Load和store才会碰memory
RISCV 所有的写地址都是rd

## Slide 16: 马德实验ppt的扩展指令后的数据通路

## Slide 17: 马德实验ppt的控制信号

## Slide 18: Performance in Single Cycle Implementation
Let’s see the following table:
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
ld | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sd | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 19: R型指令

## Slide 20: B型指令
Beq：当branch等于1，并且ALU的运算结果是0的时候才跳
Imm Gen 模块，将指令中的立即数符号扩展到 64 位；然后在 (3) 处左移 1 位，所以我们没有保存偏移的最低一位；
但是，我们是选择了直接生成，而非移动。而且是32位。再与 PC 相加

## Slide 21: Performance Issues
单周期的实现是指，一个指令的所有工作都在一个时钟周期内完成，也就是 CPI = 1。那么，一个时钟周期的长度就要足够最长的那个指令完成运行。但是，例如 load 类的指令要经过 inst mem, reg file, ALU, data mem, reg file 这么多的步骤，这会使得时钟周期变得很长，导致整体性能变得很差。单周期的实现违反了 common case fast 这一设计原则
因此我们需要引入流水线

## Slide 22: 4 Interruption & Exception

## Slide 23
Exception 异常
  Arises within the CPU when execute
  instruction
  e.g., overflow, undefined opcode, syscall, …
Interrupt 中断
  From an external I/O controller

## Slide 24: 中断异常处理
保存地址
mechain Exception Program Counter (mepc机器模式的epc，管理员模式对应sepc)， 中断保存当前pc，异常保存pc+4
保存中断原因
mechain Exception Cause Register (mcause)
处理
跳转到 stvec
恢复
mret指令回到mepc

## Slide 25: Privileged Architecture
Software stack
ABI为接口
直接到底层
通过OS访问
更安全的嵌入式系统
虚拟机

## Slide 26: Privileged level
H
Hypervisor
4个mode
Notes: 广义CPU包括内存管理MMU，浮点数管理etc

## Slide 27: CSR 特权寄存器
CSR[11..0] 4096个
12 bit encoding space
11: read only
00/01/10: read/write
The lowest privileged level that can access CSR
CSR只能读写
RISC-V中的32个寄存器都是user mode； 处理异常的寄存器是这32个之外的更高级的寄存器
Notes: S

## Slide 28: 8 important CSR for exception handling
细分中断
Mtvec中的程赋给PC，进入异常模式
引起异常或者该指令的下一条，用于处理完后返回
先处理级别高的异常，等级低的先等待

## Slide 29: How Control Checks for Exceptions (Hardware)测试中断的逻辑
Add test logic测试异常的逻辑（所有的情况或一下）
  illegal instruction, load address misaligned, store address misaligned ，overflow…
add control signal 控制信号
  CauseWrite for mcause
  EPCWrite for mepc
  TVALWrite for mtval
process of control 数据通路要求修改的地方
  mepc  PC( exception) or PC + 4 (interruption)
  mcause  set correspondent bit
  mtval  memory address or illegal instruction
  mstatus.mpie Mstatus.mie; mstatus.mie 0; mstatus.mppmp; mp11
  PC←address of process routine ( mtvec, ex. c0000000 )
Notes: 把这些异常都或起来

## Slide 30
jump when
mstatus.MIE = 1 && mie[i] = 1 && mip [i]= 1
mret
  PC  CSRs[mepc]
  mstatus.MIE mstatus.MPIE
  mp mstatus.MPP